## Slide 1: VHTz Sounding: MinToaReady
Date: 2018-02-20
Authors:

## Slide 2: VHTz Sounding Protocol
Protocol is completely unscheduled
  When medium is idle, initiator can send NDP-A followed by NDP
  If available, responder replies with NDP within SIFS
  Followed by LMR within SIFS, which contains
    Time stamps t2/t3 of this exchange, or
    Time stamps t2/t3 of a previous exchange, or
    No time stamps, if none are ready
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder

## Slide 3: Processing Time
Initiator needs feedback from responder
  T2 time-of-arrival (ToA) of NDP send by initiator
  T3 time-of-departure (ToD) of NDP send by responder
  The time available to determine t2 is about 70-80 µs
    2·SIFS = 32 µs
    VHT NDP = 40-52 µs (1-4 LTF)
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder
Processing Time
t2
t3

## Slide 4: Processing Time (cont.)
To determine an accurate ToA requires FFT processing
Implementations can be in
  Hardware (delay on order of 10s of µs)
  Firmware/software (delay on order of ms)
Processing delay can depend on
  Bandwidth
  Number or receive antennas
  Number of LTF received
  Current load of other processing (firmware/software)

## Slide 5: Immediate and Delayed Feedback
Sounding
Sequence 1
Time [ms]
Sounding
Sequence 2
LMR 1
LMR 2
Immediate Feedback
Sounding
Sequence 1
Time [ms]
Sounding
Sequence 2
Empty LMR
LMR 1
Delayed Feedback
Min Processing Time

## Slide 6: Delayed Feedback
FTM Setup/Negotiation
  Responders declares MinToaReady
    Tells the initiator when to expect measurement results availability
    After this interval the initiator can expect the time stamps t2/t3 to be included in next LMR
  Responder also declares MaxToaAvailable
    Tells the initiator for how long will the measurement results t2/t3 of previous sounding sequence instance will be stored
    If no subsequent sounding sequence is exchanged for a duration of MaxToaAvailable past the measurement responder may discarded t2/t3
Sounding
Time [ms]
LMR Availability
MinToaReady
MaxToaAvailable

## Slide 7: MinToaReady and MaxToaAvailable
MinToaReady Definition
  Represented as one octet in increments of 100 µs
  Range is 0 to 25.5 ms
MaxToaAvailable Definition
  Represented as a 4 bit exponent MaxToaAvailableExp
  Value is calculated as
  MaxToaAvailable = 2^(MaxToaAvailableExp+8) ms
  Range is 256 ms to 140 minutes

## Slide 8: MinToaReady
Set by Responder
  Processing can start after receiving the NDP (t3)
  Needs to have results ready before preparing LMR in next sequence
Used by Initiator to Set Timer
  Knows sounding was successful after receiving NDP in reply (t4)
  Can only initiate next sounding after timer expires
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder
t1/t2
t3/t4

## Slide 9: MaxToaAvailable
Set and Used by Responder to Set Timer
  Depends on storage capabilities
  Needs to receive and decode next NDP-A before timer expires (t2)
Also Used by Initiator to Set Timer
  Potentially use same timer as MinToaReady
  Needs to transmit next NDP-A so that responder can receive and decode before timer expires
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder
t1/t2
t3/t4

## Slide 10: Definition of Start and End Points
MinToaReady and MaxToaAvailable are measured
  Starting at t4/t3 and ending at t1/t2 for the initiator and responder respectively
  Meets previous criteria
  Initiator can use same time start/end points for both timers
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder
t1/t2
t3/t4
MaxToaAvailable/ MinToaReady
Start
End

## Slide 11: Motion
We agree to measure MinToaReady and MaxToaAvailable starting from t4/t3 in the preceding sounding sequence to t1/t2 when receiving the new sounding sequence, see slide 10.
Y: / N: / A: