## Slide 1: Address field in WUR frame
Date: 2018-03-04
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
In baseline spec[1], there are two types of the group addressed frames
  One is broadcast addressed frame and the other is multicast-group addressed frame
At the last meeting [2] , there was a discussion on method for indicating the group addressed frame but it had not been decided
  A wake-up frame that has the Address field set to a value of TBD indicates that the AP intends to transmit group addressed frames
  This is similar to group addressed frame indication in DTIM frame of the baseline spec regardless of frame type (broadcast or multicast-group)
The baseline spec[1] also defined several multicast methods (e.g., DMS, FMS, GCR, ….) for efficient multicast transmission but they are not used often
  That is, DTIM based group addressed indication is the basic approach in the baseline spec

## Slide 3: Address field for group addressed frame (1/2)
As a basic method for indicating the group addressed frame TX, we propose to set Address field of WUR Wake Up frame to a special value
  The Address field of WUR Wake Up frame is set to a special value (e.g., 4095) for indicating the group addressed frame presence on PCR
Upon receiving a Wake Up frame with Address field set to a special value, WUR STA can attempt to receive the group addressed frame

## Slide 4: Address field for group addressed frame (2/2)
According to the SFD[3], AP may assign one or more Group ID(s) to WUR STA through PCR WUR negotiation
  One of Group ID usages is that the assigned Group ID can correspond to a multicast-group frame (e.g., FMS, GCR-SP)
  How the Group ID is mapped to a specific multicast-group is out of scope (i.e., AP’s implementation)
Once AP assigns a Group ID corresponding to a multicast group, when the AP wants to send the multicast frame, the AP will use in Wake Up frame the corresponding Group ID instead of Address field set to the special value

## Slide 5: Reference
[1] P802.11REVmd_D1.0
[2] 18/103r3, Further considerations on WUR frame format
[3] 17/575r9, TGba Spec framework

## Slide 6: Straw Poll 1
Do you agree the following?
  The Address field of WUR Wake Up frame is set to a value of TBD for indicating that the AP intends to transmit group addressed frames
    Whether the TBD vale is fixed or randomized is TBD