## Slide 1: Length/Misc. field in WUR frame
Date: 2018-03-04
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
In SFD [1]
At the last meeting there were some discussions on Length/Misc field in WUR frame but no decision on the details (e.g., indication, the field size, etc.) [2]
  Option 1 (using 1 bit indicator) was more preferable than option 2

## Slide 3: Length/Misc field in WUR frame
Proposal
  If the Frame Body presence is set to 1, the Length/Misc subfield indicates the length of the Frame Body. Otherwise, the Length/Misc subfield indicates the Misc.
  When the Frame Body presence of the WUR Wake Up frame is 1, 3 bits Misc. is present at the beginning of the Frame Body
    Note that WUR Beacon frame always has no Frame Body and WUR Vendor Specific frame always has Frame Body
Type
Length/Misc
Reserved
Frame Body presence
3
3
1
1
Frame Control (FC) field

## Slide 4: Reference
[1] 17/575r9, TGba Spec framework
[2] 18/104r1, Clarification for Variable-length WUR frame

## Slide 5: Straw Poll 1
Do you agree the following?
  If the Frame Body presence subfield of FC field in MAC header is 1, the 3 bits Length/Misc subfield indicates the length of the Frame Body. Otherwise, it indicates the Misc.
Y: 10, N: 3, A:
Type
Length/Misc
Reserved
Frame Body presence
3
3
1
1
Frame Control (FC) field
Bits:

## Slide 6: Motion 1
Move to modify the following figure in TGba SFD as follows and add the following text to the TGba SFD
  If the Frame Body presence subfield is 1, the Length/Misc subfield indicates the length of the Frame Body. Otherwise, it indicates the Misc.
Move:
Second:
Type
Length/Misc
Reserved
Frame Body presence
3-4
3-4
1 rest
1
Bits: