## Slide 1: Length field in WUR frame
Date: 2018-03-04
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
Length field in SFD [1]
  When the Frame Body field is present in a WUR frame then:
    The length of the Frame Body field is indicated by the Length subfield in the Frame Control field
    The length is in units of TBD octets, and is up to 8 or 16 (TBD) octets.
At the last meeting, proposal on Length field in WUR frame [2]
  The unit of the Length field: 2 octets, the maximum length of frame body is 16 octets
  At 62.5kbps, the airtime of the max WUR frame is ~ 3 ms
  At 250kbps, the airtime of the max WUR frame is ~ 0.8 ms
During the discussion, someone raised the concern on the maximum air time of the frame which is larger than 2ms at the low data rate
[3] tried to limit/reduce the length of WUR frame at the low rate PHY (e.g., at least ~2ms)
Generally the error probability of the longer frame is higher than that of shorter frame in the same data rate

## Slide 3: Proposal
Option 1: Different unit(/maximum frame body length) according to data rate
  At 250kbps, unit – 2 octets, the maximum length of the frame body - 16 bytes  ~0.8ms airtime
  At 62.5kbps, unit – 1 octet, the maximum length of the frame body – 8 bytes  ~1.9ms airtime
  WUR STA can know date rate by WUR Sync field and decide the unit of the Length field if it’s included
Option 2: Unit- 1 octet, the maximum frame body length – 8 bytes
  At 250kbps, ~ 0.6ms airtime
  At 62.5kbps, ~1.9ms airtime

## Slide 4: Reference
[1] 18/0094r1, Fixing TBDs in WUR frames
[2] 17/1626r2, Frame Format Discussions

## Slide 5: Straw Poll
Do you agree the following?
    The length subfield in Frame Control field indicates the length of the Frame Body in units of 1 octets and the maximum length of the Frame Body is 8 bytes at low data rate (i.e., 62.5kbps).