## Slide 1: Wake Up Response mode to WUR frame
Date: 2018-02-22
Authors:
Name | Affiliation | Address | Email
Kaiying Lv | ZTE Corp. | No.9 XiFeng Road, Xi’An, China | lv.kaiying@zte.com.cn
Bo Sun |  |  | Sun.bo1@zte.com.cn

## Slide 2: Introduction
  IEEE 802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)[1]
The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s).
IEEE 802.11ba shall define Information Element for WUR capability that include following information
  PCR transition delay from doze state to awake state after receiving wake-up frame at STA side
How to efficiently wake up WUR STAs and respond to the WUF is discussed in this proposal.

## Slide 3: Motivation
  AP should be able to make decision the way for WUR STAs to respond to the WUR packet in PCR in order to efficiently control the medium
    Solicited/ triggered response by the AP
    Unsolicited response by contending the medium using EDCA
PCR Transition Delay should be considered when wake up response in PCR is solicited by the AP
    Aligning awake time of WUR STAs with different PCR transition delay would be helpful to reduce power consumption
  Channel access efficiency should be considered when wake up response is unsolicited by contending the medium using EDCA
    Stagger channel access contention from multiple WUR STAs when sending wake up response would be helpful to reduce contention collision

## Slide 4: Proposal (1/3)
A wake up response mode shall be indicated
  A wake up response mode indication is to indicate solicited or unsolicited response mode when receiving a multicast wake up frame
    Solicited response mode: An AP will send a frame (eg. trigger frame) to solicit the wake up response (eg. PS-Poll, QoS Null etc.) from the WUR STA(s)
    Unsolicited response mode: An WUR STA will contend to send a wake up response (eg. PS-Poll, QoS Null etc.)
  An AP can indicate wake up response mode to an WUR STA through PCR when an WUR STA negotiates WUR operation mode with the AP
    Semi-static wake up response mode
    Can only be changed when re-negotiating WUR operation mode
  One bit in an WUF can be used for dynamic wake up response mode indication
    One bit in frame body of WUR packet
    The response mode can be changed and indicated per WUR packet

## Slide 5: Proposal (2/3)
A wake up delay information shall also be indicated:
  A wake up delay indication is to indicate for an WUR STA to delay to turn on its PCR after receiving its WUF.
    A target trigger time offset to the average PCR transition delay (eg.10ms) after receiving an WUF if the WUR is indicated to be solicited by AP’s trigger to send the wake up response
    A delay window to for a WUR STA to randomly select a delay time after receiving an WUF if WUR STA is indicated to contend the medium to send the wake up response
  An AP can indicate wake up delay information to an WUR STA through PCR when an WUR STA negotiates WUR operation mode with the AP
    eg. Value “00” means no extra delay;
    eg. value “01” mean 0.5ms target trigger time offset to of average PCR transition delay after receiving the WUF for solicited response
    eg. value “01” mean 0.5ms delay time window for unsolicited response
  A wake up delay information can also be dynamically indicated in the frame body of an WUF
    can be changed and indicated per WUR packet

## Slide 6: Proposal (3/3)
Example of wake up delay shown as below
  STA1 and STA2 have PCR transition delay of 10ms indicated in WUR capability element
  STA3 and STA4 have PCR transition delay of 8ms indicated in WUR capability element
  STA1,2,3,4 are indicated solicited response mode and 10ms target trigger time (time offset set to “0” based on average PCR transition delay of 10ms)
    STA1 and STA2 turn on their PCR right after receiving the WUF
    STA3 and STA4 may turn on their PCR 2ms later after receiving the WUF

## Slide 7: Conclusion
Wake up response mode indication is proposed to indicate the solicited/unsolicited response to a WUF in PCR.
The wake up delay for solicited/unsolicited response is proposed to improve channel access efficiency.
We suggest that an AP indicate the wake up response mode and its corresponding wake up delay information in order to have better utilization of the resource and improve WUR STAs’ power efficiency.
  through PCR or through WUF or both

## Slide 8: Straw Poll 1
Do you support adding the following to 11ba SFD?
A wake up response mode and wake up delay information shall be signaled
  To indicate solicited or unsolicited response in PCR to a wake up packet
  To indicate target trigger time offset / wake up delay window
  Y:
  N:
  A:

## Slide 9: Straw Poll 2
Do you support adding the following to 11ba SFD?
A wake up response mode and wake up delay information shall be signaled through
  Option 1: WUR mode negotiation
  Option 2: frame body field in a WUR packet
  Option 3: Both WUR mode negotiation and frame body field in a WUR packet
  Y:
  N:
  A:

## Slide 10: References
[1] 11-17/0575r9 “spec framework”, Po-kai Huang
[2] 11-17/1359r0 “considerations for wur response”