## Slide 1: MC-OOK Symbol Design
Date: 2018-03-DD
Authors:

## Slide 2: Introduction
According to the SFD [1]
  “When a single band is used for transmission of WUR PPDU, the OOK waveform of WUR PPDU is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5 kHz:
    -The center subcarrier is null”
Low PAPR MC-OOK waveforms have been proposed in [2] and [3]
This contribution introduces MC-OOK waveforms that have very low PAPR and good performance
The question of the use of the DC subcarrier is revisited

## Slide 3: Symbol Generation Methodology
Generate a time-domain single carrier waveform (using continuous phase modulation) with constant envelope and 4 MHz bandwidth
Transform single carrier waveform to frequency domain
Quantize Fourier coefficients to 256-QAM and mute all inactive subcarriers (i.e. null all subcarriers except 13 contiguous subcarriers)  multicarrier waveform that resembles constant envelope waveform is generated.

## Slide 4: Design for 4 us symbols
64 point IFFT
0.8 us CP

## Slide 5: Proposed frequency domain symbols (256-QAM), 4 us symbol
Subcarrier | Proposed, with DC | Proposed, no DC
-6 -5 -4 -3 -2 -1 DC 1 2 3 4 5 6 | -0.5369 - 0.2301i -0.5369 - 0.8437i -0.0767 - 0.9971i 0.6903 - 1.1504i 0.9971 - 0.3835i -0.6903 - 0.0767i -0.9971 - 0.9971i 0.0767 + 0.6903i -0.3835 + 0.9971i 1.1504 - 0.6903i -0.9971 - 0.0767i 0.8437 + 0.5369i -0.2301 - 0.5369i | -0.6903 - 0.3835i -0.5369 + 0.6903i -0.0767 + 0.0767i 0.6903 + 1.1504i 1.1504 - 0.6903i -0.6903 + 0.0767i 0.0000 + 0.0000i 0.0767 - 0.6903i 0.6903 - 1.1504i 1.1504 + 0.6903i -0.0767 + 0.0767i 0.6903 - 0.5369i 0.3835 + 0.6903i

## Slide 6: I/Q diagrams of proposed symbols, 4 us symbol
Benchmark: opt1 [2] Proposed

## Slide 7: Instantaneous power of proposed MCS-OOK waveforms, 4 us symbol

## Slide 8: MC-OOK waveform performance
Data rate: 62.5 kbps, 4 us symbols
Waveform | PAPR (dB) | SNR (dB) @10% PER AWGN | SNR (dB) @10% PER TGnB | SNR (dB) @10% PER TGnD
DC only | 0 | -9.1 | 0.1 | -0.9
Random QPSK | > 5 | -8.5 | 0.1 | -2.2
Opt 1 [1] | 2.1 | -8.8 | 0.0 | -2.3
Proposed with DC | 0.6 | -8.7 | 0.0 | -2.3
Proposed no DC | 1 | -8.9 | 0.0 | -2.3

## Slide 9: Performance 62.5 kbps

## Slide 10: Design for 2 us symbols
32 point IFFT
0.4 us CP

## Slide 11: Proposed frequency domain 2us symbols (256-QAM)
Subcarrier | Proposed, no DC
-3 -2 -1 DC 1 2 3 | 0.2301 + 0.5369i 0.0767 + 1.1504i -0.3835 + 0.9971i 0 0.9971 - 0.3835i -1.1504 - 0.0767i 0.5369 + 0.2301i

## Slide 12: I/Q diagrams of proposed 2 us symbols
Benchmark: trade-off [3] Proposed

## Slide 13: Performance 250 kbps using 2 us symbols

## Slide 14: MC-OOK waveform performance
Data rate: 250 kbps
Waveform | PAPR (dB) | SNR (dB) @10% PER AWGN | SNR (dB) @10% PER TGnB | SNR (dB) @10% PER TGnD
Random QPSK | > 5 | -4.1 | 4.8 | 1.7
Best tradeoff [3] | 3.5 | -4.1 | 4.7 | 1.0
Proposed no DC | 0.6 | -4.7 | 4.6 | 1.3

## Slide 15: Observations 1
Constant envelope waveforms exhibit the best performance in AWGN
Waveforms with equal power in all active subcarriers exhibit the best performance in fading channels, due to harvesting of frequency diversity
Proposed waveforms have nearly constant envelope
Proposed waveforms don’t have zero crossings

## Slide 16: Observations 2
Proposed waveforms show gains in AWGN channel, with respect to waveforms with equal power in all active subcarriers
Proposed waveforms may suffer small losses at high SNR in fading channels, with respect to waveforms with equal power in all active subcarriers
62.5 kbps | 250 kbps
0.2 dB gain | 0.6 dB gain
62.5 kbps | 250 kbps
No losses for TGnB | No losses for TGnB
No losses for TGnD @ 10% PER | 0.3 dB loss for TGnD @ 10% PER

## Slide 17: Observations 3
The proposed waveforms have a substantially lower PAPR than other MC-OOK waveforms presented in [2], [3]
Proposed waveforms are advantageous when the TX is PA limited
Use of the DC subcarrier allows a PAPR reduction of 0.5 dB compared to waveform with null DC (62.5 kbps only)
62.5 kbps | 250 kbps
PAPR reduction 1.1dB -1.6dB | PAPR reduction 2.9dB

## Slide 18: Straw poll #1
For the 4 us symbol, do you prefer to specify:
Proposed with DC
Proposed no DC
Both of the above
Other waveform(s)
To not specify a waveform
1/2/3/4/5:

## Slide 19: Straw poll #2
For the 2 us symbol, do you prefer to specify:
Trade-off [3]
Proposed
Both of the above
Other waveform(s)
To not specify a waveform
1/2/3/4/5:

## Slide 20: References
[1] IEEE 802.11-17/0575r9 Specification Framework for TGba
[2] IEEE 802.11-17/0964r4 Signal Bandwidth and Sequence for OOK Signal Generation
[3] IEEE 802.11-18/0097r0 2 us OOK pulse for high rate

## Slide 21: Appendix
PSD of OOK signals using proposed waveforms, with windowing according to equation (17-5) IEEE 802.11-2016