## Slide 1: 3GPP TSG SA Status Update
Date: 2018-03-06
Authors:

## Slide 2: Abstract
This document provides an update on the current status of the 3GPP TSG SA specifications which relate to integration of 802.11 WLAN with the 3GPP 5G Core Network via non-3GPP access and a brief overview of some of the specified features.

## Slide 3: AANI SC/3GPP TGS SA Correspondence and Overview
Incoming LS from 3GPP SA TSG – 6/17 - (11-17/0903r0): “Reply LS to IEEE 802.11 Requesting Status and Information on WLAN integration in 3GPP NextGen System”
The reference documents provided in the 3GPP SA reply were summarized in: 11-17/1064r0 – “Overview of 3GPP SA Next Generation System Documents”
3GPP TSG SA has completed the following specifications:
  23.501 v15.0.0: System Architecture for the 5G System; Stage 2 (Release 15) 2017-12
  23.502 v15.0.0: Procedures for the 5G System; Stage 2 (Release 15) 2017-12
3GPP TSG SA is still working on the following specifications:
  33.501 v0.7.1: Security architecture and procedures for 5G system (Release 15) 2018-01
3GPP TSG SA is still working on the following studies:
  TR 23.793 v0.2.0: Study on Access Traffic Steering, Switching and Splitting support in the 5G system architecture (Release 16) 2018-01
    Status – move from Rel-15 to Rel-16 – end date: 2018-09-13

## Slide 4: 23.501 v15.0.0: System Architecture for the 5G System; Stage 2 (Release 15) 2017-12 - Update
Untrusted non-3GPP access has been specified (trusted non-3GPP access is TBS)
4.1 General concepts - changes:
  Minimize dependencies between the Access Network (AN) and the Core Network (CN). The architecture is defined with a converged access agnostic core network with a common AN - CN interface which integrates different Access Types e.g. 3GPP access and non-3GPP access types.
4.2.2 Network Functions and entities - changes:
  Removed:
    Structured Data Storage network function (SDSF)
  Added:
    Network Slice Selection Function (NSSF)
    Unified Data Repository (UDR)
    5G-Equipment Identity Register (5G-EIR)
    Security Edge Protection Proxy (SEPP)

## Slide 5: 23.501 v15.0.0: System Architecture for the 5G System; Stage 2 (Release 15) 2017-12 – Update (cont.)
4.2.8.1 General concepts to Support Non-3GPP - changes:
  It shall be possible to maintain the UE signalling connection with the AMF over the non-3GPP access after all the PDU Sessions for the UE over the non-3GPPthat access have been released or handed over to 3GPP access.
  Added: User plane QoS differentiation between UE and N3IWF is supported as described in clause 5.7 and TS 23.502 [3] clause 4.12.5
Added:
  4.3.3 Interworking between 5GC via non-3GPP access and E-UTRAN connected to EPC
  5.3.2 Registration Management: “The 3GPP and Non-3GPP RM states are independent of each other, see clause 5.3.2.4.”
  Many changes to: 5.3.2.4 Support of a UE registered over both 3GPP and Non3GPPNon-3GPP access
  Many changes to: 5.5 Non-3GPP access specific aspects
  Many changes and additions to: 6.3.6 N3IWF selection

## Slide 6: 23.502 v15.0.0: Procedures for the 5G System; Stage 2 (Release 15) 2017-12 – Update
Untrusted non-3GPP access has been specified (trusted non-3GPP access is TBS)
4.9.2 Handover of a PDU Session procedure between 3GPP and untrusted non-3GPP access – basically completely re-written
  Provides handover procedures for:
    From untrusted non-3GPP access to 3GPP access
    From 3GPP access to untrusted non-3GPP access
4.12 Procedures for non-3GPP access – basically completely re-written
  Note: HO/Mobility procedures between 3GPP AN and non-3GPP and vice versa is to be added

## Slide 7: 33.501 v0.7.1: Security architecture and procedures for 5G system (Release 15) 2018-01 - New
Untrusted non-3GPP access has been specified (trusted non-3GPP access is TBS)
Status: v0.8.0 will be submitted to the SA plenary for information (March 21-23 2018) and for approval to v15.0.0 (June 13-15 2018).
6.1 Primary authentication and key agreement:
  “Keys for more than one security context can be derived from the KSEAF without the need of a new authentication run. A concrete example of this is that an authentication run over a 3GPP access network can also provide keys to establish security between the UE and a N3IWF used in untrusted non-3GPP access.”
  “This implicit serving network authentication shall be provided to the UE irrespective of the access network technology, so it applies to both 3GPP and non-3GPP access networks.”

## Slide 8: 33.501 v0.7.1: Security architecture and procedures for 5G system (Release 15) 2018-01 – New – (Cont.)
6.2 Key hierarchy, key derivation, and distribution scheme:
  “Keys in the N3IWF
    The N3IWF receives KN3IWF from the AMF.
    The N3IWF shall use KN3IWF as the key MSK for IKEv2 between UE and N3IWF in the procedures for untrusted non-3GPP access, cf. clause 11.”
  There are open issues which are FFS regarding non-3GPP access keys.
7.0 Security for non-3GPP access to the 5G core network
  This clause specifies how a UE is authenticated to 5G network via an untrusted non-3GPP access network.

## Slide 9: TR 23.793 v0.2.0: Study on Access Traffic Steering, Switching and Splitting support in the 5G system architecture (Release 16) - New
This study is currently on going.
This study address:
  Access Traffic Steering: The procedure that selects an access network for a new data flow and transfers the traffic of this data flow over the selected access network. Access traffic steering is applicable between 3GPP and non-3GPP accesses.
  Access Traffic Switching: The procedure that moves all traffic of an ongoing data flow from one access network to another access network in a way that maintains the continuity of the data flow. Access traffic switching is applicable between 3GPP and non-3GPP accesses.
  Access Traffic Splitting: The procedure that splits the traffic of a data flow across multiple access networks. When traffic splitting is applied to a data flow, some traffic of the data flow is transferred via one access and some other traffic of the same data flow is transferred via another access. Access traffic splitting is applicable between 3GPP and non-3GPP accesses.
  Multi-Access PDU Session: A PDU session whose traffic can be sent over 3GPP access, or over non-3GPP access, or over both accesses.

## Slide 10: References
LS (11-16/1574r3) to 3GPP SA (5/17): “IEEE 802.11 Working Group Liaison Statement Requesting status and technical information on WLAN integration in 3GPP NextGen System.”
LS (11-17/0903r0) from 3GPP SA TSG – 6/17 – “Reply LS to IEEE 802.11 Requesting Status and Information on WLAN integration in 3GPP NextGen System”
11-17/1064r0 – “Overview of 3GPP SA Next Generation System Documents Reviewed the 3GPP SA Documents provided in the reply LS
3GPP TR 23.799 “Study on Architecture for Next Generation System”
3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
3GPP TS 23.501 System Architecture for the 5G System (Stage 2), companion to TS 23.502
3GPP TS 23.502 Procedures for the 5G System (Stage 2), companion to TS 23.501
3GPP TS 33.501 Security Architecture and Procedure for the 5G System
3GPP TR 23.793 “Study on Access Traffic Steering, Switching and Splitting support in the 5G system architecture”