## Slide 1: WUR Discovery Frame Format
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
A type of WUR discovery frame has been supported in the current specification framework for 11ba [1]
  R.4.8.A: Define a type of WUR frame as WUR Discovery frame to assist the STAs to discover the BSS.
Furthermore, smart scanning using WUR discovery has been added to WUR usage mode document [2]
WUR discovery frame includes compressed SSID, PCR operation channel, and AP identifier [3]
On the other hand, a format of WUR discovery frame has not been specified yet
In this contribution, we propose a specific WUR discovery frame format for smart scanning

## Slide 3: Proposed Methods
Option 1: Mandatory information into MAC header
  Frame control (8 bits) + Address (12 bits) + TD control (12 bits) = 32 bits
    Type (e.g. 4 bits)
    APID as is (e.g. 12 bits)
      Use Address field itself
    PCR channel (e.g. 8 bits)
    Compressed SSID (e.g. 8 bits)
  No capability issue for STAs which can not support Frame Body field
  Collision could be occurred, but it might be trivial
  Length or misc. field can be used for a part of the mandatory information
Address
Frame Control
TD Control
APID
Compressed SSID
8 bits
12 bits
12 bits
Type
PCR Channel
Frame Body
FCS
An example of WUR discovery frame
Field order and size are TBD
FCS

## Slide 4: Proposed Methods
Option 2: Mandatory information into MAC header and Frame body
  Frame body should be mandatory for WUR discovery frame in this option
  If so, there would be more room for mandatory information
    E.g. Lengthened APID or SSID to avoid hash collision
  Collision probability would be decreased due to the lengthened APID or SSID
  Length or misc. field can be used for length indication or miscellaneous information rather than a part of the mandatory information of discovery
  Extra information (in order to support other applications) can be included in Frame body field
Address
Frame Control
TD Control
APID
Compressed SSID
8 bits
12 bits
12 bits
Type
PCR Channel
Frame Body
FCS
e.g., 8 octets
FCS
An example of WUR discovery frame
Field order and size are TBD
Length/Misc

## Slide 5: Summary
We have discussed a specific frame format for WUR discovery
To support mandatory things, these need to be squeezed or additional space (i.e., frame body field) is needed

## Slide 6: Straw Poll 1
Which option do you prefer as a WUR frame format for discovery? (Size and location of the information is TBD, Mandatory information includes compressed SSID, PCR operation channel, and AP identifier)
  Option 1: Put mandatory information into MAC header (in Slide 3)
  Option 2: Put mandatory information into the field which consist of MAC header and Frame body (in Slide 4)
  A

## Slide 7: References
[1] 11-17/0575r9, “Spec framework”
[2] 11-17/0029r10, “WUR usage model document”
[3] 11-18/0160r7, “WUR discovery frame content”