## Slide 1: Ultra Short Range Channel
Date: 2018-03-01
Authors:

## Slide 2: Abstract
This presentation discuss channel access for Ultra Short Range (scenario) as resolution to CID 1084.

## Slide 3: CID 1084
As there is a close proximity use case, to achieve it, mechanism of determining carrier sense level according to transmission power, i.e., when transmission power is lower then carrier sense level is higher, should be included somewhere in section 10. | As in comment.

## Slide 4: Discussion
What is “close proximity” or “Ultra Short Range”?
We propose that this is limited to transmissions within a range of 10cm (D1).
What change is needed in Channel Access rules?
We propose that if the device does not create significant interference at a ragne of 30cm (D2), it may ignore channel access rule (i.e it may transmit even when there is NAV or active packet on the medium).

## Slide 5: What is significant interference
We propose that significant interference will be defined as causing interference of 3dB below MCS 1 sensitivity at range of 30cm.
This means that the EIRP of TX in this case is limited to -13.5dBm
This mean that device at 10cm receives at most -65dBm
  This would limit the rate in USR to MCS 8 (1.925Gbs)
This rate may be too low
  We can fix that by either reducing D1 (e.g. to 5cm) or increasing D2

## Slide 6: Options for Resolution
Add an exception to channel access rules:
  “If the EIRP of the Transmitter is below -13dBm (resulting in a level of 3dB below MCS1 at a range of 30cm), a STA may initiate transmission even if PHY-CCA.indication(busy) or NAV is active”
Reject the comment
Modify the numbers (30cm, -13dBm)
Adapt the CCA sensitivity to TX-Power/EIRP

## Slide 7: References