## Slide 1: Summary of BCS Discussion Points
Date: 2018-03-08
Authors:

## Slide 2: Abstract
Summary of discussion points that came up during the BCS sessions

## Slide 3: Commonality in use cases
Simultaneous transmission of an information from a single source to multiple destinations
“Downstream scenario”: AP sends a information in a single MAC frame (i.e. simultaneously) to several STA
“Upstream scenario”:
  STA wants to send information to a receiving entity but does not care via which AP it is forwarded.
  Hopes that an AP picks the message up and forwards it. (broadcasting)
  May address a specific AP but does not want to associate

## Slide 4: Discussion items
Requirement of the sending STA to “know” that a receiving STA is present?
  Not necessarily, open for discussion
Always broadcast
  Depends on the scenario. Most likely yes, but
  There are use cases in which a (single) self-contained frame might be send towards a specific receiving STA (unicast) without association
  Is there always bi-directional traffic or only uni-directional traffic
  Do we need to support optional negotiation of broadcast service parameters?
Where do the packets end?
  Beyond the AP (for upstream information)
    Should consider if the AP analysis / compiles the frame before “blindly” forwarding it beyond the AP
  Involves at least the DS
  Relation to higher layer protocols, at least IP address of the final destination (and identify source via MAC address?)
What are the packets: MSDU vs. MPDU  MSDU

## Slide 5: Discussion items (cont)
Discuss “downstream” (APSTA) and „upstream“ (STAAP) separately
  Requirements are likely to be different
  Technical solutions might overlap
  Single PAR or two PARs?

## Slide 6: Security Questions
What kind of “trust” exists today between STA and AP after initial packet exchange (4-way handshake, EAP, EPOL-Key…)?
  Trust between STA and AP
  Prevention from replay attacks
What are the precise security requirements of the use cases
  Authentication of sender (of transmission)
  Authentication of receiver (of transmission)
  Prevention of replaying frames required
  Integrity protection
  Encryption
What is the threat for each use case?
Assumption (to be verified) use cases do not need mutual trust, i.e. we do not need that “AP trusts STA” && “STA trusts AP”
As the flow of information is only directional, we only need to achieve “AP trusts STA” or (!!) “STA trusts AP”
  Is this possible to achieve in a single self-contained packet transmission?
  Is the lack of auth in both directions a problem?
Relation to higher layer security (e.g. higher layer association and security with end- / application-server)
  Where is the difference from what we provide in 802.11 today vs. what the suggested solution would offer

## Slide 7: Competitors
Difference to existing technologies
  LoRa WAN
Other technology / systems that can address the use cases / do we prefer WiFi in contrast to other technologies?

## Slide 8: Other
Should a frequency band be specified?
Is the proposed approach feasible for all PHYs?
Is the proposed approach feasible for possible receiver STA roles?
Do we see a benefit in spectrum usage?
  Need evaluation criteria
Analysis for broad market potential
Can we prevent “unsolicited broadcast”

## Slide 9: References