## Slide 1: 802.11ba Architecture Discussion
Date: 2017-02-06
Authors:

## Slide 2: Abstract
This presentation addresses some of the issues that were listed as questions to TGba in a prior ARC session
The intent in this presentation to is provide resolutions to the issues or list additional questions/issues to make progress toward a resolution
The intent in this presentation is not to propose new features to Tgba.
New ideas/proposals to ba is best addressed when proposed and discussed directly in a ba session

## Slide 3: Current 802.11 architecture concepts
A STA typically has a single MAC, single PHY, and Mgmt

## Slide 4: How is the 802.11ba STA related to other 802.11 STAs/AP?
Is the WUR STA in a BSS, IBSS?
  WUR STA is akin to HT STA or VHT STA, etc. WUR STA is not a physical device but just an operating mode of the IEEE802.11 STA
  802.11ba enables a new mode of operation for the legacy 802.11 STA while operating over a 802.11n, 802.11ac or 802.11ax PHY
  The WUR-mode is configured when the 802.11 STA associates with a 802.11 AP. Only the BSS topology between the 802.11 STA and the 802.11 AP is supported for the 802.11STA to have its WUR-mode configured
  The non-WUR radio in the WUR-capable 802.11 STA is called the Primary Connectivity Radio (PCR)
  The WUR-mode is a low power operating mode where only the Rx Chain (called WURx) is active and can receive WUR frames from a 802.11 transmitter.
  The WURx is in WURx active or WURx doze state while the corresponding 802.11 STA is in doze state

## Slide 5: Current 802.11 architecture concepts
There are devices with more than one PHY:
An “AP device” (a box people tend to call an “AP”) typically has multiple PHYs (different bands). These are separate STAs, that happen to be collocated. Interaction between them is out of scope for 802.11. (Effectively, it is via the DS, just like non-collocated APs.)
802.11ad added the concept of FST, and a multi-band device. These, again, contain multiple STAs, but with Management and an optional Transparent FST Entity interconnection that is within 802.11 scope.

## Slide 6: Current 802.11 architecture concepts
There is no “STA” with more than one PHY
A “STA” is a singly addressable instance of a MAC and PHY
  With 802.11ba WUR-mode enabled, the definition of ‘STA’ still holds
  Enabling 802.11ba WUR-mode does not result in a ‘STA’ with more than one PHY active at the same time
  802.11ba enables a new mode of operation for the PHY where the receiver operates in a low power mode – Clause 17 PHY followed by a simple modulation scheme

## Slide 7: Architectural Concepts
Ba amends the definition of the 802.11-2016 STA
  802.11ba amends the definition of the 802.11 OFDM PHY by enabling a new mode of operation called WUR-mode
    802.11 AP: upon a WUR Setup exchange with the STA, configure 802.11 STA that is WUR-Capable with operating parameters while in WUR-mode
    802.11 STA: upon a WUR Setup exchange with the STA, accept operating parameters for operating in WUR-mode; and WURx operation
the WUR STA [physical box] is a
  There is no concept of a WUR STA as a physical box and hence the physical box is still a 802.11 STA. The specification uses the term WUR STA to identify the 802.11 STA that is capable of operating in WUR-mode
  There is a concept of a 802.11 STA with its OFDM PHY operating in WUR-mode
  802.11ba defines a new modulation scheme for 802.11 OFDM PHYs to transmit with; and for 802.11 OFDM PHYs in WUR-mode to receive
  The 802.11 OFDM PHY of a 802.11 STA is configured to operate in WUR-mode after association with the 802.11 AP via a WUR Setup frame exchange – a Wake Up ID and a Group ID is assigned to the STA upon successful setup

## Slide 8: Questions/topics for TGba
Is the WUR an independent PHY? No. It is a new mode of OFDM PHY operation
Is the WUR an independent MAC? No
Is the WUR always physically collocated with an 802.11 AP or STA? No. It is a capability and not a logical entity (The capability is enabled if the corresponding implementation has <<tbd> MIB variable> set to true)
Does the WUR have an address? Or, does it “share” the collocated STAs address? WUR is a capability of a 802.11 STA operating in 802.11n, 802.11ac or 802.11ax. There is only one MAC address
Does the WUR MAC connect to/integrate with the 802.11 MAC? As defined in 802.11-2016
OR… Does the WUR ‘wake’ the device, and the device contains independent WUR and an 802.11 MAC/PHY, and some ‘host function’ between them? See response to 5

## Slide 9: Questions/Topics for TGba
Perhaps related/duplicate: Does the introduction of the WUR impact the behavior of a collocated/integrated STA’s MAC/PHY? Only in the following aspects:
  Activate the STA’s MAC/PHY on the receipt of a ‘Wake Up’ frame by while in WUR-mode, from a peer
  Do some vendor specific action which may have an impact on the STA’s MAC/PHY on the receipt of a ‘WUR Vendor Specific’ frame while in WUR-mode. from a peer

## Slide 10: More advanced questions/topics for TGba
Does a WUR associate to a BSS? When a 802.11-2016 STA associates with an AP and operates in .11n, .11ac or .11ax mode associates, WUR-mode may be configured in the 802.11-2016 STA (when the STA is WUR-capable)
If yes, the same BSS as any collocated/integrated STA, or a separate ‘overlay’ BSS of WUR devices? See response to 1.
Does the WUR work with all 802.11 PHYs e.g. a, b, g, n, ac, ad, ah, ax, ay? Draft 0.1 only calls out .11n, .11ac and .11ax
Does the WUR work with mesh STAs? IBSS? OCB? The specification (802.11ba D0.1) only addresses BSS. Other topologies may be addressed in a future project.

## Slide 11: TGba architecture new questions (from July 12 ARC)
Does every WUR stack have an individual “ID” (“WUR address”)? Or, could a given WUR stack be only addressed using a “group ID” in some scenarios? a WUR ID and a group ID are assigned when WUR-mode is configured
How are WUR ID’s made globally unique, or are they? What about overlapping WUR coverage? Prevented using the same solution as security protections? Prevented through selection of different sub-carriers? WUR ID is like AID. Need not be globally unique.
How does the WUR stack become aware of ongoing NAV protections? RX doesn’t need to know. What about the TXr? Uses the same rules currently defined in 802.11-2016 for channel access and protection
For protection – how much of a legacy frame header is sent? Just PHY header? Some MAC header (addresses? NAV? Etc) Just the preamble

## Slide 12: TGba architecture new questions (from July 12 ARC)
Is there any sharing (necessarily, as part of the design, not implementation choice) of RF front-end?
  The WUR waveform is defined to be Multi-carrier On-Off Keying (OOK) which means on the transmitter side we will reuse OFDM transmitter + ON/OFF Keying modulation. Therefore it is possible to reuse the existing hardware with some minor addition/modification, however, this would be an implementation choice.
  On the receiver, the WUR is completely new hardware that has to have a low power design. The OOK modulation and narrower bandwidth (4MHz) has been wisely selected for the WUR waveform to allow a simple and low power receive, which is a non-coherent envelop detector.

## Slide 13: TGba architecture potential assumptions (from July 12 ARC)
What happens when the Main stack wakes up? Does it still have an association? Is it in some power save state (which)? Yes the AP and the STA remain associated while the STA is operating in WUR_mode.
What about error recovery? STA goes out of range? What if the AP changes (DFS, ITS, etc)? Same rules that apply to the 802.11-2016 STA applies to the WUR-mode enabled 802.11-2016 STA
How does the WUR stack become aware of ongoing NAV protections?
  RX doesn’t need to know. The master’s Main stack obeys the IEEE802.11-2016 medium access rules, and wait until it has a TXop, then triggers the WUR to TX.
  On the RXr, only one stack (WUR or Main) are active at a given point in time.
  When the Main stack wakes up, it still has an association and is in a power save state (a new “WUR” power save state). The Main stack TXs, which is the indication that the wakeup was successful and completed.

## Slide 14: TGba architecture potential assumptions (from July 12 ARC)
There are 100% RX WURs, at the sleeping node. There are TXrs, on the master node, and these are therefore (potentially) different architecturally.
  Needs more discussion in ARC
  The WUR transmission from the master node (AP) follows the standard IEEE802.11-2016 medium access rules.
  The WUR-mode Rx at the sleeping node(s) (WUR-capable STA(s)) are just receivers looking for a WUR frame to be transmitted by the master (AP)
The WUR “wakeup” frame does not NAV protect to cover the sleeping device’s Main radio waking up and TXing.
  The std IEEE802.11-2016 STA at the sleeping device follows IEEE802.11-2016 medium access rules, acquires the medium and transmits. Does not need any special NAV protection.
Review 11-17/972 to confirm/before proceeding on the above