## Slide 1: Broadcast Service flow and evaluation
Date: 2018-03-8
Authors:

## Slide 2: Abstract
This presentation describes a prospected service flow of BCS and evaluation method for the feasibility study

## Slide 3: Overview of Broadcasting
Single way Authentication
  AP do not request to authenticate STAs, because this is a Broadcast.
  STA may request authentication of desired AP to avoid undesired broadcast service.
Benefit
  User experience
    Simple operation as like a radio and TV service. (Passive device operation)
    No any link setup process are required.
    Protect user privacy
      user device never transmit any personal information such as a mac address
  Efficient spectrum use
    Definitely reduce the air time consumption.
  Easy implementation over existing system.
    No any changes of PHY are required.
  Boost new market
    Create new market model by broadcasting services.

## Slide 4: Prospected services flow
Preparation
  AP indicate service capability by broadcasting frame without any authentication.
  STA decide to receive or not by the capability information.
Data flow
  Service host transmit broadcast service frame with some indicator.
  AP transmit the broadcast frame to broadcast address.
  STAs receive the broadcast frame simultaneously.
Service Host
IEEE802.3
AP
IEEE802.3
STA
IEEE802.11
IEEE802.11
STA
IEEE802.11
STA
IEEE802.11

## Slide 5: Discussion point of service
How AP choose the desired frame to broadcast.
  Destination address?
How AP provide the capability information to STAs.
  Specify identify IE in Beacon
  Specify identify IE in FILS discovery frame
  Specify identify IE in TGaq frame
What kind of information is required to recognize the desired broadcasting services.
  Which channel
  Who‘s services
  Type of contents etc,.

## Slide 6: Evaluation of the efficiency of spectrum use
Condition parameter
  Number of STA
  Size of transmit frame
Comparison Unicast Vs Broadcast
Additional parameter what we have to consider
  FEC
  Data rate
    BCS may use lower data rate
BCS reduce xxx% of airtime occupation when at least N=x or more STA receive the same information.
N: Number of STAs
Air time occupation
N=1
Unicast
Broadcast
Broadcast with FEC
Break even point
N=x