## Slide 1: 60GHz AOD-Messaging
Date: 2018-03-01
Authors:

## Slide 2: Abstract
This presentation describes the protocol and message changes needed to enable use of Angle of Departure (AOD) in 60GHz Direction measurement protocol

## Slide 3
Problem Statement
While it is well defined within the protocol how AOA is sent from the responder to the initiator. It is not clear how to return either the Best Sector/Channel Measurement feedback or the final AOD results.
What needs to be sent:
  Both initiator and responder need to be able to send Best Sector and Channel Measurement results
  Responder need to be able to send AOD results
Basic Assumption: Only the ISTA needs final direction information.

## Slide 4: What Information Needs To be transferred?
For Initiator to responder AOD:
  Responder Shall send the BS feedback and/or Channel Measurement Feedback
  Initiator determines AOD based on this information
  Proposed Solution: Add BS_feedback field to Direction Measurement Results field and enable adding Channel Measurement Feedback to FTM frame
  enables orientation
For Responder to Initiator AOD:
  Initiator shall send the BS feedback and/or Channel Measurement Feedback
  Responder shall estimate AOD based on this information and send AOD to the initiator
  Problem: During FTM exchanges, the initiator sends only ACKs
  Important – enables direction and location (with ranging)

## Slide 5: How can we deal with the I2R AOD?
The responder collects the BS Feedback results during the burst.
After the burst, the initiator sends an FTM Measurement Frame to the responder, with a list of BS feedback results, the responder responds with an ACK
  Multiple Channel Measurement Feedback
    Channel Measurement Feedback is an element used in DMG.
The responder (possibly after taking time for calculation) responds with an FTM Measurement Frame to the initiator, including a list of AOD results

## Slide 6: Elements to be added

## Slide 7: Protocol Modification
Two exchanges added after the end of the burst
Each of them is a separate channel access
In the first exchange: Multiple BS feedback are sent from the initiator to the responder in an FTM frame
In the second exchange Multiple AOD results are sent from the responder to the initiator in an FTM frame.

## Slide 8: References