## Slide 1: 60GHz AOD-Messaging
Date: 2018-03-01
Authors:

## Slide 2: Abstract
This presentation describes the protocol and message changes needed to enable use of Angle of Departure (AOD) in 60GHz Direction measurement protocol

## Slide 3
Problem Statement
While it is well defined within the protocol how AOA is sent from the responder to the initiator. It is not clear how to return either the Best AWV ID/Channel Measurement feedback or the final AOD results.
What needs to be sent:
  Both initiator and responder need to be able to send Best AWV ID and Channel Measurement results
  Responder need to be able to send AOD results
Basic Assumption: Only the ISTA needs final direction information.

## Slide 4: What Information Needs To be transferred?
For Initiator to responder AOD:
  Responder Shall send the Best AWV ID and/or Channel Measurement Feedback
  Initiator determines AOD based on this information
  Proposed Solution: Add Best AWV ID field to Direction Measurement Results field and enable adding Channel Measurement Feedback to FTM frame
  enables orientation
For Responder to Initiator AOD:
  Initiator shall send the Best AWV ID and/or Channel Measurement Feedback
  Responder shall estimate AOD based on this information and send AOD to the initiator
  Problem: During FTM exchanges, the initiator sends only ACKs
  Important – enables direction and location (with ranging)

## Slide 5: How can we deal with the I2R AOD?
The responder collects the Best AWV ID results during the burst.
After the burst, the initiator sends an FTM Measurement Frame to the responder, with a list of Best AWV ID results, the responder responds with an ACK
  Multiple Channel Measurement Feedback
    Channel Measurement Feedback is an element used in DMG.
The responder (possibly after taking time for calculation) responds with an FTM Measurement Frame to the initiator, including a list of AOD results

## Slide 6: Elements to be added

## Slide 7: Protocol Modification
Two exchanges added after the end of the burst
Each of them is a separate channel access
In the first exchange: Multiple Best AWV IDs are sent from the initiator to the responder in an FTM frame
In the second exchange Multiple AOD results are sent from the responder to the initiator in an FTM frame.

## Slide 8: Strawpoll 1
Do you agree to add the following to the SFD:
“In the DMGz/EDMGz direction measurement protocol, to enable Initiator to Responder AOD measurement feedback, a Best AWV ID field (11bit) will be added to the Direction Measurement result element. As in slide 5. The Best AWV ID will be sent in the first FTM frame sent from the responder to the initiator after the transmission of the AOD TRN field”

## Slide 9: Strawpoll 2
Do you agree to add the following text to the SFD:
“In the DMGz/EDMGz direction measurement protocol, to enable Responder to Initiator AOD feedback, Two new elements will be defined as in slide 7. The exchange of these element, as part of FTM frames will occur after the end of the FTM burst. The multiple Best AWV ID element will be sent by the initiator to the responder. The responder will then send (allowing time for performing the calculation) the multiple AOD feedback element to the initiator.”

## Slide 10: References