## Slide 1: NDP Ranging Error Recovery
Date: 2018-03-06
Name | Affiliation | Address | Phone | Email
Liwen Chu |  |  |  | 
Christian Berger |  |  |  | 
Niranjan Grandhe |  |  |  | 

## Slide 2: Recap: SU/MU NDP Ranging
VHTz NDP ranging includes immediate ranging feedback and delayed ranging feedback.
NDPA
NDP
NDP
Feedback)
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
HEz NDP ranging includes delayed and immediate ranging feedback.
Trigger
NDP
NDPA
NDP
AP
STAs
SIFS
SIFS
SIFS
Feedback
SIFS
Trigger
FTM (TBD)
SIFS
SIFS

## Slide 3: AC for NDPA Transmission in VHTz NDP Sounding
In 802.11baseline, the AC used for the control frame transmission is related to the QoS Data/Management frame.
In 11ax, the AP can use any AC for Trigger frame transmission where Trigger is not combined with other frames.
For VHTz NDP sounding, we propose the similar rules as Trigger in 11ax for the AC selection for NDPA transmission:
  Any AC can be used for SU NDP ranging.
Liwen Chu, et al, Marvell

## Slide 4: Recovery of SU NDP Ranging with Delayed Feedback
For SU NDP with the delayed Feedback, a reference is added to LMR Feedback frame to indicate the SU NDP frame exchange where the LMR feedback is measured
  Otherwise the STA may not know the matching between SU NDP frame exchange and the LMR report as shown below.
This change is also applied to MU NDP ranging.
NDPA
NDP
NDP
Feedback
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
NDPA
NDP
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
Nth NDP exchange
(N-1)th feedback
(N+1)th NDP exchange
(N)th feedback
Nth NDP exchange
(N+1)th NDP exchange
(N-1)th feedback
AP can’t identify the related NDP frames which match T2, T3 in feedback frame.

## Slide 5: Straw Poll 1
Do you support that the LMR feedback frame includes a reference to the associated NDP exchange?

## Slide 6: Straw Poll 2
Do you support that:
  Any AC can be used for the transmission of the NDPA frame within the VHTz ranging.

## Slide 7: Motion 1
Move to add the following text to 11az SFD:
  the LMR feedback frame includes a reference to the associated NDP exchange.

## Slide 8: Motion 2
Move to add the following text to 11az SFD:
  Any AC can be used for the transmission of the NDPA frame within the VHTz ranging.