## Slide 1: NDP Ranging Error Recovery
Date: 2018-03-06
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Ln, Santa Clara, CA |  | liwenchu@marvell.com
Christian Berger | Marvell |  |  | 
Niranjan Grandhe | Marvell |  |  | 

## Slide 2: Recap: SU/MU NDP Ranging
VHTz NDP ranging includes immediate ranging feedback and delayed ranging feedback.
NDPA
NDP
NDP
Feedback
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
HEz NDP ranging includes delayed and immediate ranging feedback.
Trigger
NDP
NDPA
NDP
AP
STAs
SIFS
SIFS
SIFS
Feedback
SIFS
Trigger
FTM (TBD)
SIFS
SIFS

## Slide 3: Access Category for NDPA Transmission in VHTz
In 802.11baseline, the Access Category (AC) used for the control frame transmission is related to the QoS Data/Management frame.
In 11ax, the AP can use any AC for Trigger frame transmission where Trigger is not combined with other frames.
For VHTz NDP sounding, we propose a similar rule as Trigger in 11ax for the AC selection for NDPA transmission:
  Any AC can be used for VHTz ranging.
Liwen Chu, et al, Marvell
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS

## Slide 4: Recovery of VHTz Ranging with Delayed Feedback
For VHTz ranging with delayed feedback, a reference is added to the LMR Feedback frame to indicate the VHTz sounding frame exchange where the LMR feedback was measured
  Otherwise the STA may not know the matching between VHTz sounding frame exchange and the LMR report as shown below.
This change should also apply to HEz ranging.
NDPA
NDP
NDP
Feedback
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
NDPA
NDP
NDPA
NDP
NDP
Feedback
STA
AP
SIFS
SIFS
SIFS
SIFS
Nth NDP exchange
(N-1)th feedback
(N+1)th NDP exchange
(N)th feedback
Nth NDP exchange
(N+1)th NDP exchange
(N-1)th feedback
AP can’t identify the related NDP frames which match T2, T3 in feedback frame.

## Slide 5: Straw Poll 1
Do you support that the LMR feedback frame includes a reference to the associated NDP exchange?

## Slide 6: Straw Poll 2
Do you support that:
  Any Access Category (AC) can be used for the transmission of the NDPA frame within the VHTz ranging.

## Slide 7: Motion 1
Move to add the following text to 11az SFD:
  the LMR feedback frame includes a reference to the associated NDP exchange.

## Slide 8: Motion 2
Move to add the following text to 11az SFD:
  Any Access Category (AC) can be used for the transmission of the NDPA frame within the VHTz ranging.