## Slide 1: Overview of Proposed text changes to support Group Beamforming and Other Beamforming procedures
Name | Affiliation | Address | Phone | Email
Tony Xiao Han | Huawei |  |  | tony.hanxiao@huawei.com
Yan Xin |  |  |  | yan.xin@huawei.com
Chenlong Jia |  |  |  | jiachenlong@huawei.com
Mengyao Ma |  |  |  | ma.mengyao@huawei.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Oren Kedem |  |  |  | oren.kedem@intel.com
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Assaf Kasher |  |  |  | akasher@qti.qualcomm.com
Djordje Tujkovic | Facebook | 1 Hacker Way Menlo Park, CA 94025 USA |  | djordjet@fb.com
Krishna Gomadam |  |  |  | kgomadam@fb.com
Payam Torab |  |  |  | ptorab@fb.com
Michael Grigat | Deutsche Telekom AG | Deutsche-Telekom-Allee 7, 64295 Darmstadt, Germany | +49-6151-5833533 | m.grigat@telekom.de

## Slide 2: Background TDD beamforming operations
Draft 1.1 has defined individual beamforming based on [4]; proposed beamforming text revision [5] this week extends the beamforming procedure to group beamforming, and also covers the other procedures for Distribution Networks described in [1-3]
  Periodic beamforming (e.g., for beam refinement) – a connected target STA sweeps its sectors (synchronously with Initiator, under SME control) and reports measurements (TDD Route IE) to controller (SME for 802.11 description) – no beamforming packet sent by responder
  Interference scan (measurement) – all neighboring connected STAs sweep their sectors (synchronously with Initiator, under SME control) and report measurements (TDD Route IE) to controller (SME for 802.11 description) – no beamforming frame sent by responder

## Slide 3: Background Periodic beamforming and interference measurement unified
Procedures are the same from protocol standpoint, with RA (typically) set to a unicast address in the first case and broadcast address in the second
  Responder transmitting no frames, i.e., no TDD SSW Feedback
  Initiator behavior the same as individual beamforming, except no TDD SSW Ack
These procedures are unified into one operation - TDD Beam Measurement
The scope of the beamforming text revision
  Adding group beamforming
  Adding beam measurement
  “Group Beamforming” field added to clear the ambiguity with broadcast RA
  MLME extensions to cover the procedures at initiator and responder

## Slide 4: TDD Beamforming Control field Include beamforming operation type
TDD Group Beamforming and TDD Beam Measurement fields added to TDD Beamforming Control field to resolve ambiguity
 | TDD Group Beamforming | TDD Beam Measurement | TDD Beamforming Frame Type | End of Training | Reserved
Bits: | 1 | 1 | 2 | 1 | 53
Figure 13—TDD Beamforming Control field format
Group Beamforming | Beam Measurement | RA field | Beamforming procedure
0 | 0 | Unicast | Individual BF with a known peer
0 | 0 | Broadcast | Individual BF with an unknown peer
0 | 1 | Unicast | Beam measurement – Periodic Beamforming (beam refinement, calibration, …)
0 | 1 | Broadcast | Beam measurement – Intereference scan
1 | 0 | Unicast | Reserved
1 | 0 | Broadcast | Group BF with two or more peers
1 | 1 | Unicast | Reserved
1 | 1 | Broadcast | Group BF with two or more peers (per responder list); other neighboring STAs to perform beam measurement (Interference scan) under SME command

## Slide 5: MLME modifications, additions
MLME-TDD-BF-MEASUREMENT (NEW)
  Applicable to both initiator and responder sides to cover beam measurement
  Beamforming operation type (BFType argument in the primitive) expanded to
    Individual Beamforming
    Group Beamforming
    Beam measurement
      Examples: Periodic Beamforming (~Beam Refinement), Interference Measurement
MLME-TDD-BF-TRAINING
  Extended for group beamforming (vectorized arguments)

## Slide 6: References
[1] IEEE 802.11-17/1019 “mmWave Mesh Network Usage Model”
[2] IEEE 802.11-17/1321 “Features for mmW Distribution Network Use Case”
[3] IEEE 802.11-17/1679 “Beamforming protocol reuse for mmWave Distribution Networks”
[4] IEEE 802.11-18/0179 “Beamforming for mmWave Distributed Network”
[5] IEEE 802.11-18/0234 “Draft text for TDD Group Beamforming for mmWave Distributed Network”