## Slide 1: Draft agenda for IEEE 802.11 Coexistence SC meeting in Warsaw in May 2018
23 April 2018
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Welcome to the 6th F2F meeting of the Coexistence Standing Committee in Warsaw in May 2018
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
    To discuss issues related to the 3GPP RAN1 request to IEEE 802.11 WG to adopt an ED of -72dBm
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018) and will meet twice this week
    Wed PM1
    Thu PM1

## Slide 3: The first task for the Coexistence SC today is not to appoint a secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …
  … and even better, he did not need to be bribed with free beer to do the work

## Slide 4: The Coexistence SC will review the official IEEE-SA patent material for pre-PAR groups

## Slide 5: The Coexistence SC hoc will operate using accepted principles of meeting etiquette
  IEEE 802 is a world-wide professional technical organization
  Meetings shall be conducted in an orderly and professional manner in accordance with the policies and procedures governed by the organization
  Individuals shall address the “technical” content of the subject under consideration and refrain from making “personal” comments to or about others

## Slide 6: The Coexistence SC will review the modified “Participation in IEEE 802 Meetings” slide
Participation in any IEEE 802 meeting (Sponsor, Sponsor subgroup, Working Group, Working Group subgroup, etc.) is on an individual basis
  Participants in the IEEE standards development individual process shall act based on their qualifications and experience (IEEE-SA By-Laws section 5.2.1)
  IEEE 802 Working Group membership is by individual; “Working Group members shall participate in the consensus process in a manner consistent with their professional expert opinion as individuals, and not as organizational representatives”. (sub-clause 4.2.1 “Establishment”, of the IEEE 802 LMSC Working Group Policies and Procedures)
  Participants have an obligation to act and vote as an individual and not under the direction of any other individual or group. A Participant’s obligation to act and vote as an individual applies in all cases, regardless of any external commitments, agreements, contracts, or orders
  Participants shall not direct the actions or votes of any other member of an IEEE 802 Working Group or retaliate against any other member for their actions or votes within IEEE 802 Working Group meetings, (IEEE-SA By-Laws section 5.2.1.3 and the IEEE 802 LMSC Working Group Policies and Procedures, subclause 3.4.1 “Chair”, list item x)
By participating in IEEE 802 meetings, you accept these requirements. If you do not agree to these policies then you shall not participate

## Slide 7: The Coexistence SC will consider a proposed agenda
Proposed Agenda
  Bureaucratic stuff, including approving minutes
  What is happening this week? (in no particular order)
    Some history of why we are here
    Relationships
      Review ETSI BRAN meeting results
      Review recent 3GPP RAN1 activities
      Discuss possibility of a workshop with 3GPP
      Follow up on WFA’s recent LS to 3GPP RAN4
      …
    Technical issues
      Adaptivity in EN 301 893
      Blocking energy in ETSI BRAN
      “Paused COT” interpretation
      6GHz greenfield coexistence in EN 301 893
Additional agenda items are requested from all interested stakeholders

## Slide 8: The Coexistence SC will consider a proposed agenda
Proposed Agenda
    …
    Other issues
      DRS issue
      MulteFire
      Deterministic access
      …
  Other business
Additional agenda items are requested from all interested stakeholders

## Slide 9: The Coexistence SC will consider approval of the meeting minutes from Chicago
  George Calcev (Huawei) kindly took minutes for the Coexistence SC at the Chicago meeting in Mar 2018
  The minutes are available on Mentor:
    11-18-0671-00
  Are there any objections to approval of these minutes of the meeting by consent?

## Slide 10
  Some history of why we are here

## Slide 11: The agreed Coexistence SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 12: Coexistence SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 13
  Agenda items
  Review of recent ETSI BRAN meeting

## Slide 14: The Coex SC will hear reports of the ETSI BRAN meeting held in March 2018
  The last meeting of ETSI BRAN was held in March 2018
    Dates: 26-29 March 2018
    Location: Sophia Antipolis
  The Coex SC will hear a full report of the meeting particularly on issues related to:
    Adaptivity
    Blocking energy
    Paused “COT” feature interpretation
  The SC will also need to discuss the next ETSI BRAN meeting in June
    Participation by Wi-Fi stakeholders
    Potential LS’s

## Slide 15
  Agenda items
  Review of recent ETSI BRAN meeting
  Adaptivity

## Slide 16: There was lots of debate but almost consensus on the adaptivity clause in EN 301 893
Adaptivity proposal
Simulation
Technology neutrality
The adaptivity refinements to EN 301 893 were presented in BRAN(18)097004r1/5
Both IEEE 802.11 WG & WFA expressed support for the adaptivity refinements
There was some opposition (& other comments) to the adoption of the refined adaptivity proposal
Ericsson provided new simulation results supporting the use of ED = -72 dBm by systems in BRAN(18)097016r1
BRAN(18)097017 from Ericsson made a similar case
There were some differing interpretations of the Ericsson simulation results
Ericsson made a presentation focused on “technology neutrality” in BRAN(18)097032
There was a diversity of opinion in relation to the technology neutrality argument in BRAN(18)097032
After all the debate and contention …
…consensus almost broke out in relation to adaptivity!

## Slide 17: The adaptivity refinements to EN 301 893 were presented in BRAN(18)097004r1/5
  The first topic discussed in relation to EN 301 893 was the proposal by Cisco, Intel, Broadcom & HPE for a revised adaptivity clause that:
    Allows any technology to use the:
      Traditional ED/PD thresholds defined by the 802.11
      The ED-only threshold defined by various LTE based technologies
    Limits the rate of transition between these two modes of operation
  The adaptivity proposal is described in
    BRAN(18)097004r1 – .ppt description
    BRAN(18)097005 - .doc editing instructions
  There was quite a lengthy discussion after the presentation of BRAN(18)097004/5

## Slide 18: Both IEEE 802.11 WG & WFA expressed support for the adaptivity refinements
Support for adaptivity refinements
  It was noted that the IEEE 802.11 WG LS in BRAN(18)097012 expressed support for the refinements because they:
    Enhance the “technology neutrality” of EN 301 893 by making both adaptivity options accessible to all technologies
    Enable IEEE 802.11ax to use the “dual threshold option” (Option 1), thus maintaining the status quo established over many years with IEEE 802.11a/n/ac.
  At the time of the presentation the WFA representative noted that we was awaiting confirmation of WFA’s support for the IEEE 802.11 WG position
    The confirmation was received and noted towards the end of the meeting

## Slide 19: There was some opposition to the adoption of the refined adaptivity proposal
Opposition to adaptivity refinements
  An Ericsson rep indicated that his employer does not support these changes, noting this goes against agreement achieved in 2015 (and minuted)
    AFM comment: there is ongoing disagreement among various stakeholders about what was actually agreed in 2015
    AFM note: Ericsson provided material later in the meeting that supported its position (discussed later in this agenda)
  Another Ericsson rep noted wi-fi has no regulatory priority in the band
    AFM comment: this is a true statement, and indeed the proposal emphasises equal access to two mechanisms for all technologies; 3GPP simulations show that different technologies using different mechanisms are “fair”
  A Nokia rep stated he didn’t support the proposal
    AFM comment: no reason was provided

## Slide 20: Other comments were made about the adoption of the refined adaptivity proposal
Other comments on adaptivity refinements
  Ofcom suggested 802.11ax should only have to use a lower mandated ED if there was agreement from the major 802.11 chip set and/or device manufacturers:
    We should not do anything in the next version of the harmonised standard which stops the current versions of the 802.11 standards e.g. 11ac being placed on the market, if manufacturers are still promoting and producing these older standards (e.g. 802.11ac) or are still using the two threshold levels for preamble and non-preamble detection in the latest version of 802.11 standards
    If there is to be a move for one mandated level for the detection threshold in the adaptivity clause in the next version of the standard then it would have to be agreed by all of the attendees representing the major 802.11 chip set and/or device manufacturers

## Slide 21: Ericsson provided new simulation results supporting the use of ED = -72 dBm by systems in BRAN(18)097016r1
  Ericsson presented new simulation results in BRAN(18)097016r1, which are an extension of Coexistence Analysis of ED Threshold Levels – Overview of Discussion in PDED Adhoc by K. Aio et al in 11-17/348r1
    11-17/348r1 concluded that changing the ED threshold to -72dBm makes ax WLAN performance worse than both 11ac and LAA
  The Ericsson simulations in BRAN(18)097016r1used the same parameters as 11-17/348r1 but used dynamic rate selection rather than fixed rate selection
    AFM note: dynamic rate selection is arguably more realistic
  The presentation concluded that 802.11ax would be better off using an ED threshold of -72dBm because:
    If one 802.11 system uses ED of -72 dBm and the other -62dBm then both are better off than both using -62 dBm
    If both 802.11 systems use an ED of -72 dBm then both are better off than both using -62 dBm
File link

## Slide 22: BRAN(18)097017 from Ericsson made a similar case to BRAN(18)097016r1
  BRAN(18)097017 from Ericsson documented similar simulations as presented in BRAN(18)097016r1
  BRAN(18)097017 was claimed to be more realistic than 11-17/348r1 because:
    BRAN(18)097017 it used a dynamic MCS mechanism
    Whereas 11-17/348r1 used a static MCS mechanism
  BRAN(18)097017 concluded 802.11ax would not be harmed by the use of an ED of -72 dBm
    A lower ED threshold is detrimental neither in scenarios of coexistence with legacy 802.11 equipment nor with non-802.11 equipment
File link

## Slide 23: There were some differing interpretations of the Ericsson simulation results in BRAN(18)097016r1
  There was quite a lengthy discussion after the presentation of BRAN(18)0970016r1 (& 17), without consensus
  Cisco asserted that the material in BRAN(18)097016r1 (& 17) supports the adaptivity proposal in BRAN(18)0970004/5
    Suppose the simulations are incorrect; then any conclusion should be ignored and it is vital to continue to allow 802.11ax to use ED of -62 dBm
    Suppose the simulations are correct; then any rational 802.11 vendor will want to use ED of -72 dBm, even if allowed to use a higher ED, and so it is vital to allow any 802.11 system to use an ED of -72 dBm too
    Both possibilities are supported by the refinements in BRAN(18)0970004/5
  Cisco additionally asserted that it is logically flawed to conclude an ED of -72 dB is better, unless simulations are undertaken that cover all important use scenarios, rather than just a single use case
    In contrast, BRAN(18)0970004/5 supporters just need to show an important scenario is adversely affected by ED-only of -72 dB to justify the status quo

## Slide 24: There were some differing interpretations of the Ericsson simulation results in BRAN(18)097016r1
  Qualcomm commented that there is no need to say if Ericsson conclusions are right or wrong. Ericsson used a certain assumptions and conclusions were right for these assumptions. TC BRAN will need more simulations.
    AFM comment: more (independent) simulations probably are required; some real life measurements would be good too
  Qualcomm then went on to suggest that BRAN might consider ED at -62 dBm only; there were multiple objections:
    Cisco responded that this would take us back 5 years, and is contrary to the 3GPP simulations that show LAA using -62 dBm causes unfairness
    Ericsson noted that ED at -62 dBm only may potentially cause a lot of months of discussion

## Slide 25: Ericsson made a presentation focused on “technology neutrality” in BRAN(18)097032
  Ericsson built on the simulation results from BRAN(18)097016r1 in BRAN(18)097032 …
  … by asserting that the ED-only approach validated by the results are more “technology neutral”
  It particular, Ericsson noted in BRAN(18)097032 that:
    Companies are now proposing to perpetuate the exemptions for IEEE 802.11a/n/ac and to further extend the exemption to IEEE 802.11ax or proposing mandating the use of a single (existing) preamble scheme for channel coordination.
    Clearly, these proposals violate technology neutral access to unlicensed spectrum
File link

## Slide 26: There was a diversity of opinion in relation to the technology neutrality argument in BRAN(18)097032
  Wi-Fi Alliance noted the approach presented in BRAN(17)097032 is advocating for the technology neutrality, but at the same time many devices on the market now will not be compliant with the proposed approach
    Ericsson responded by saying there was no proposal to delete the provisions from the standard
    AFM comment: however there appears to be an intention to stop 802.11ax using the provisions that allow 802.11a/n/ac to use the traditional thresholds
  German Federal Ministry of Economic Affairs & Energy explained that:
    the term “technology neutral” is used by regulators as regulatory framework condition. Manufacturers with different technologies in TC BRAN have to come up with a technical solution how to comply with the “technology neutral” regulatory framework
    AFM comment: it is not entirely clear what this means in practice

## Slide 27: There was a diversity of opinion in relation to the technology neutrality argument in BRAN(18)097032
  Cisco noted allowing “dual threshold” for all technologies is more “technology neutral” than not allowing it:
    … a previous submission to BRAN in 2017 (later identified as BRAN(17)000062) had explained why allowing both the single (ED-only) and dual threshold (ED with PD) is more aligned with the definition of technology neutrality under the European regulatory framework than a rules that specify an ED-only of -72 dBm
    AFM: BRAN(17)000062 is essentially the same as 11-17-0915-00

## Slide 28: After all the debate and contention … consensus almost broke out in relation to adaptivity!
  Towards the end of the meeting, it appeared that there was going to be no agreement and little progress on adaptivity issues  … and then a potential path to consensus emerged  based on two observations:
    802.11ax using the traditional thresholds is a “market reality”
    More scientific analysis needs to be completed to understand coexistence between different technologies using different/same thresholds
  Guido Hiertz (as an individual) then suggested that 802.11ax might be allowed to use the traditional thresholds subject to
    The motivation being clearly documented as “market reality”
    Agreement that further scientific evaluations of coexistence will be undertaken and the results reflected in future revisions of EN 301 893
  The acting BRAN Chair concluded:
    BRAN will continue to discuss the issue …
    At the same time Ericsson and Cisco may want to discuss another way forward with an exception for 802.11ax to not disrupt the market …

## Slide 29: The BRAN minutes document four alternatives, noting none yet have consensus
Alt | Description | Comment
1 | ED-only at -72 With 802.11a/ac/n allowed to use ED at -62 (dual threshold) | Current status quo in current version of EN 301
2 | ED-only at -72 With 802.11a/ac/n/ax allowed to use ED at -62 (dual threshold) | To be justified as “market reality”
3 | ED at -62 dBm & PD at -82 dBm as defined in 802.11-2016 §17.3 ED-only at -72 dBm | Position supported by IEEE 802.11 WG LS
4 | ED at -62 dBm & PD at -82 dBm, with PD technology specific (ie the technology defers to its own preamble only) ED-only at -72 dBm | Concept previously discussed & rejected in Coex SC

## Slide 30
  Agenda items
  Review of recent ETSI BRAN meeting
  Adaptivity – response to BRAN(18)097016r1 & BRAN(18)097017

## Slide 31: The Coex SC may hear a presentation responding to BRAN(18)097016r1 & BRAN(18)097017
  ETSI BRAN heard results of simulations extending:
    Coexistence Analysis of ED Threshold Levels – Overview of Discussion in PDED Adhoc by K. Aio et al in 11-17/348r1
  The Coex ad hoc may hear a response from the authors of 11-17/348r1

## Slide 32
  Agenda items
  Review of recent ETSI BRAN meeting
  Adaptivity – next steps?

## Slide 33: It is proposed that the Coex SC discuss the situation related to proposed adaptivity refinements
  It is proposed that the Coex SC discuss the situation related to proposed adaptivity refinements before continuing with review of rest of the ETSI BRAN meeting …
  The Coex SC Chair will propose a way forward based on the four alternatives discussed at the end of the BRAN meeting
  Ultimately, the Coex SC may consider approving a LS to ETSI BRAN for consideration at their next meeting in June 2018
    Any voting in the Coex SC will occur Thu PM1
    Any voting in the WG will occur on Fri AM

## Slide 34: IEEE 802.11 WG could consider a LS to ESTI BRAN expressing support for Alt 3 combined with Alt 2
  A review of the four alternatives suggests Alt 3, with the conditions from Alt 2, is a good solution for all stakeholders
    Alt 1 is probably not acceptable to IEEE 802.11 WG because it is the status quo
    Alt 4 is probably not acceptable to IEEE 802.11 WG because the concept has been previously rejected
    Alt 2 is probably broadly acceptable to IEEE 802.11 WG but has some practical difficulties
    Alt 3, with the conditions imported from Alt 2, should be acceptable to all 802.11 & LTE stakeholders
  IEEE 802.11 WG could consider a LS to ESTI BRAN expressing support for Alt 3, with conditions imported from Alt 2

## Slide 35: Alt 1 is probably not acceptable to IEEE 802.11 WG because it is the status quo
  Alt. 1 is the status quo in the current version of EN 301 893
  It is assumed that the IEEE 802.11 WG does not support alt. 1 because it is directly contrary to the LS sent to ETSI BRAN in Mar 2018
  Is there any reason to discuss alt. 1 at this time?

## Slide 36: Alt 4 is probably not acceptable to IEEE 802.11 WG because the concept has been previously rejected
  Alt. 4 allows any technology to use an ED of -62 dBm as long as it also detects and defers its own preambles at -82 dBm
  The Coex SC has previously discussed rejected this concept
    It does not promote the use of a common preamble thus discouraging cross technology communications, which is a step backwards
    It effectively allows a LTE based system to ignore surrounding 802.11 systems up to -62 dBm, which 3GPP simulations suggest is adverse for fairness
    It is not supported by any simulation work or by any known specification
    …
  Is there any reason to discuss alt. 4 at this time?

## Slide 37: Alt 2 is probably broadly acceptable to IEEE 802.11 WG but has some practical difficulties
  Alt. 2 essentially extends the status quo of 802.11a/n/ac to 802.11ax
  It is conditional on:
    The motivation being documented as “market reality”
    An agreement that there should be future science based investigation of coexistence that may lead to future changes to EN 301 893
  Alt. 2 should be broadly acceptable to 802.11 stakeholders
  However, Alt. 2 does have some practical difficulties:
    It will be difficult to define the exception in the same way as previously until 802.11ax is ratified – that is too late given the market reality that pre 11ax products are about to be released
    If the Ericsson simulations are correct then it stops 802.11a/n/ac/ax equipment from transitioning as soon as possible to an ED of -72 dBm (possibly with a PD of -72 dBm too)
      The way the current text is written only equipment that has no non-802.11 modes is allowed to use the ED at -62 dBm option, otherwise it must use ED of -72 dBm

## Slide 38: Alt 3, with the conditions imported from Alt 2, should be acceptable to all 802.11 & LTE stakeholders
  Alt. 3 is the position supported by the IEEE 802.11 WG in the recent LS to ETSI BRAN
  Alt. 3 could be made closer to Alt. 2 by making it conditional on:
    The motivation being documented as “market reality”
    An agreement that there should be future science based investigation of coexistence that may lead to future changes to EN 301 893
  Alt. 3 should be acceptable to both 802.11 & LTE stakeholders
    Same as Alt 2, except it enables 802.11 to use the ED-only mode at -72 dBm in cases where it makes sense (presumably as shown by scientific evidence)
    Gives LTE based equipment freedom to use 802.11 preamble if desired (it is reported that some LAA equipment uses 802.11 preambles today)

## Slide 39: The WG will consider a LS to ESTI BRAN with support for Alt 3 with conditions imported from Alt 2
  It is proposed that IEEE 802.11 WG send a LS to ETSI BRAN supporting Alt. 3 with the conditions from Alt. 2
  The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
    See following pages
  The complete proposed LS is in 11-18-0708-00
  A possible motion for Thu PM1 is:
    The IEEE 802.11 Coex SC recommends that the material in 11-18-0708-00 be sent to ETSI BRAN, expressing support for a refinement to the adaptivity clause in EN 301 893

## Slide 40: The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
Broad outline of proposed LS
  The WG has been made aware of the discussions at the last ETSI BRAN meeting related to refinements to adaptivity in EN 301 893
    Define the four Alternatives
  The IEEE 802.11 WG does not support Alt 1, which represents the status quo in EN 301 893, and does not allow IEEE 802.11ax to use the traditional and well proven dual threshold mechanism used by IEEE 802.11a/n/ac in the 5GHz band since 1999.
  The IEEE 802.11 WG also does not support Alt 4, because it effectively allows LTE based equipment to ignore IEEE 802.11a/n/ac/ax equipment up to ED of -62dBm, which 3GPP RAN1 simulations show does not promote fair coexistence between IEEE 802.11 and LAA systems.
  …

## Slide 41: The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
Broad outline of proposed LS
  …
  It is the view of the IEEE 802.11 WG that both Alt 2 & Alt 3 have merit because they both allow IEEE 802.11ax to use the traditional dual threshold mechanism.
  Alt 2 is particularly attractive because it recognises the “market reality” that IEEE 802.11ax will specify the use of dual thresholds and documents a commitment by all stakeholders to undertake and act upon proper scientific investigation of coexistence in future revisions of EN 301 893
  …

## Slide 42: The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
Broad outline of proposed LS
  …
  However, Alt 2 has a practical difficulty in that the revised EN 301 803 can’t use the same method as the current version to reference IEEE 802.11ax
  The problem is that IEEE 802.11ax will not be ratified for a number of years and so cannot be easily referenced by an ETSI standard in the meantime.
  …

## Slide 43: The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
Broad outline of proposed LS
  …
  Alt 2 is also problematic in that it does not have the flexibility to allow IEEE 802.11 equipment to choose to use the single threshold mechanism in those situations where any future scientific investigation suggests it might makes sense
  Similarly, it does not allow non-IEEE 802.11 equipment to use the dual threshold mechanism in situations it might make sense
  …

## Slide 44: The proposed LS from IEEE 802.11 WG to ETSI BRAN supports a combination of Alt 3 & Alt 2
Broad outline of proposed LS
  …
  The 802.11 WG suggests that ETSI BRAN consider adopting Alt3, which resolves these practical difficulties, but with the addition of the motivation and understanding from Alt 2, namely that:
    Alt 3 is justified as representing the “market reality” that IEEE 802.11ax is being specified to use dual thresholds
    Alt 3 is adopted on the understanding that further scientific evaluations of coexistence will be undertaken to better inform future revisions of EN 301 893
  The 802.11 WG thanks ETSI BRAN for its efforts in ensuring that there is good balance between fair coexistence between all technologies operating in the 5GHz band and efficient use of the band
  We look forward to hearing the result of your deliberations on this matter

## Slide 45
  Agenda items
  Review of recent ETSI BRAN meeting
  Other adaptivity issues

## Slide 46: The submission refining adaptivity related to “paused COT” was not discussed by ETSI BRAN
  BRAN(18)097006/7 are submissions from Cisco, Intel, Broadcom & HPE to ETSI BRAN that were discussed at the Coex SC meeting in Chicago
  BRAN(18)097006/7 document a minor change to the adaptivity clause related to “paused COT”
    It only allows the use of ED of -72 dBm with the “paused COT” feature to maintain the status quo
  A Coex SC motion for the 802.11 WG to support these submissions failed 15/10/7, and it was not considered by the WG
  The submission were not discussed in ETSI BRAN, beyond noting them, because they were dependent on a consensus on the adaptivity proposal in BRAN(18)097004r1/5

## Slide 47
  Agenda items
  Review of recent ETSI BRAN meeting
  Paused COT interpretation

## Slide 48: There is a disagreement within ETSI BRAN on an interpretation of the “paused COT” feature
  EN 301 893 contains a feature called “paused COT” that was inserted to allow:
    An LAA eNB to send a grant to an EU
    The LAA UE to access the medium after a “pause” and 25µs of energy detection
  When it was included in EN 301 893, it was understood by many that:
    Only a single grant per UE per COT was allowed
    If energy was detected in the 25 µs period then the UE would have to wait for another grant
  3GPP took a different view of what was agreed, asserting that the LAA UE can have multiple grants
  The extrapolation of this view is a device could be issued with an infinite number of grants, which would effectively give the device access whenever there was any 25 µs period with energy less than -72 dBm

## Slide 49: The interpretation of the “paused COT” feature has been discussed previously in Coex SC & ETSI BRAN
  The pause COT interpretation issue was discussed by the Coex SC in Nov 2017
    See 11-17-1577-00
  It was subsequently discussed by ETSI BRAN in Dec 2017 without consensus
    There was no agreement
    However, it was requested that explicit text be proposed for discussion

## Slide 50: Discussion of the interpretation of the “paused COT” feature will continue in ETSI BRAN in June 2018
  At the March 2018 meeting of ETSI BRAN, Broadcom proposed explicit text in BRAN(18)097031 as follows:
    The Channel Access Engine may grant a maximum of one authorization to transmit for each Responding Device within a single COT
  There was limited discussion on the issue and no consensus
    Ericsson volunteered to work with Broadcom on an appropriate number of grants (per Responding Device?) between 1 and 10
    Broadcom suggested a rate limit of a maximum of one grant per ms per Responding Device
    Qualcomm asked to be kept in the loop
  It was decided to address the issue again at the next ETSI BRAN meeting
  AFM comment: there seems to be at least be agreement that there should be some sort of finite limit to the number of attempts

## Slide 51
  Agenda items
  Review of recent ETSI BRAN meeting
  Blocking energy

## Slide 52: IEEE 802 has a long standing concern about the use of blocking energy
  IEEE 802 has expressed concern to 3GPP RAN/RAN1 about the use of blocking energy by some implementations of LAA for a number of years
  Blocking energy is the energy transmitted in the time between when the LBT mechanism gives it access and the time it is ready to use the medium
    Also known as reservation signals
  The primary purpose of blocking energy is to stop other system gaining access to the medium in the meantime
  The concern expressed by IEEE 802 in various Liaison Statements regarding blocking energy was that it was unnecessary use of the medium and, as such, it represented inappropriate interference to other devices

## Slide 53: The discussion with 3GPP related to blocking energy ultimately went nowhere
  The position expressed by IEEE 802 to 3GPP RAN/RAN1 was that blocking energy should be limited to a level less than currently used by some LAA implementations
    Current blocking energy is used up to 0.5ms or 1ms per COT (up to ~8ms)
  3GPP RAN/RAN1 agreed that the use of blocking energy is undesirable
    They noted it is unnecessary for good performance
    They noted it is so unnecessary that the LAA spec did even not define it
  3GPP RAN/RAN1 agreed at one point to limit the need for blocking energy by defining additional starting positions to the LAA spec
    This would reduce the length of any blocking energy
  IEEE 802 agreed that this approach might be a reasonable compromise, subject to testing with real systems
  Unfortunately, 3GPP RAN1 later reneged on their commitment to define additional starting positions in LAA

## Slide 54: There was no consensus in ETSI BRAN on restricting the use of blocking energy as a compromise
  There has been a series of discussion about blocking energy in ESTI BRAN over a number of years without consensus
  In Dec 2017, Cisco made a compromise proposal that any use of blocking energy be limited to 100µs
    This would have the effect of limiting the use of blocking energy by LAA implementations to no longer than the time before the next symbol
    It recognised that some use of blocking energy is reasonable/acceptable
  There were many objections to this proposal from both Wi-Fi & LTE communities
    Some objections were self interested because of a desire not to change LAA implementations in the pipeline
      Note: it believed this is why 3GPP couldn’t agree on adding new starting positions
    Some objected on the basis it was not fair to pick on blocking energy when there were many other examples of inefficient use of the medium
      eg padding, use of low data rate, etc
      Some in Wi-Fi community were concerned some 802.11ax features might be impacted

## Slide 55: There was not consensus on the use of a new methodology being applied to blocking energy in LAA
  Before the March 2018 BRAN meeting, Cisco (Andrew Myles) facilitated an e-mail discussion on a new approach to dealing with blocking energy
  The discussion and conclusions are summarised in BRAN(18)097010, which was presented to ETSI BRAN in March 2018
    BRAN(18)097010 documented a methodology for dealing with “blindingly obvious” cases
    The BRAN(18)097010 methodology applied to blocking energy means it should be disallowed for LAA
    BRAN(18)097010 did not propose a mechanism for disallowing blocking energy for LAA
  There is still not consensus in ETSI BRAN on the question of blocking energy

## Slide 56: BRAN(18)097010 documented a methodology for dealing with “blindingly obvious” cases
Summary of BRAN(18)097010 methodology
  The general principle in Europe is that devices should not transmit unnecessarily because the transmission will often cause interference
    Based on consensus that unnecessary or transmissions whose sole purpose is preventing other devices using the spectrum are not allowed
  However, it is often difficult) to make judgements on what is an unnecessary transmission in complex systems like LAA or Wi-Fi
    ETSI BRAN does not normally have the skills to make these judgements
  That does not mean ETSI BRAN should do nothing; it has a responsibility to at least deal with the “blindingly obvious” cases
  It was proposed that “blindingly obvious” cases are those in which
    There is universal agreement it is “blindingly obvious” ; OR
    An authoritative source provided evidence it is “blindingly obvious”

## Slide 57: The BRAN(18)097010 methodology applied to blocking energy means it should be disallowed for LAA
Summary of BRAN(18)097010 methodology applied to LAA
  3GPP RAN1 is an authoritative source on LAA matters
    Particularly on the use of blocking energy (also known as reservation signals)
  3GPP RAN1 has explicitly stated in LS’s to IEEE 802.11 WG that reservation signals are unnecessary for good performance
  3GPP RAN1 has also stated blocking energy is not defined in the LAA specification
    Suggesting blocking energy is so unnecessary that it is not even defined
  There is thus a “blindingly obvious” case that blocking energy should not be allowed in the very specific case of LAA
    Note: this conclusion creates no precedent for any other situation because it depends on the existence of an authoritative source (3GPP RAN1 in this case) to judge the particular facts

## Slide 58: BRAN(18)097010 did not propose a mechanism for disallowing blocking energy for LAA
  BRAN(18)097010 concluded that:
    The use of blocking energy by some implementations of LAA …
    … represents a “blindingly obvious” example of an unnecessary transmission …
    … and so should be disallowed
  BRAN(18)097010 did not say how blocking energy should be disallowed by did float a couple of possibilities:
    Refine EN 301 893, perhaps to restricted the use of blocking energy to a maximum period of 100us, as proposed in Dec 2017
    Issue some sort of “opinion” that makes it clear the use of blocking energy, as used by some implementations of LAA, is not allowed

## Slide 59: There is still not consensus in ETSI BRAN on the question of blocking energy
Summary of discussion
  WFA rep stated he believed that the presentation showed that there might be a need for creation of an additional test
  Nokia stated they were not sure that the problem was clearly described and questioned any need for a continuation of the discussion at BRAN
  Ericsson doesn’t support this document and believes that the further discussion may delay the progress of the standard (EN 301 893)
  German Federal Ministry of Economic Affairs & Energy asked for more technical details to demonstrate the problem
    He also noted that BRAN has put significant effort into defining an LBT mechanism and asked why it is not sufficient?
      Andrew Myles responded that LBT rules actually allow a bad actor to fill the medium with noise almost continuously; LBT was not designed to stop this
  …

## Slide 60: There is still not consensus in ETSI BRAN on the question of blocking energy
Summary of discussion
  …
  OFCOM asked why the principles being proposed don’t mean that EN 301 893 should force use of higher data rates
    Andrew Myles responded, with data rates it is not always obvious what is the best rate, although all spectrum users should be encouraged to use the highest rate possible in the interests of efficient use of spectrum. In contrast, 3GPP is an authoritative source that has stated blocking energy is never required
  Qualcomm disagree on this approach and call on BRAN to concentrate on more important issues
  Conclusion
  Acting TC BRAN Chairman summarised that the discussion will be continued by email

## Slide 61: Ericsson used an access method taxonomy to justify the use of blocking energy
  There was a presentation before the blocking energy discussion that was related to blocking energy
  Ericsson provided a taxonomy of access methods in BRAN(18)0000001
    The main purpose was not to make a proposal for a change in the standard, but to bring discussion on mechanism to a technical matter (the purpose these mechanism serve)
  BRAN(18)0000001 listed various mechanisms for devices to share the medium with other devices using the same & different technologies
    At both PHY and MAC levels
  It highlighted that many PHY based synchronisation methods need to use padding of various types, ie padding can be necessary
    Pre-pending, appending or inserted into a transmission
  The implication of the presentation was that blocking energy (as a PHY synchronisation mechanism) is also justified
File link

## Slide 62: There was not consensus on the conclusions that can be drawn from the access method taxonomy
  There was limited discussion of in BRAN(18)0000001 at the time of presentation; it was discussed in more detail as part of the blocking energy discussion
  Andrew Myles asserted BRAN(18)0000001 cannot be used to justify the use of blocking energy by some implementations of LAA; he noted that:
    BRAN(18)0000001 highlighted the inclusion of a mechanism in the taxonomy does not mean it is appropriate for use
      eg PCF is in the taxonomy and yet its use is not allowed under EN 301 893 rules because it does not enable sharing
    There is agreement that many PHY sync methods are necessary, whereas even 3GPP RAN1 agrees the use of blocking energy with LAA is unnecessary

## Slide 63
  Agenda items
  Review of recent ETSI BRAN meeting
  Blocking energy – next steps?

## Slide 64: It is proposed that the Coex SC discuss the situation related to blocking energy
  It is proposed that the Coex SC discuss the situation related to blocking energy
  Ultimately, the Coex SC may consider approving a LS to ETSI BRAN for consideration at their next meeting in June 2018
    Any voting in the Coex SC will occur Thu PM1
    Any voting in the WG will occur on Fri AM

## Slide 65: The WG will consider a LS to ESTI BRAN asking they consider discouraging or limiting blocking energy
  It is proposed that IEEE 802.11 WG consider a LS to ESTI BRAN asking they consider discouraging or limiting blocking energy
  This would be consistent with IEEE 802’s previous LS’s to 3GPP RAN/RAN1 related to blocking energy
    See following pages
  The complete proposed LS is in 11-18-0706r0
  A possible motion for Thu PM1 is:
    The IEEE 802.11 Coex SC recommends that the material in 11-18-0706r0 be sent to ETSI BRAN, expressing support for discouraging or limiting the use of blocking energy

## Slide 66: The proposed LS from IEEE 802.11 WG asks ESTI BRAN to consider discouraging/limiting use of blocking energy
Broad outline of proposed LS
  IEEE 802.11 WG has been made aware of discussions in BRAN#97 related to the use of blocking energy (also known as reservation signals) by some implementations of LAA, based on BRAN(18)097010. They have been reviewed in detail in the IEEE 802.11 Coexistence Standing Committee.
  IEEE 802 has previously expressed a position to 3GPP RAN1 in various Liaison Statements,, in 2016 and 2017 that the unnecessary use of blocking energy by LAA should be both discouraged & limited in length on the basis that any unnecessary transmissions will cause interference to other systems.
  …

## Slide 67: The proposed LS from IEEE 802.11 WG asks ESTI BRAN to consider discouraging/limiting use of blocking energy
Broad outline of proposed LS
  …
  IEEE 802’s position is supported by a Liaison Statement from 3GPPP RAN1 to IEEE 802 as far back as May 2016 in which 3GPP RAN1 states that the use of reservation signals is not necessary for good LAA performance and not using reservation signals is a viable implementation option.
  In the same Liaison Statement, 3GPP RAN1 states that the LAA specification does not even define reservation signals or their use, highlighting the unnecessary nature of their use by some LAA implementations.
  …

## Slide 68: The proposed LS from IEEE 802.11 WG asks ESTI BRAN to consider discouraging/limiting use of blocking energy
Broad outline of proposed LS
  …
  In a Liaison Statement to 3GPP RAN/RAN1 in March 2017, IEEE 802 accepted a compromise proposal in a Liaison Statement from 3GPP RAN1 in November 2016 to limit the length of any blocking energy by increasing the number of starting positions in LAA
  Unfortunately, we understand that 3GPP RAN1 subsequently decided not to specify the additional starting positions for LAA, apparently because some vendors were concerned about the additional implementation complexity
  ...

## Slide 69: The proposed LS from IEEE 802.11 WG asks ESTI BRAN to consider discouraging/limiting use of blocking energy
Broad outline of proposed LS
  …
  The current situation is that some vendors’ LAA equipment will transmit up to 0.5ms of what is essentially unnecessary noise at the start of every COT for the sole purpose of blocking access to the medium to other devices
  This use of blocking energy by some LAA devices will cause interference to other devices attempting to use the medium, including IEEE 802.11 devices, and yet is not required for good performance of LAA according to 3GPP RAN1
  …

## Slide 70: The proposed LS from IEEE 802.11 WG asks ESTI BRAN to consider discouraging/limiting use of blocking energy
Broad outline of proposed LS
  …
  IEEE 802.11 WG requests that ETSI BRAN take IEEE 802’s position into account when deciding how to deal with the blocking energy issue
  In particular, IEEE 802.11 WG requests that ETSI BRAN consider the viability of various options for strongly discouraging, or even banning, the use of blocking energy by LAA devices (as well as other devices) and restricting its length in the event blocking energy is used
  The IEEE 802.11 WG looks forward to hearing the result of ETSI BRAN’s deliberations on this matter

## Slide 71
  3GPP NR-U
  6GHz greenfield

## Slide 72: The Coex SC may discuss another perspective on sharing new spectrum from LTE community
  In previous meetings the Coex SC has discussed the possibility of new coexistence mechanisms in new spectrum
    eg a new preamble at 6Ghz
  There was not much interest at the time, mainly because most in the 802.11 community want to think of 6GHz as an extension of 5GHz
    The simplest approach, aligned with status quo
  However, it appears the LTE community has different ideas
    See embedded document from Qualcomm, Nokia Corporation & Ericsson to CEPT ECC FM57
  The Coex SC will discuss alternate approaches to 6Ghz (and other new spectrum) and possible responses

## Slide 73: A submission to FM57 proposes non LBT style access in the 6GHz band
  The document to FM57 was sent in the context of new greenfiels unlicensed spectrum that 802.11 may want to use in the future
  The document asserts that NR’s flexible framework allows a shift from today’s spectrum technologies …
    eg LTE-U/LAA, LWA, MulteFire, CBRS/LSA, …
  … to new sharing paradigms
    Evolutionary, based on traditional uncoordinated sharing
    Revolutionary, based on coordinated sharing in greenfield spectrum
  The greenfield spectrum they are talking about clearly includes the planned Wi-Fi expansion spectrum in the 6GHz band
    note the information in the slides attached to this submission introducing technologies LTE-LAA and 5G-NR for operation in the license-exempt spectrum 5 925 - 6 425 MHz

## Slide 74: A submission to FM57 proposes non LBT style access in the 6GHz band

## Slide 75
  3GPP NR-U
  Status report on the most recent 3GPP RAN1 meeting

## Slide 76: The Coex SC will hear an update on coexistence relevant activities at the recent 3GPP RAN1 meeting
  3GPP RAN1 (#92-bis) was held 16 – 220 Apr 2018 in Sanya, China
  The Coex SC may hear a status update … focused on coexistence issues of course!
    This item probably depends on Shubhodeep Adhikari & Sindhu Verma obtaining visas in time
    Does anyone else have a report?

## Slide 77
  3GPP NR-U
  Simulation of coexistence

## Slide 78: The Coex SC may discuss simulation models for Wi-Fi/NR-U coexistence
  We know there were significant flaws in the simulation models used to evaluate coexistence between Wi-Fi and LAA
    IEEE 802 raised the topic in several LS’s to 3GPP RAN1
  3GPP is currently discussing simulation models that will be used to evaluate coexistence between Wi-Fi and NR-U
  Now is the time to ensure the same mistakes are not made in this round of evaluation
  The Coex SC may review recent discussions in 3GPP
    This item probably depends on Shubhodeep Adhikari & Sindhu Verma obtaining visas in time
    Does anyone else have a report?

## Slide 79
  Agenda items
  A workshop?

## Slide 80: 802.11 WG will probably need to work with 3GPP RAN1 on “fair” access in 6GHz
  It was noted in Chicago that 3GPP is treating 802.11 as an incumbent in the 5GHz band, which they have agreed to protect with a “one way definition”
    ie, the addition of an LAA systems will not cause any more loss of performance on a Wi-Fi system that the addition of a Wi-Fi system will cause
    ie, there is no expectation that Wi-Fi (with possible exception of 802.11ax) will do the same to LAA
  It was also noted that 3GPP consider 6 GHz to be greenfield spectrum and so Wi-Fi should expect no “incumbency” based protection
  This highlights the need for 3GPP RAN1 and IEEE 802.11 to engage with the goal of agreeing on how fair access between all technologies can be maintained in the 6GHz band

## Slide 81: The SC will discuss the possibility of a workshop to engage with 3GPP RAN1 on sharing of 6GHz
  In Chicago it was suggested that IEEE 802.11 WG be proactive about engaging with 3GPP on “fair” sharing mechanisms for 6GHz
  It was further suggested that IEEE 802 could invite 3GPP RAN1 to participate in a workshop on this topic
    Possibly at the IEEE 802 plenary in July 2018 (with invitation in May 2018)
  Questions:
    Is this a good idea?
    What would the agenda look like?
  We probably are not going to come to a conclusion today …
  … and so interested people are encourage to work with the Chair to put together a proposal for the May meeting

## Slide 82
  Agenda items
  Status of WFA LS to 3GPP RAN

## Slide 83: In Irvine, the SC discussed a LS from WFA to 3GPP RAN in relation to coexistence testing
  In Irvine, the IEEE 802.11 Coex SC discussed LS from WFA to 3GPP RAN that was copied to IEEE 802.11 WG
    See 11-17-1853-00
  It appeared the WFA was concerned that 3GPP RAN4 developed coexistence tests:
    Do not test all the LAA Release 14 features
    Are not being used to validate coexistence claims, as previously committed to IEEE 802 in Nov 2016 (in 3GPP R1‐1613770)
  Ultimately, the SC decide to not participate in the LS ping pong but did formally recommended to the WG that it pass a motion express support for the content of the LS
    Just in case it was useful in discussions at 3GPP RAN
  The IEEE 802.11 WG approved the recommendation

## Slide 84: The reply to the WFA confirmed 3GPP is reneging on previous validation commitments
  The IEEE 802.11 WG was not copied on the response from 3GPP RAN
  However, the response is available as 3GPP R1-1801314
  In the reply, 3GPP RAN:
    Confirmed that they do not plan to use the RAN4 tests to validate LAA coexistence
    Informed WFA there is no Study Item to extend the tests for Rel-14 updates to LAA
    Informed WFA there is no current Work Item to define pass/fail criteria for the RAN4 tests
  The reply is as one might expect and essentially confirms that 3GPP RAN is reneging on previous commitments to IEEE 802 in relation to coexistence testing
  One possible reasonable conclusion is that future commitments from 3GPP RAN should be taken with a “grain of salt”

## Slide 85: The Coex SC will review the most recent LS from WFA to 3GPP RAN4
  See Draft WFA LS to 3GPP_2018_03_19.docx
    A open link needs to be found

## Slide 86
  Agenda items
  A possible coexistence issue with DRS?

## Slide 87: Does DRS cause a coexistence issue?
  DRS in LAA is roughly equivalent to a Beacon in Wi-Fi
  More details of the use DRS by LAA systems recently became available, which demonstrated some differences - see following page
  Specific known differences include:
    DRS accesses the medium using PIFS … whereas Beacon uses normal broadcast LBT
      Note: this is allowed in EN 301 893 for a certain proportion of the traffic for historical reasons
    DRS explicitly blocks Wi-Fi in 6 of 12 symbols (each symbol is ~71 us) … whereas Wi-Fi just has bloated Beacons
  The WFA has noted to various regulators (including Singapore) that the effect of DRS style access on fair and efficient use of the medium has never been evaluated
  Does anyone have any concerns?

## Slide 88: LAA’s DRS uses PIFS access and explicitly sends dummy signals to block Wi-Fi

## Slide 89
  Agenda items
  MulteFire

## Slide 90: Does anyone think we should look at MulteFire coexistence?
  The DRS topic has also been raised wrt MulteFire
  So far most of IEEE 802’s coexistence focus (after initially looking at LTE-U) has been on LAA
  There might be some future focus on NR-U
  But what about MulteFire?
    Is there no concern?
    Or a lack of visibility?
    Or is it immaterial in the market?
    …
  Does anyone think we should look at MulteFire coexistence?
    … and does anyone want to volunteer?

## Slide 91
  Agenda items
  Next ETSI BRAN meeting

## Slide 92: The next ETSI BRAN meeting is being held in late June 2018
  Dates
    18-21 June 2018
  Location
    Sophia-Antipolis
    Call in possible
  Attendees
    ETSI members, including
      WFA, Cisco, Qualcomm, Ericsson, Nokia, …
  Agenda
    Not yet issued but it will include issues related to revision of EN 3091 893
      Adaptivity
      Blocking energy
      Interpretation of “Paused COT”
      …

## Slide 93
  Agenda items
  Motions

## Slide 94: The Coex SC will consider any motions on Thu PM1
  Any motions will be considered on Thu PM1
  Possible motions include:
    …

## Slide 95
  Agenda items
  Plans for next meeting

## Slide 96: The Coex SC will discuss plans for the next session in San Diego
  Possible items include
    Review of ETSI BRAN meeting
      BRAN#98
    Review of 3GPP RAN1 activities
      Focus on NR-U
    … <other suggestions?>

## Slide 97: The IEEE 802.11 Coexistence SC meeting in Warsaw in May 2018 is adjourned!