## Slide 1: Clarification on TXSS Sector List Feedback
Date: 2018-04-25
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Hiroyuki Motozuka | Panasonic Corporation |  |  | 

## Slide 2: Introduction
Initiator
Responder(s)
SISO, SU-MIMO or MU-MIMO BF training
TXSS sector list feedback
Initiator/Responder TXSS
Common flow for SISO, SU-MIMO and MU-MIMO BF:
  Assumptions:
    the SISO phase of SU-MIMO or MU-MIMO BF does not comprise TXSS subphase.
    SISO BF is based on BRP phase (e.g., BRP setup, BRP transaction)
  TXSS sector list feedback is mainly used for sector down-selection purpose

## Slide 3: TXSS Sector List Feedback for SISO BF
BRP
BRP
Initiator
Responder
Feedback for initiator link is contained in EDMG Channel Measurement element & Channel Measurement Feedback element:
  If the number of the received sectors is less than 16, all received sectors shall be feedback. Otherwise at least 16 received sectors shall be feedback.
Optional feedback request for responder link
BRP
If requested, feedback for responder link is included in EDMG Channel Measurement element & Channel Measurement Feedback element:
  If the number of the received sectors is less than 16, all received sectors shall be feedback. Otherwise at least 16 received sectors shall be feedback.
Feedback request for initiator link

## Slide 4: TXSS Sector List Feedback for SU-MIMO BF
BRP
BRP
Initiator
Responder
Feedback for initiator link is included in EDMG Channel Measurement element & Channel Measurement Feedback element:
  If the number of the received sectors for a pair of TX/RX antennas is less than 16, all received sectors for the pair of TX/RX antennas shall be feedback. Otherwise at least 16 received sectors for the pair of TX/RX antennas shall be feedback.
Feedback for responder link is included in EDMG Channel Measurement element & Channel Measurement Feedback element:
  If the number of the received sectors for a pair of TX/RX antennas is less than 16, all received sectors for the pair of TX/RX antennas shall be feedback. Otherwise at least 16 received sectors for the pair of TX/RX antennas shall be feedback.
Feedback request for initiator link

## Slide 5: TXSS Sector List Feedback for MU-MIMO BF
BRP
BRP
Initiator
Any responder in MU group
EDMG Channel Measurement element & Channel Measurement Feedback element:
  If the number of the received sectors for a pair of TX/RX antennas is less than 16, all received sectors for the pair of TX/RX antennas shall be feedback. Otherwise at least 16 received sectors for the pair of TX/RX antennas shall be feedback.
EDMG BRP Request element:
  the L-TX-RX and Requested EDMG TRN-Unit M fields indicate the number of TRN subfields requested for receive AWV training in the following non-reciprocal MU-MIMO BF training
Feedback request for initiator link

## Slide 6: Problem Statement
  When receiving a BRP frame soliciting TXSS sector list feedback for initiator link, the responder may not know how to provide enough feedback information for the following BF training since it has no idea about the following BF training is for SISO, SU-MIMO or MU-MIMO BF training.
    Notice that the content of TXSS sector list feedback varies depending on what type of BF training will be performed.

## Slide 7: Proposal
  Add a 2-bit field called BF Training Type into the DMG Beam Refinement element to indicate whether the following BF training is SISO, SU-MIMO or MU-MIMO BF training.
    0: SISO BF training
    1: SU-MIMO BF training
    2: MU-MIMO BF training
    3: reserved
  The spec text proposal is provided in 18/0681r0.

## Slide 8: Reference
  Draft P802.11ay_D1.1