## Slide 1: 802.11REVmd LB232 Multi-BSS CIDs
Date: 2018-April
Authors:

## Slide 2: Summary of Comments
The comments are classified into the following broad categories:
  Spec clarification in 11.1.3.8
    1289, 1290, 1291, 1292, 1296, 1295, 1297  to be discussed by TGax
  Insufficient information from a multi-BSS AP
    CIDs 1293 & 1294  proposed resolution in doc 11-18/0675r0
  Conditional inheritance
    CID 1298  proposed resolution in doc 11-18/0675r0
  Editorial/Typo in 9.4.2.21.10
    CID 1299  resolved in this presentation
  MAC Address representation
    CIDs 1287, 1288, 1300  needs discussion

## Slide 3
(1) Spec Clarification

## Slide 4: (1) Spec Clarification
Support for multiple BSSID feature is mandatory for a non-AP HE STAs.
  Therefore, TGax is looking into fixing some of the inconsistencies in the spec.
  The resolutions are expected to address the comments in this category
Requesting REVmd to defer the discussion on these CIDs until after the May meeting
  REVmd can either close or discuss any CIDs not addressed by TGax
A slide summarizing the direction that TGax is anticipated to follow is provided in the appendix section.

## Slide 5
(2) Insufficient information from a multi-BSS AP

## Slide 6: (2) Insufficient information from a multi-BSS AP
MaxBSSID Indicator (9.4.2.45) indicates the maximum (2n) possible BSSIDs that can be hosted on the device
  There is no indication of what is the actual count of ‘active’ BSSIDs
Further, 11.1.3.8 permits an AP to advertise a partial list of nontransmitted BSSID profiles (in the Multiple BSSID element) without any indication of whether the list if complete or partial.
  A non-AP STA has no way to know if it has received information about all the BSSIDs in the set.
  STA may end-up scanning several beacons and still not be sure.

## Slide 7: Resolution Summary
Add a bit to Extended Capabilities element so that an AP can indicate if the list is complete.
Define a new element which an AP can advertise in its mgmt. frames to indicate the count of active BSSIDs in the set.
With the above two pieces of information, a non-AP STA can determine if it has received information about all the active nontransmitted BSSIDs on the device.

## Slide 8: Proposed resolution for CID 1293 & 1294
Review doc 11-18/0675r0

## Slide 9
(3) Conditional Inheritance

## Slide 10: (3) Conditional Inheritance
Background: Per spec:
  If an element X is advertised in the mgmt. frame transmitted by the TxBSSID and not present in the nonTxBSSID profile, then a STA associated with that nonTxBSSID shall use (inherit) the values of the element X as advertised by the TxBSSID.
  If a nonTxBSSID wants to have a different value for element X, it can advertise element X in its nonTxBSSID profile with a different set of values.
For example,
  TxBSSID advertises TWT service periods every 20ms by advertising the appropriate parameter set in TWT element
  nonTxBSSID (with say BSSID index 1) sets up a TWT service period with different periodicity (say 30ms) by advertising its own TWT element in the corresponding nonTxBSSID profile.

## Slide 11: (3) Conditional Inheritance
Problem
  The spec doesn’t allow a nonTxBSSID from not inheriting an element advertised by the TxBSSID
For example,
  nonTxBSSID (with say BSSID index 2) doesn’t want to set-up or support TWT  spec doesn’t provide a mechanism
  STAs associated with BSSID-2 will expect inheritance from TxBSSID (i.e., TWT SPs every 20ms)  leads to unexpected behavior

## Slide 12: Resolution Summary
If a nonTxBSSID doesn’t want to inherit element X, it advertise element X in its nonTxBSSID profile with the Information field missing.
  Element ID, Length and Element ID Extension are the only fields present.
  Length field set to 0 or 1 depending on whether the element carries Element ID Extension field.

## Slide 13: Proposed resolution for CID 1298
Review doc 11-18/0675r0

## Slide 14
(4) Editorial/Typo in 9.4.2.21.10

## Slide 15: (4) Editorial/Typo in 9.4.2.21.10
The description for Co-Located BSSID List subfield (in section 9.4.2.21.10) makes reference to MaxBSSID Indicator field which is present in Multiple BSSID element (9.4.2.45).
However, the section reference points to 9.4.2.25 which corresponds to Vendor Specific element.

## Slide 16: Proposed resolution for CID 1299
TGm Editor please make the following changes to the 3rd paragraph below Figure 9-248 (REVmd D1.0, P996L27):
The MaxBSSID Indicator field is as defined in 9.4.2.45 (Multiple BSSID element) 9.4.2.25 (Vendor Specific element). When set to a nonzero value, it indicates the maximum possible number of BSSs, including the reference BSS, which share the same antenna connector and have the same 48-(MaxBSSID indicator field) MSBs of the BSSIDs. When the BSSIDs of the co-located BSSs are configured at the reporting STA but not represented by the MaxMBSSID Indicator field, the BSSID fields are present in the Co-located BSSID List subelement to provide an explicit list of such BSSID values.

## Slide 17
(5) MAC Address representation

## Slide 18: (5) MAC Address representation
Background
  REVmd section 9.2.2 (P725L57): MAC addresses are assigned as ordered sequences of bits. The Individual/Group bit is always transferred first and is bit 0 of the first octet.
  The above description seems to be consistent with the MAC address definition in clause 8 of 802-2014 spec (see pg 24 Fig. 10)

## Slide 19: (5) MAC Address representation
Issue 1: Several instances in the spec where I/G bit is referred to as the MSB bit
  9.4.2.25 (P857L34): B63 contains the LSB of the group address (considering the Individual/Group bit to be the most significant bit (MSB)).
  9.4.2.104 (P1183L1): When a mesh peering is not established with this neighbor STA, the MSB of this field is set to 1, and the rest of this field is set to the last 7 digits (7 LSBs, taking the I/G bit as the MSB) of the 48-bit MAC address of this neighbor STA.
  14.13.2.4.5 (P2612L1): When the Beacon Timing element is received from a nonpeer mesh STA, the mesh STA checks if the MSB of the Neighbor STA ID subfield is set to 1 and the rest of the field matches with the 7 LSBs of its own MAC address (taking the I/G bit as the MSB).

## Slide 20: (5) MAC Address representation
Issue 2: BSSIDs of a multi-BSS (or co-located BSSID) set differing by n-LSB
  Per 9.4.2.45 (Multiple BSSID element), the BSSID(i) in a multiple BSSID set would have the n-LSB bits changing  this would mean the I/G bit is being affected, which is not the intention.
  Same comment applies to the description of Co-Located BSSID List subelement (9.4.2.21.10 – P996)

## Slide 21: (5) MAC Address representation
Issue 3: Integer operation on bit fields of the MAC address
  BSSID_B is a BSSID with (48–n) MSBs equal to 0 and n LSBs equal to [(n LSBs of REF_BSSID) +i] mod 2n

## Slide 22: Discussion (issue #1)
For resolving issue #1, group needs to agree on whether bit 0 of the MAC address / BSSID should be called as MSB or LSB
Also, suggest refrain from describing the address bits as LSB or MSB but instead in terms of their bit position as it is done in section 10.21 – see Tables 10-13 & 10-14 and the note below the tables.
REVmd D1.0 pg 1661

## Slide 23: Discussion (issue #2)
Once the group comes to a suitable resolution for issue #1, the text in 9.4.2.45 & 9.4.2.21.10 can be updated to fix the LSB/MSB references

## Slide 24: Discussion (issue #3)
Assuming the address bits are represented in terms of their bit positions, issue #3 could be addressed as follows:
  In 9.4.2.45, remove BSSID_A and BSSID_B and instead have a single equation as follows:
BSSID(i) = (REF_BSSID & ZERO_BSSID[(48-n):47]) |
(ZERO_BSSID[0:47] & Int2Binn([Bin2Int(REF_BSSID[(48-n):47])+i] mod 2n))
where
  ZERO_BSSID[b:c] represents bits b to c inclusive of a 48-bit address set to 0
  REF_BSSID[b:c] represents bits b to c inclusive of the REF_BSSID address
  Bin2Int(x) represents an integer value of a sequence of bits [b:c]
  Int2Binn(x) represents a n-bit binary value of an integer x
In the above operation, the spec could add clarification on how bits in the BSSIDs are converted to a sequence of bits.
  As an example, please see 802.11-2016 spec section 10.20 (pg 1374) under Table 10-9, i.e. “ZERO_BSSID[b:c] and REF_BSSID[b:c] represent bits b to c inclusive of the ZERO_BSSID and REF_BSSID respectively, with bit 0 being the Individual/Group bit and bit 47 being the last transmitted bit, in which bit position b is then scaled by 20 and c by 2c−b.
An alternative could be to define a term which represents such conversion and reference it here.

## Slide 25: Appendix

## Slide 26: Spec Clarification in 11.1.3.8
Define mandatory elements (CID 1295)
  Clarify which elements are required to be present in each nonTxBSSID
Clarify the inheritance model (CID 1289, 1290)
  A nonTxBSSID is not required to advertise all elements instead it inherits elements advertised by TxBSSID if they are not present in the nonTxBSSID profile for that BSS
    This also helps reduce the size of nonTxBSSID profile
Disallow advertising partial profile (CID 1291, 1292, 1296)
  If a nonTxBSSID profile is present in the mgmt. frame, it will include all the element specific to that BSS
General Spec clean-up (CID 1297)
  Remove extraneous or declarative sentences.