## Slide 1: Discussion on the Multi-band Discovery Assistance Proposal
Date: 2018-04-25
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4027 | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4405 | kazuyuki.sakoda(at)sony.com

## Slide 2: Expected Latency Due to BHI (1)
TXTIME(µs) = TL-STF+ TL-CE+ ((Length +LL-Header)x 8 + NCW x 168) x 32/1.76e3 + TTRN
LL-Header=5 Octets
BHI
Frame Spacing | Time (µs)
MBIFS ( between BTI and ABFT) | 9
LBIF ( when switching DMG antennas) | 2
SBIF ( between sweeping frames) | 1
 | Length (octets) | TX Time (µs)
SSW Frame | 26 | 14.91
SSW FB Frame | 28 | 18.25
Beacon Frame no TRN | 72 | 30.76
Beacon Frame with 31 TRN | 72 | 118.69

## Slide 3: Expected Latency Due to BHI (2)
 | Beacons/BI | No of SSW slots | SSW frames/ slot | No of DMG Antennas | No of beacon TRNs
Option 1 | 1 | 2 | 8 | 1 | 0
Option 2 | 8 | 4 | 16 | 1 | 0
Option 3 | Full beacon sweep | 9 | 16 | 1 | 0
Option 4 | Full beacon sweep | 9 | 16 | 2 | 0
Option 5 | Full beacon sweep | 9 | 16 | 2 | 16
Option 6 | Full beacon sweep | 9 | 16 | 2 | 31
Option 7 | Full beacon sweep | 36 | 16 | 2 | 31

## Slide 4: Proposed Solution in March Meeting [1] Option 1
New STA receives a beacon on sub-6GHz from a multi-band STA indicating mmW band support and discovery assistance support (beacon has the multi-band element with added 1-bit to indicated discovery assistance support)
New STA authenticates/associates to the STA on the sub-6GHz
New STA sends Discovery Assistance Request action frame (new frame) with Discovery Assistance Request element on the sub 6GHz to STA
The Discovery Assistance Request element when used in the Discovery Assistance Request action frame has the following information:
  (New node DMG capability, New node SAT address, New node requested scanning mode )
STA responds with Discovery Assistance Response and attach the Discovery Assistance Response element
The Discovery Assistance Response element when used in the Discovery Assistance Response frame has the following
  (Discovery assistance response ( accept, reject,..) , Discovery assistance window length, New node dwelling time ( used for TDD mode scanning, New node scanning mode )
New STA and STA start the discovery procedure

## Slide 5: Updated Proposed Solution Option 2
New STA receives a beacon on sub-6GHz from a multi-band STA indicating mmW band support and discovery assistance support (beacon has the multi-band element with added 1-bit to indicated discovery assistance support)
New STA authenticates/associates to the STA on the sub-6GHz
New STA sends FST Request action frame with Discovery Assistance Request element on the sub 6GHz to STA- frame is used for triggering discovery only
The Discovery assistance Request element when used in the FST request has the following information:
  (New node DMG capability, New node SAT address, New node requested scanning mode )
STA responds with FST response and attach the Discovery Assistance Response element to it
The Discovery Assistance Response element when used in the FST response has the following
  (,Discovery assistance window length, New node dwelling time ( used for TDD mode scanning, New node scanning mode )
New STA and STA start the discovery procedure

## Slide 6: Updated Proposed Solution Option 3
New STA receives a beacon on sub-6GHz from a multi-band STA indicating mmW band support and discovery assistance support ( beacon has the multi-band element with added bit to indicated discovery assistance support)
New STA associates/authenticates to the STA on the sub-6GHz
New STA sends OCT Request action frame with an Information Request action frame attached to it
The Information Request action frame includes the Discovery Assistance Request element
The Discovery Assistance Request element when used in the information request action frame has the following information:
  (New node DMG capability, New node SAT address, New node requested scanning mode )
STA responds with OCT Response action frame and attach the Information Response action frame to it
The Information Response action frame includes Discovery Assistance Response element
The Discovery Assistance Response element when used in the Information Response has the following
  (Discovery assistance response ( accept, reject,..) , Discovery assistance window length, New node dwelling time ( used for TDD mode scanning, New node scanning mode )
New STA and STA start the discovery procedure

## Slide 7: Standard Requirements for Each Option
All options require the following:
  Adding 1-bit to the multi-band element to indicate discovery assistance feature
  2 new elements (Discovery Assistance Request and Discovery Assistance Response elements)
Option 1:
  Define 2 new action frames, Discovery Assistance Request and Discovery Assistance Response action frames to carry the newly defined Discovery Assistance elements
Option 2:
  Enable FST Request and FST Response action frames to carry the newly defined Discovery Assistance elements
Option 3:
  Enable Information Request and Information Response action frames to carry the newly defined Discovery Assistance elements

## Slide 8: mmW Discovery Assistance
Option 1 and Option 3 allow mmW Discovery Assistance- no standard action needed
STAs in the mmW ESS or Distribution Network trigger other STAs to enable discovery for the new STA
Allowing the Information Req/Resp or the Discovery Assistance Req/Resp action frames to carry the Discovery Assistance elements enables other nodes in the ESS or Distribution Network to trigger discovery for the new node
  New node ( STA 1) discovers one STA ( STA 2) through multi-band signal (Option 1, 2 or 3)
  Discovered STA (STA 2) sends Information Req or Discovery Assistance Req with Discovery Assistance Request element to nearby mmW enabled STA ( STAs already connected to, STA 3) to trigger discovery for the new STA
  Other STAs ( STA 3) respond with Information Resp or Discovery Assistance Resp with Discovery Assistance Response element to the discovered STA (STA 2) and start the discovery protocol if Discovery Assistance request is accepted
  The request can propagate through the network ( STA3 to STA 4)
STA 2
STA 3
STA 1
Multi-band Discovery Assistance (Option 1, 2 or 3)
STA 4

## Slide 9
Option 1 (Mar 18) |  | Option 2 (FST) |  | Option 3 (OCT) | 
Pros | Cons | Pros | Cons | Pros | Cons
Cleaner Frames can be sent on mmW band and Sub-6GHz band (Work for Multi-band Discovery Assistance and mmW Discovery Assistance ) | 2 new action frames need to be defined Need to define state machine for the transaction of theses frames | Reuse existing state machines Less changes in the specs compared to Option 1 | Introducing DMG specific features as part of a generic MB operation frame Using the FST outside its intended use case Would work with Multi-band Discovery Assistance only | Reuse existing state machines Less changes in the specs compared to Option 1 Work for Multi-band Discovery Assistance and mmW Discovery Assistance | Add new flavor to the Information Request and Information Response frames

## Slide 10: Wi-Fi Agile Multi-band
Facilitates better management of Wi-Fi networks changing conditions and improved resource utilization
Uses several mechanisms
  Dynamic network monitoring: APs and client devices continually exchange information about the current Wi-Fi network environment
  Intelligent steering: APs suggest another AP, frequency band, or channel to client devices when the Wi-Fi environment becomes congested
  Fast network transitions: Once a client device decides to roam to a different AP, band, or channel, the association and connection happen quickly and seamlessly
WiFi Agile Multi-band does not consider network discovery and beacon/BF sweeping issues, it only exchanges information of prioritized available networks

## Slide 11: References
[1] IEEE 802.11-18/486r0, “Multi-band Discovery Assistance”, Mohamed Abouelseoud, et.al.