## Slide 1: Efficient FDMA transmission for WUR
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
May 2018

## Slide 2: Introduction
The concept of FDMA scheme for WUR transmission[2] was decided in last f2f meeting.
  As described in SFD[1], the wake-up signal can be transmitted by using the only one 4MHz in each 20MHz channel.
  FDMA transmission of wake-up signal is used for multiple users.
For the supporting of the various multiple users that have a different condition, we can consider the transmission of WUR PPDU applied the different data rates per 20MHz channel.
And, it can occur some problem when wake-up signal is transmitted by using the FDMA due to misalignment of PPDU length per 20MHz channel.
So, In this contribution, we investigate the misalignment of PPDU length in FDMA transmission and consider the efficient method for using the WUR FDMA transmission in a wide bandwidth.

## Slide 3: MU wake-up transmission with FDMA
In FDMA transmission, on the contrary of non-WUR portion, WUR portion per each 20MHz can have a different length.
  According to data rate and length of frame body, WUR PPDU can has a various length.
    Two data rates ( i.e. 62.5kbps and 250kbps) are used for WUR data portion and according to data rates, the length of WUR preamble is also different.
    In [1], for the frame body, three length is considered
      Octets for frame body : 0/ 8 /16

## Slide 4: Early end of WUR transmission
In FDMA transmission, the different length of WUR PPDU per channel can occur the following issues.
  It can lead the unnecessary UL transmission from the other PCR STA in BSS.
    If length of WUR PPDU transmitted on the primary channel is shorter than that of WUR PPDU on the secondary channel, after end of WUR transmission on the primary channel, PCR STA can transmit the signal by using this channel while AP transmits the WUR signals to other STA. so, AP cannot receive the signal from the PCR STA.
    It can also occur the unnecessary power consumption of PCR STA.
So, we need to consider the method to adjust the transmission time on the primary channel as much as that max duration of transmission in FDMA.

## Slide 5: Length Difference of WUR PPDU
Length of WUR PPDU according to data rate and length of FB.
  Regardless of the frame body, when HDR has applied on the WUR PPDU, the length of PPDU is shorter than that of case 1.
  As shown in above figure, the differences between two PPUDs can be larger than 1 ms.
  So, It can occur the worthless transmission on the primary channel while AP transmits signal. Because it can be recognized as a idle channel to other STAs in BSS.
Case | Data rate | Length of FB (byte)
1 | LDR | 0
2 | HDR | 0
3 | LDR | 8
4 | HDR | 8
5 | LDR | 16
6 | HDR | 16
Chart: length of WUR PPDU
 | 920 | 280 | 1944 | 536 | 2968 | 792

## Slide 6: TXOP guarantee on primary channel
As shown in slide 5, the difference between two PPDUs is not minor.
So, we should fill the difference of PPDU length at the primary channel for prohibiting of unintended transmission while AP transmits the Wake-up signal.
For the this, we can consider the following options
  Option 1 : adjustment of data rate
    The PPDU applied the LDR has the longer preamble length and symbol duration than that applied the HDR.
      In previous slide, we checked that case 1 is longer than other cases that are applied the HDR.
    So, by applying the LDR to WUR PPDU on the Primary channel, we can meet the Max length of WUR PPDU on transmission of same frame type.

## Slide 7: TXOP guarantee on primary channel
  Option2 : Adding the additional WUR frame until the max length of WUR PPDU .
    For the alignment of primary PPDU length as to max PPDU length among the each channel, additional frame may be added after WUR frame.
    Because additional WUR frame is attached in WUR PPDU, a wake-up receiver may try to decode all frames transmitted on the primary channel.
      It can lead the more power consumption.
    The configuration of additional WUR frame is TBD

## Slide 8: TXOP guarantee on primary channel
  Option 3 : Adding the padding as much as the difference
    It is very simple but may not be efficient because this length of padding can be very long according to cases.
    Since WUR Rx can sense the signal power due to padding symbol after the end of WUR PPDU, other WUR RXs may be try to decode this.
      It can lead the unnecessary power consumption of WUR RXs.
    How to construct the padding symbol is TBD.

## Slide 9: Conclusion
The length of WUR PPDU per 20Mhz can be different in the WUR FDMA transmission.
  The difference in length is not trivial.
  And, the early end of transmission on the primary channel can lead the unnecessary channel access and transmission at the primary channel.
Thus, to solve this problem, we should align the length of PPDU on the primary channel with that of other channels in WUR FDMA.
Also, as to align the length of PPDU on primary channel as much as the max length of other channels in WUR FDMA transmission, we can consider the three options.
  Op1 : applying the low data rate on the primary channel
  Op2 : adding the additional WUR frame.
  Op3 : adding the Padding symbol.
The method

## Slide 10: Straw Poll #1
Do you agree that transmission on the primary channel is equal to or longer than transmissions on other channels in WUR FDMA?
  Y
  N
  A

## Slide 11: Straw Poll #2
Which option do you prefer for alignment of a length of WUR PPDU transmitted on the primary channel with other channels if the length of WUR PPDU on the primary channel is shorter than that of other channels in FDMA transmission?
  Option 1:
  Option 2:
  Option 3:

## Slide 12: Reference
[1] IEEE 802.11-17/0575r9 Specification Framework for TGba
[2] IEEE 802.11-17/1625r6 Efficient FDMA MU Transmission Schemes for WUR WLAN

## Slide 13: Appendix

## Slide 14: Recap. FDMA transmission [2]
Each 20MHz only contain one 4MHz sub-channel for wake-up signal transmission.
Similar to 11ax’s 20MHz only operation, one wake-up receiver can stay in one of the sub-channel in wide bandwidth.