## Slide 1: 11az Negotiation Protocol Update (overview)
Date: 2018-07-09
Authors:

## Slide 2: Motivation/Background
Submission 17-1473r2 discussed 802.11az Negotiation Protocol and had several aspects designated as <TBD>
Proposals discussing details of the Ranging Protocols have resulted in further refinements to the 802.11az Negotiation Protocol
In this presentation, we summarize the developments since the last discussion and provide an update to the 802.11az Negotiation protocol.
The companion submission document 18/788 has the corresponding amendment text

## Slide 3: 802.11-2016 FTM
IEEE802.11-2016 Fine Timing Measurement protocol is supported over 2.4/5/60 GHz bands
The Fine Timing Measurement Parameters element includes fields to describe parameters relevant to FTM ranging over 60 GHz band
  Additional parameters resulting from 802.11az ranging over 60GHz band could be added by extending the FTM Parameters element
    Table 9-77 shows FTM Parameters element as extensible (change this to subelements)
Extend FTM Parameters element with DMGz/EDMGz Specific Parameters as needed using Optional subelements

## Slide 4: Rename NGP Parameters Element
NGP was a place holder name. A more apt name that is allowed in the IEEE802.11az amendment is needed
Proposed Name: Ranging Parameters – already applied to some parts Draft 0.3.

## Slide 5: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | Ranging Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11* | variable
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer | 
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16 | 
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period | Optional subelements
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16 | variable
* To be extended from the description in IEEE802.11-2016 to include new fields required to support DMGz/EDMGz ranging protocols
Element Id
Length

## Slide 6: Optional subelements in FTM Parameters element
Subelement ID* | Name | Extensible
0 | DMG Direction Measurement Parameters | Yes
1 | EDMG Direction Measurement Parameters | Yes
2-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
* Submission 18-1274 adds more optional subelements to this list. Subelement ID assignment may change as a result

## Slide 7: Ranging Parameters Element (in IFTMR)
 | Element ID (255) | Length | Element ID Extension | Ranging Parameters | Ranging subelements
Octets | 1 | 1 | 1 | 3 | <tbd>
 | Reserved | Reserved | Secure LTF Required | Secure LTF Supported | ISTA2RSTA LMR Feedback | Format and Bandwidth | Number of Antennas
Bits | 2 | 5 | 1 | 1 | 1 | 6 | 8

## Slide 8: Ranging Parameters Element (in IFTM)
 | Element ID (255) | Length | Element ID Extension | Ranging Parameters | Ranging subelements
Octets | 1 | 1 | 1 | 3 | <tbd>
 | Status | Value | Secure LTF Required | Secure LTF Supported | ISTA2RSTA LMR Feedback | Format and Bandwidth | Number of Antennas
Bits | 2 | 5 | 1 | 1 | 1 | 6 | 8

## Slide 9: Ranging subelements in the Ranging Parameters element
Subelement ID | Name | Extensible
0 | VHTz-specific subelement | Yes
1 | HEz-specific subelement | Yes
2-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 

## Slide 10: Status field
IEEE802.11-2016 specifies the Status field with a value of 1 to indicate “Successful (some requested parameters might have been overridden). Measurement exchanges are about to begin”

## Slide 11: VHTz Specific subelement
Fields included in IFTMR
  None
Fields included in the IFTM frame
  MinToABetweenMeasurements (expressed in units of 100us)
    Minimum time between measurements
    Same as MinToaReady if MinToaReady != 0
  MinToaReady (expressed in units of 100us)
    the results (ToA/ToD) are available after MinToaReady and can be obtained by initiating a ranging exchange after MinToaReady
    If IFTMR included a Ranging Period value, then Ranging Period shall be greater than MinToaReady; otherwise the negotiation fails
  MaxToaAvailableExp
    If the next ranging exchange is initiated before the expiry of MaxToaAvailableExp, the measurements (ToA/ToD) from the last ranging exchange are delivered in the Location Measurement Report (LMR)
    If the next ranging exchange is not initiated before the expiry of MaxToaAvaialableExp, the session terminates

## Slide 12: HEz Specific Subelement
Fields included in IFTMR frames
  Bit map of ISTA’s Availability/Unavailability in units of 10msec intervals for a 3-second period
Fields included in IFTM frame when Status is Successful:
  Ranging ID
    Ranging ID assigned to the initiator (463r1) – only to unassociated STA; Associated STAs use AID instead of Ranging ID.
  Response: Immediate or Delayed
  MaxToAAvailableExp
  BSS Color*
  Ranging Window
    Ranging Window assigned to the ISTA for executing the HEz Ranging exchange
Fields included in IFTM frame when Status is not Successful:
  RSTA’s Availability Window for Ranging IE – needs discussion
* Note that IFTMR/IFTM are public access frames and hence are not colored

## Slide 13: .11az Negotiation
Performed with one of more discovered Responders
Initial FTM Request contains:
  Trigger
  [FTM, Ranging Parameters element contain proposed parameters to execute FTM, VHTz, HEz Ranging protocols
  Location Civic and/or LCI Request elements
Initial FTM frame contains
  Responder’s LCI, location civic if IFTMR included corresponding request elements
  A Neighbor List if IFTMR included a Neighbor Report Request element
  One of FTM or Ranging Parameters to execute the Ranging protocol chosen by the responder
    The Ranging Parameters element, if present, includes either the VHTz-Specific or HEz-Specific parameters subelement

## Slide 14: How does all this work? -- an example
STA discovers ranging capability of the environment
  STA listens to Beacons from a set of Responders
  STA selects a subset based on the ranging capabilities supported by each of the Responders
STA initiates Negotiation with one or more of the discovered responders
STA executes the negotiated Ranging protocol with one or more of the responders with which it successfully completed the negotiation
NGPv refers to Ranging Parameters element with a VHTz-Specific sub-element
NGPh refers to Ranging Parameters element with a HEz-Specific sub-element
NGPv,h refers to Ranging Parameters element with a VHTz-Specific sub-element and a HEz-Specific sub-element

## Slide 15: Review Amendment Text
In document 18-788r0

## Slide 16: Motion
Move to
  approve document 18-788r0 for inclusion in the 802.11az draft
  Instruct the TGaz Editor to apply editorial instructions as described in submission 18-788r0 in the next 802.11az draft
  Grant TGaz Editor, editorial license
Mover:
Seconder:
Results: