## Slide 1: OOK Waveform Generation for FDMA Transmission
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have agreed to allow FDMA transmission in wide bandwidths such as 40MHz and 80MHz as depicted in [1]
  Each 20MHz bandwidth only contains one 4MHz sub-band for WUR
  One wake-up receiver can stay in one of the sub-bands in wide bandwidth
In this contribution, we deal with OOK waveform generation for the WUR FDMA transmission

## Slide 3: OOK Waveform Generation (1/4)
To generate OOK waveform, we consider the following
  Each 4MHz sub-band is located at the center of 20MHz bandwidth to reduce interference with each other
  The conventional Wi-Fi transmitter is reused
    For each sub-band, subcarriers from -6 to 6 in each 20MHz bandwidth with the subcarrier spacing of 312.5KHz are used
    7 length sequence or 13 length sequence is applied to each sub-band for the ‘ON’ part
    128- and 256-point IFFTs are performed in 40MHz and 80MHz, respectively
  Data rate in each sub-band can be different

## Slide 4: OOK Waveform Generation (2/4)
For example, consider the following case
  40MHz bandwidth is used for the FDMA transmission
  Data rate for STA 1 assigned to sub-band 1 is low
  Data rate for STA 2 assigned to sub-band 2 is high
  In the figure below, WUR-Sync 1, WUR-Sync 2 and WUR-Data 2 are composed of 2us ‘ON’ and ‘OFF’ parts while WUR-Data 1 consists of 4us ‘ON’ and ‘OFF’ parts
  In Region A, both sub-bands are based on the 2us signal
  In Region B, although sub-band 1 consists of 4us ‘ON’ and ‘OFF’ parts, we can consider both sub-bands are based on the 2us signal to easily generate the FDMA OOK waveform
Legacy preamble
Mark
WUR-Sync 1
WUR-Data 1
Legacy preamble
Mark
WUR-Sync 2
WUR-Data 2
Sub-band 1
Sub-band 2
Region A
Region B

## Slide 5: OOK Waveform Generation (3/4)
Assume, in Region B, Sub-band 1 and Sub-band 2 have data as shown below
  We can generate OOK waveform every 2us by applying 7 length sequence to every other subcarrier in all sub-bands corresponding to the ‘ON’ part
    For the second and sixth 2us waveforms (2~4us, 10~12us), 7 length sequence is applied only to sub-band 2
    For the third and seventh 2us waveforms (4~6us, 12~14us), 7 length sequence is applied to both sub-band 1 and sub-band 2
    For the forth and eighth 2us waveforms (6~8us, 14~16us), 7 length sequence is applied only to sub-band 1
  Then, Perform 128-point IFFT and choose either the first or second 1.6us signal in a 3.2us signal with 1.6us periodicity
  Finally, prepend 0.4us GI
In Region A, the same approach can be employed
Sub-band 1
Sub-band 2
Information 1
Information 1010
2us 4us 6us 8us 10us 12us 14us 16us

## Slide 6: OOK Waveform Generation (4/4)
For the case where all of the data rates are high in all sub-bands, we can use the 2us waveform generation approach as in the previous slide
For the case where all of the data rates are low in all sub-bands, we can also use the same approach or alternatively apply the following approach
  In Region A, the approach based on 2us waveform generation as in the previous slide can be applied
  In Region B, although we can employ the 2us waveform generation approach, we can use the following approach based on 4us waveform generation since both sub-bands are based on 4us signal
    To generate each 4us OOK waveform, 13 length sequence is applied to all sub-bands corresponding to the ‘ON’ part
    Then, Perform 128-point IFFT and finally prepend 0.8us GI
For the unification and simple implementation, we prefer to employ the 2us waveform generation based approach in all cases for the FDMA transmission
Legacy preamble
Mark
WUR-Sync 1
WUR-Data 1
Legacy preamble
Mark
WUR-Sync 2
Sub-band 1
Sub-band 2
Region A
Region B
WUR-Data 2

## Slide 7: Proposal
For the WUR FDMA transmission, center 13 subcarriers in each 20MHz with the subcarrier spacing of 312.5KHz are used for sub-band
The waveform of the WUR portion is generated every 2us except for the WUR-Data field with all assigned sub-bands using low data rate
To generate each 2us OOK waveform
  7 length sequence is applied to every other subcarrier in all sub-bands corresponding to the ‘ON’ part
  Perform 128-point IFFT and 256-point IFFT for 40MHz and 80MHz, respectively
  Choose either the first or second 1.6us signal in a 3.2us signal with 1.6us periodicity and finally prepend 0.4us GI
For the WUR-Data field with all assigned sub-bands using low data rate, the waveform is generated every 2us or 4us
To generate each 4us OOK waveform
  13 length sequence is applied to all sub-bands corresponding to the ‘ON’ part
  Perform 128-point IFFT and 256-point IFFT for 40MHz and 80MHz, respectively, and finally prepend 0.8us GI

## Slide 8: Straw Poll #1
Which option do you prefer for the data rates in the WUR FDMA transmission?
  Option 1 : all sub-bands used for WUR PPDU transmission use the same data rate
  Option 2 : each sub-band can use a different data rate
OP1/OP2/A :

## Slide 9: Straw Poll #2
Do you agree to add the following to the TGba SFD?
  For the WUR FDMA transmission, center 13 subcarriers in each 20MHz bandwidth with the subcarrier spacing of 312.5KHz can be used for sub-band
    For 40MHz, subcarriers with indices from -38 to -26 and indices from 26 to 38 is used for sub-band 1 and sub-band 2, respectively
    For 80MHz, subcarriers with indices from -102 to -90, indices from -38 to -26, indices from 26 to 38 and indices from 90 to 102 is used for sub-band 1, sub-band 2, sub-band 3 and sub-band 4, respectively
Y/N/A :

## Slide 10: Straw Poll #3
Do you agree to add the following to the TGba SFD?
  For the WUR FDMA transmission, the waveform of the WUR portion, i.e., the WUR-Sync and WUR-Data fields is generated every 2us except for the WUR-Data field where LDR is applied to all sub-bands used for a WUR PPDU transmission
Y/N/A :

## Slide 11: Straw Poll #4
Do you agree to add the following to the TGba SFD?
  For the WUR-Data field where LDR is applied to all sub-bands used for a WUR PPDU transmission, the waveform is generated every 2us or 4us
Y/N/A :

## Slide 12: Straw Poll #5
Do you agree to add the following to the TGba SFD?
  For the WUR FDMA transmission, the following approach can be applied to generate each 2us OOK waveform
    7 length sequence is applied to every other subcarrier in all sub-bands corresponding to the ‘ON’ part
    Perform 128-point IFFT and 256-point IFFT for 40MHz and 80MHz, respectively
    Choose either the first or second 1.6us signal in a 3.2us signal with 1.6us periodicity and finally prepend 0.4us GI

## Slide 13: Straw Poll #6
Do you agree to add the following to the TGba SFD?
  For the WUR FDMA transmission, the following approach can be applied to generate each 4us OOK waveform for WUR-Data field where LDR is applied to all sub-bands used for WUR PPDU transmission
    13 length sequence is applied to all sub-bands corresponding to the ‘ON’ part
    Perform 128-point IFFT and 256-point IFFT for 40MHz and 80MHz, respectively, and finally prepend 0.8us GI

## Slide 14: References
[1] IEEE 802.11-17/1625r6 Efficient FDMA MU Transmission Schemes for WUR WLAN