## Slide 1: PAPR Investigation on FDMA Transmission
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have agreed to allow WUR FDMA transmission in wide bandwidths such as 40MHz and 80MHz as depicted in [1]
  Each 20MHz bandwidth only contains one 4MHz sub-band for WUR
  One wake-up receiver can stay in one of the sub-bands in wide bandwidth
In this case, we investigate the PAPR by applying the phase rotation to each 20MHz sub-band
Furthermore, we propose 7/13 length sequences to guarantee a good PAPR

## Slide 3: Phase Rotation for Legacy Portion
The current Wi-Fi system employs the phase rotation to reduce the PAPR as follows [2]
For the legacy portion including the BPSK-Mark, we propose to use the phase rotation above
  By doing so, the PAPR for the L-SIG which may be the worst in WUR PPDU can be less than 12 dB in the wide bandwidths
  PAPRs for the legacy portion are shown in Appendix A
Simply denoted as [1 j]
Simply denoted as [1 -1 -1 -1]

## Slide 4: Phase Rotation for WUR Portion
We assume that OOK waveform for the WUR portion is generated as follows [3]
  2/4us waveforms are generated by applying 7/13 length sequences to all sub-bands corresponding to the ‘ON’ part
We consider full allocation, i.e., all sub-bands are used to transmit WUR PPDU
  In Appendix C, we additionally consider various partial allocation cases for 80MHz
To investigate the PAPR of the WUR portion, we need to consider various combinations of ‘ON’ and ‘OFF’ among all sub-bands
  For 40MHz and 80MHz, there are 4 and 16 combinations, respectively
  By considering all the combinations, we compute WUR PPDU and calculate PAPR
    The WUR PPDU structure used for the PAPR calculation is shown in Appendix B
PAPR is investigated by applying the following phase rotation
  No phase rotation (no PR) [1,1], [1,1,1,1]
  Phase rotation used in the current Wi-Fi (PR1) [1,j], [1,-1,-1,-1]
  New phase rotation (PR2) [1,-1], [1,j,j,1]  When considering various 7/13 length sequences, the majority of sequences select these values in terms of the PAPR
For the investigation, we assume 7/13 sequences with random BPSK coefficients
 For 80MHz, [1,j,j,1] comes from considering only full allocation and if we consider both full and partial allocation, phase rotation values can be different as shown in Appendix C

## Slide 5: PAPR for 40MHz
7 length sequence
13 length sequence
Each randomly generated sequence has different PAPR, and thus we plot the CDF of the PAPR
In 40MHz, the phase rotation does not guarantee a PAPR reduction
PAPR of the WUR portion can be worse than that of the L-SIG

## Slide 6: PAPR for 80MHz
7 length sequence
13 length sequence
These are only for the full allocation case
In 80MHz, PAPR is enhanced by the phase rotation
PAPR of the WUR portion can be worse than that of the L-SIG

## Slide 7: 7/13 Length Sequences Minimizing PAPR
In both wide bandwidths, PAPR of the WUR portion can be too high according to the 7/13 length sequences used for the OOK waveform generation
  PAPR can be even worse than the worst PAPR of the L-SIG shown in Appendix A
Also, the PAPR reduction gain by the phase rotation is marginal especially for 40MHz
Thus, to guarantee a good PAPR of the WUR portion for the WUR FDMA transmission, we need to use a proper sequence for the OOK waveform generation
By the minimax approach, we can obtain the following sequences (Seq1)
  [1 1 1 0 -1 1 -1], [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
  Note that these sequences also minimize the PAPR for the single-band transmission
  The minimax approach selects a sequence which minimizes the maximum PAPR among PAPRs of the WUR PPDU in 20MHz, 40MHz and 80MHz
For the WUR FDMA transmission, we don’t need to consider DC, and thus we can alternatively apply the following sequences which are also obtained by the minimax approach (Seq2)
  [1 1 1 -1 -1 1 -1], [1 1 1 -1 -1 -1 1 1 -1 1 1 -1 1]
Note that these four sequences are optimal even for the partial allocation cases in 80MHz

## Slide 8: PAPR for 40MHz
7 length sequence
13 length sequence
Low PAPR can be guaranteed by using Seq1 or Seq2
For the 7 length sequence, Seq2, i.e., the sequence with non-zero center tone is better (1dB gain)
For 40MHz, there is no PAPR reduction gain by the phase rotation

## Slide 9: PAPR for 80MHz
7 length sequence
13 length sequence
These are only for the full allocation case and PAPRs for the partial allocation cases are shown in Appendix C
Low PAPR can be guaranteed by using Seq1 or Seq2
For the 7 length sequence, Seq2, i.e., the sequence with non-zero center tone is better (1dB gain)
For 80MHz, PAPR can be further decreased by the phase rotation (max 3dB gain)
Performance difference between PR1 and PR2 is not big

## Slide 10: Conclusion
For the WUR FDMA transmission, the phase rotation used for the current Wi-Fi system can be applied to the legacy portion including BPSK-Mark for PAPR reduction
For the WUR portion, we need to apply proper sequences for the OOK waveform generation as described in slide 7 to guarantee a good PAPR
In addition, the phase rotation can further enhance the PAPR especially for 80MHz
  The existing phase rotation used for the current Wi-Fi system is sufficient
Furthermore, the sequence with non-zero center tone can additionally reduce the PAPR especially for the 7 length sequence
  However, the gain is not significant
  For the unified sequence between single- and multi-bands, the sequence with null center tone can be more preferred

## Slide 11: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  For the WUR FDMA transmission, the existing phase rotation is applied to the legacy portion including BPSK-Mark
Y/N/A :

## Slide 12: Straw Poll #2
Do you agree to add the following to the 11ba SFD?
  For the WUR FDMA transmission, the existing phase rotation is applied to the WUR portion
Y/N/A :

## Slide 13: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  For the WUR FDMA transmission, the following sequence is applied to generate the 2us OOK waveform
    [1 1 1 0 -1 1 -1]
Y/N/A :

## Slide 14: Straw Poll #4
Do you agree to add the following to the 11ba SFD?
  For the WUR FDMA transmission, the following sequence is applied to generate the 4us OOK waveform
    [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
Y/N/A :

## Slide 15: References
[1] IEEE 802.11-17/1625r6 Efficient FDMA MU Transmission Schemes for WUR WLAN
[2] IEEE P802.11-REVmd/D1.0
[3] IEEE 802.11-18/xxxxr0 OOK Waveform Generation for FDMA Transmission

## Slide 16: Appendix A – PAPR for Legacy Preamble
PAPR for L-STF [dB]
PAPR for L-LTF [dB]
 | 20MHz | 40MHz | 80MHz
no phase rotation | 2.2394 | 5.0997 | 8.1100
Phase rotation | 2.2394 | 5.2497 | 4.3480
 | 20MHz | 40MHz | 80MHz
no phase rotation | 3.1658 | 6.1761 | 9.1864
Phase rotation | 3.1658 | 5.7938 | 5.3962

## Slide 17: Appendix A – PAPR for Legacy Preamble
PAPR for L-SIG [dB]
 |  | Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6 | Worst
40MHz | No phase rotation | 8.4251 | 8.7728 | 10.9557 | 9.2245 | 8.1282 | 8.7728 | 10.9557
 | Phase rotation | 8.1208 | 9.7488 | 9.9882 | 8.2288 | 9.1345 | 8.5720 | 9.9882
80MHz | No phase rotation | 11.4354 | 11.7831 | 13.9660 | 12.2348 | 11.1385 | 11.7831 | 13.9660
 | Phase rotation | 8.6150 | 9.6555 | 8.5311 | 7.4858 | 8.0437 | 8.0419 | 9.6555
Case 1 | Frame Body = 0 octet, HDR
Case 2 | Frame Body = 0 octet, LDR
Case 3 | Frame Body = 8 octets, HDR
Case 4 | Frame Body = 8 octets, LDR
Case 5 | Frame Body = 16 octets, HDR
Case 6 | Frame Body = 16 octets, LDR

## Slide 18: Appendix A – PAPR for Legacy Preamble
CDF of PAPR for L-SIG considering various PPDU lengths

## Slide 19: Appendix B – PAPR for WUR Portion
In 40MHz, to calculate the PAPR, we consider the following PPDU
  If each combination occurs almost evenly in a practical WUR PPDU, this PPDU format may be reasonable for PAPR calculation
In 80MHz, similar to 40MHz case, we consider the PPDU which consists of all of the combinations of ‘ON’ and ‘OFF’ for the PAPR calculation
Sub-band 1
Sub-band 2
2us 4us 6us 8us for 7 length sequence
4us 8us 12us 14us for 13 length sequence
OFF ON ON OFF
ON OFF ON OFF

## Slide 20: Appendix C – PAPR for WUR Portion with Partial Allocation in 80MHz
Allocation cases for 80MHz (O: allocated, X: not allocated)
  Case 0 : O O O O (full allocation)
  Case 1 : O O O X
  Case 2 : O O X O
  Case 3 : O X O O
  Case 4 : X O O O
  Case 5 : O O X X
  Case 6 : O X O X
  Case 7 : O X X O
  Case 8 : X O O X
  Case 9 : X O X O
  Case 10 : X X O O
For the cases where three sub-bands are allocated for FDMA transmission, there are 8 combinations of ‘ON’ and ‘OFF’, and we consider the PPDU which consists of all 8 combinations of ‘ON’ and ‘OFF’ for the PAPR calculation
For the cases where two sub-bands are allocated for FDMA transmission, there are 4 combinations of ‘ON’ and ‘OFF’, and we consider the PPDU which consists of all 4 combinations of ‘ON’ and ‘OFF’ for the PAPR calculation

## Slide 21: Appendix C – PAPR for WUR Portion with Partial Allocation in 80MHz
By considering all of the allocation cases in the previous slide, we can obtain the following sequences which optimize the PAPR by the minimax approach
  7 length sequence with DC : [1 1 1 0 -1 1 -1]
  13 length sequence with DC : [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
  7 length sequence with no DC : [1 1 1 -1 -1 1 -1]
  13 length sequence with no DC : [1 1 1 -1 -1 -1 1 1 -1 1 1 -1 1]
  Note that these are the same as Seq1 and Seq2
In each sequence, the following phase rotation (PR3) is optimal in terms of the PAPR when considering all of the allocation cases
  [1 1 1 0 -1 1 -1]  [1,-1,-1,1]
  [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]  [1,-1,-1,1]
  [1 1 1 -1 -1 1 -1]  [1,j,1,j]
  [1 1 1 -1 -1 -1 1 1 -1 1 1 -1 1]  [1,-j,1,-j]

## Slide 22: Appendix C – PAPR for WUR Portion with Partial Allocation in 80MHz
PAPR [dB] – 7 length sequence
 | Case 0 | Case 1 | Case 2 | Case 3 | Case 4
Seq1 w/ PR1 | 8.7625 | 7.4665 | 9.9291 | 8.9520 | 10.0119
Seq1 w/ PR3 | 8.9644 | 7.4665 | 8.9313 | 8.9313 | 7.4665
Seq2 w/ PR1 | 7.8858 | 6.6108 | 9.1365 | 8.0826 | 9.0985
Seq2 w/ PR3 | 8.1126 | 6.5812 | 8.0822 | 8.0822 | 6.5812
Case 5 | Case 6 | Case 7 | Case 8 | Case 9 | Case 10
8.1682 | 8.2583 | 8.1682 | 8.2509 | 8.2509 | 8.2509
8.1682 | 8.2583 | 8.2509 | 8.2509 | 8.2583 | 8.1682
7.3762 | 7.4032 | 7.3762 | 7.3395 | 7.3723 | 7.3395
7.4112 | 7.3723 | 7.4042 | 7.3914 | 7.3723 | 7.4112

## Slide 23: Appendix C – PAPR for WUR Portion with Partial Allocation in 80MHz
PAPR [dB] – 13 length sequence
 | Case 0 | Case 1 | Case 2 | Case 3 | Case 4
Seq1 w/ PR1 | 8.5916 | 7.2822 | 9.7838 | 8.7660 | 9.8415
Seq1 w/ PR3 | 8.7850 | 7.2822 | 8.7519 | 8.7519 | 7.2822
Seq2 w/ PR1 | 8.6308 | 7.3275 | 9.8804 | 8.8014 | 9.8535
Seq2 w/ PR3 | 8.8404 | 7.3273 | 8.8070 | 8.8070 | 7.3273
Case 5 | Case 6 | Case 7 | Case 8 | Case 9 | Case 10
8.0228 | 8.0739 | 8.0228 | 8.0803 | 8.0803 | 8.0803
8.0228 | 8.0739 | 8.0803 | 8.0803 | 8.0739 | 8.0228
8.1195 | 8.1194 | 8.1195 | 8.0928 | 8.1190 | 8.0928
8.1179 | 8.1190 | 8.1188 | 8.1204 | 8.1190 | 8.1179