## Slide 1: Multi-band WUR
Date: 2018-05-05
Authors:

## Slide 2: Recap: WUR in 5GHz band
From current TGba SFD, the WUR PPDU shall not be transmitted on the DFS channel.
  Because the WUR PPDU can be considered as a radar signal by a legacy AP.
So, when an AP operates its BSS in the DFS channel, the WUR operation may be supported by one of the following:
  Off-channel WUR in the same band: The AP transmits the WUR PPDU outside the BSS bandwidth.
    Because the AP have to switch its operating channel frequently, it can degrade the performance of the BSS.
  Multi-band WUR: A STA uses the WUR operation in 2.4 GHz served by the same AP.

## Slide 3: Multi-band WUR
STA
AP
WUR Mode setup request
WUR Mode setup response
WUR PPDU
PS-Poll
DATA
WUR PPDU
802.11 Radio in 5 GHz band
WUR in 2.4 GHz band
ON
ON
ON
ON
Frame exchange in 5 GHz band
Frame exchange in 2.4 GHz band
A STA associates with an AP operating in 5 GHz band and sets up the WUR operation in 5 GHz band.
The WUR of the STA is activated to receive WUR PPDUs in 2.4 GHz band during the negotiated WUR duty cycle schedule.
Data frame delivery is occurred in 5 GHz band.

## Slide 4: Multi-band WUR
From current TGba Draft 0.2
  The WUR Operation element contains the set of parameters necessary to support the WUR operation.
    The WUR Operating Class field indicates the operating class in use for transmission of WUR frame from the WUR AP to the WUR non-AP STA.
    The WUR Channel field indicates the channel in use for transmission of WUR frame from the WUR AP to the WUR non-AP STA.
  It seems that the WUR operating channel indicated by the WUR Operating Class and WUR Channel fields can be chosen from different band.
  In consequence, the multi-band WUR is allowed in current draft.

## Slide 5: Multi-band WUR
Discussion
  When TSF timers between the APs operated on the different bands are not synchronized, which TSF timer is applied on the WUR duty cycle schedule?
  If it is based on TSF timer of the AP with which the STA is not associated, the time offset of the TSF timers between those APs should be provided to the STA.
    STA’s implementation can be complicated.
  If it is based on TSF timer of the AP with which the STA is associated, no more protocol change is needed.
    AP’s implementation can be complicated but STA’s implementation may not have any impact.
  We support 2nd option.

## Slide 6: Multi-band WUR
Discussion
  When the WUR duty cycle schedule is based on TSF timer of the AP with which the STA is associated, the AP schedules multiple WUR Beacon frames for synchronizing the STAs having different TSF timers.
STA
AP
WUR Mode setup request
WUR Mode setup response
WUR PPDU
PS-Poll
DATA
WUR Beacon PPDU
with 5 GHz partial TSF
802.11 Radio in 5 GHz band
WUR in 2.4 GHz band
ON
ON
ON
ON
Frame exchange in 5 GHz band
Frame exchange in 2.4 GHz band
WUR Beacon PPDU
with 2.4 GHz partial TSF

## Slide 7: Conclusion
Through a multi-band WUR, an AP not only utilizes a full spectrum in 5 GHz band but also efficiently provide the wake-up service to a STA associated in 5 GHz band.
Also, because a service coverage of the WUR PPDU in 2.4 GHz band is much longer, the proposed multi-band WUR can have a service coverage extension gain.

## Slide 8: Straw Poll 1
Do you support a multi-band WUR (slide 3)?

## Slide 9: Straw Poll 2
Do you support that the WUR duty cycle schedule is based on the TSF timer of the AP with which the STA is associated?