## Slide 1: FDMA Channel signaling
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have discussed and passed a motion about FDMA transmission
So we will address channel signaling for FDMA transmission

## Slide 3: FDMA
We had a passed motion for FDMA transmission [1]
  WUR PPDU can be transmitted in multiple channels
  WUR STAs are distributed in multiple channels
  Each WUR STA may only receive WUR PPDU through the allocated WUR channel

## Slide 4: Channel signaling for FDMA
We should define following signaling for FDMA transmission
  WUR operating channel indication
  WUR beacon channel indication
  WUR channel switch indication

## Slide 5: WUR operating channel indication
A WUR STA has to be allocated in one of WUR channel before it begins WUR operation
We already define WUR channel field in WUR Operation element [2]
  So we can use this field to
  support FDMA transmission
  AP allocates different channels
  to each STA

## Slide 6: WUR beacon channel indication
WUR beacon channel indication is highly relevant to how WUR beacon frame is transmitted
  Issue on WUR beacon transmission is addressed in another submission [3]
  If WUR beacon is transmitted in one WUR channel only, WUR beacon channel should be indicated to WUR STA
    If WUR channel is same as PCR channel, WUR beacon will be transmitted on primary channel of PCR
    If WUR channel is different with PCR channel, WUR beacon channel shall be indicated

## Slide 7: WUR channel switch indication
There are several reasons why an AP may change WUR channel
  PCR channel has been changed
  Poor performance on a current FDMA channel
  Regrouping for WUR STA
We already have signaling for channel switch
  CSA (Channel Switch Announcement) element

## Slide 8: Channel Switch Announcement
Channel Switch Mode
  0: No restriction on transmission until a channel switch
  1: No transmission until a channel switch
New Channel Number: the number of the channel after the channel switch
Channel Switch Count: the number of TBTTs until the channel switch

## Slide 9: Proposed CSA modification
Add new value in Channel Switch Mode field for WUR
  Value 2: WUR channel switch
New Channel Number: the number of the WUR channel after the channel switch (when CSM value is 2)
Channel Switch Count: the number of TWBTTs until the channel switch (when CSM value is 2)

## Slide 10: Summary
In this submission, we address channel signaling issue in FDMA transmission
  WUR operating channel can be easily indicated through WUR mode signaling
  If WUR channel is different with PCR channel, WUR beacon channel shall be indicated
  WUR channel switch indication can be indicated through modified CSA element

## Slide 11: References
[1] 11-17-1625-06-00ba-efficient-fdma-transmission-schemes-for-wur-wlan.pptx
[2] IEEE P802.11ba™/D0.2
[3] 11-18-0716-00-00ba-WUR-Beacon-transmission.pptx

## Slide 12: Straw poll 1
Do you support following sentence?
  If WUR channel is different with PCR channel, the channel to which WUR beacon frame is transmitted shall be indicated to WUR STAs

## Slide 13: Straw poll 2
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA

## Slide 14: Straw poll 3
Do you support WUR channel switch signaling in slide 9?