## Slide 1: FDMA Channel signaling
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Lei Huang | Panasonic |  |  | lei.huang@sg.panasonic.com

## Slide 2: Introduction
We have discussed and passed a motion about FDMA transmission
So we will address channel signaling for FDMA transmission

## Slide 3: FDMA
We had a passed motion for FDMA transmission [1]
  WUR PPDU can be transmitted in multiple channels
  WUR STAs are distributed in multiple channels
  Each WUR STA may only receive WUR PPDU through the allocated WUR channel

## Slide 4: Channel signaling for FDMA
We should define following signaling for FDMA transmission
  WUR operating channel indication
  WUR beacon channel indication
  WUR channel switch indication

## Slide 5: WUR operating channel indication
A WUR STA has to be allocated in one of WUR channel before it begins WUR operation
→ This issue is resolved by
Yongho Seok (790r0)[4]

## Slide 6: WUR beacon channel indication
We have an agreement on how WUR beacon frame is transmitted
  WUR beacon frame is transmitted on one single channel
  So WUR beacon channel should be indicated
→ This issue is resolved by Yongho Seok (790r0) [4]

## Slide 7: WUR channel switch indication
There are several reasons why an AP may change WUR channel of a certain WUR STA
  PCR channel has been changed
  Poor performance on a current FDMA channel
  Regrouping for WUR STA
  Duty cycle operation of a WUR STA is changed
Also, WUR channel switching capability is define in WUR Parameters field
So we have to define WUR channel switch indication

## Slide 8: WUR channel switch indication
We may have several options
  Reuse WUR Mode Setup frame
    Option 1: Define a new Action Type: Change WUR Parameter
      Both WUR AP and WUR STA can initiate WUR parameter change
    Option 2: Enter WUR Mode Response can be transmitted in unsolicited manner
      Only WUR AP can initiate WUR parameter change
    Using option 1 and 2, we can change not only WUR channel but also other WUR parameters
  Reuse Channel Switch Announcement element
    Option 3: Define a new Channel Switch Mode

## Slide 9: Summary
In this submission, we address channel signaling issue in FDMA transmission
  WUR operating channel can be easily indicated through WUR mode signaling
  WUR beacon channel shall be indicated
  WUR channel switch indication shall be defined

## Slide 10: References
[1] 11-17-1625-06-00ba-efficient-fdma-transmission-schemes-for-wur-wlan.pptx
[2] IEEE P802.11ba™/D0.2
[3] 11-18-0716-00-00ba-WUR-Beacon-transmission.pptx
[4] 11-18-0790-00-00ba-spec-text-for-wur-fdma-operation.docx

## Slide 11: Straw poll 1
Which option do you prefer?
  Option 1: Reuse WUR Mode Setup frame and define a new Action Type(Change WUR Parameter)
  Option 2: Reuse WUR Mode Setup frame and Enter WUR Mode Response can be transmitted in unsolicited manner
  Option 3: Reuse Channel Switch Announcement element