## Slide 1: Discovery Assistance for 802.11ay
Date: 2018-05-08
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4027 | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4405 | kazuyuki.sakoda(at)sony.com

## Slide 2: Overview
Robustness and latency are critical for consumer devices use cases
In [1], we proposed the use of the multi-band discovery assistance to:
  Reduce BHI overhead latency
  beacons are reduced to minimum and on-demand SLS is triggered
  Enable TDD channel access for consumer devices without relying on human triggering
  Use multi-band to signal the request for beamforming
In [2], 3 options for discovery assistance implementation are proposed
  Option 1: new defined action frames
  Option 2: FST Setup Request and Response frames
  Option 3: OCT + Information Request and Response frames
Majority of TGay members suggested Option 2
This contribution presents details on Option 2 solution to use the FST setup frames to trigger discovery assistance

## Slide 3: Multi-band Discovery Assistance (1)
Beacons/Probe Responses advertise the multi-band and discovery assistance capabilities on lower band
Need to add 1-bit in the Multi-band element to indicate that STA supports discovery assistance for the advertised frequency band and channel
Propose to use 1 bit out of the 3 reserved bits in the Multi-band Control field
 | B0 B2 | B3 | B4 | B5 | B5B6 B7
 | STA Role | STA MAC Address Present | Pairwise Cipher Suite Present | Discovery Assistance Enabled | Reserved
Bits: | 3 | 1 | 1 | 1 | 32
Multi-band element

## Slide 4: Multi-band Discovery Assistance (2)
New STA sends FST Setup Request frame containing DMG Discovery Assistance Request element on lower band
Discovery assistance can happen in conjunction with FST
FST Setup Request frame

## Slide 5: Multi-band Discovery Assistance (3)
FST Setup Response Frame
AP responds with FST Setup Response frame containing DMG Discovery Assistance Response element on lower band

## Slide 6: Multi-band Discovery Assistance (4)
Use MLME-BF-TRAINING primitives to trigger beacon sweeping for new STA or MLME-TDD-BF-TRAINING primitives to trigger TDD beamforming
AP starts sweeping DMG beacons, sends the beamforming frames or listens for new STA beamforming frames/probes on mmW band
New STA is expecting discovery/beamforming frames from the network STA or start transmitting beamforming frames/probes

## Slide 7: Multi-band Discovery Assistance Standard Requirements*
Adding 1-bit to the multi-band element to advertise discovery assistance capability
2 new elements (DMG Discovery Assistance Request and DMG Discovery Assistance Response elements)
Enabling FST Setup Request and FST Setup Response frames to carry the DMG Discovery Assistance Request and DMG Discovery Assistance Response elements, respectively
Enabling triggering SLS or TDD beamforming when FST Setup Response frame with DMG Discovery Assistance Response element is received and notified discovery assistance acceptance
* Normative Text available at 11-18/0817r0

## Slide 8: Straw poll (1)
Do you support the use of the FST setup protocol as described in 11-18/0817r0 to enable multi-band discovery assistance in multi-band capable devices?
  Yes
  No
  Abstain

## Slide 9: mmW Discovery Assistance
Problem:
  New STA needs to discover more than one STA in the DMG BSS or distribution network
  New STA does not have to associate through lower band to each STA in the network to request discovery assistance
  All STAs are not necessary expected to operate BSS on lower band
Solution:
  Existing STAs can forward the DMG Discovery Assistance Request element to neighbor STAs to trigger neighbor STAs to enable discovery assistance for the new STA

## Slide 10: Multi-band Discovery Assistance Example
STA 1
(New Multi-band STA)
STA 2
(Multi-band AP)
DMG Discovery Asst.
Req ie.
DMG Discovery Asst.
Resp ie.

## Slide 11: mmW Discovery Assistance Example
STA 1
(New Multi-band STA)
STA 2
(Multi-band AP)
STA 1 discovers STA 2 on lower band
STA 1 sends discovery assistance request on lower band to STA 2
STA 2 sends discovery assistance request to STA 3 to trigger discovery assistance for the new STA
STA 3 sends discovery assistance response to STA 2 and starts the discovery assistance
STA 2 sends discovery assistance response to the STA 1 and start the discovery assistance
STA 3
(DMG STA)
DMG Discovery Asst.
Req ie.
DMG Discovery Asst.
Resp ie.
DMG Discovery Asst.
Req ie.
DMG Discovery Asst.
Resp ie.

## Slide 12: mmW Discovery Assistance Standard Implementation
STA 1
(New Multi-band STA)
STA 2
(Multi-band AP)
STA 2
(DMG STA)
FST Setup Req. with DMG
Discovery Asst. Req ie.
FST Setup Resp. with DMG
Discovery Asst. Resp ie.
Information Resp. with DMG
Discovery Asst. Resp ie.
Information Req. with DMG
Discovery Asst. Req ie.

## Slide 13: mmW Discovery Assistance Standard Requirements
Enable Information Request and Information Response frames to carry the DMG Discovery Assistance Request and DMG Discovery Assistance Response elements, respectively
Enable triggering SLS or TDD beamforming when Information Response frame with DMG Discovery Assistance Response element is received and notified discovery assistance acceptance

## Slide 14: Straw poll (2)
Do you support the use of Information Request and Information Response frames to enable mmW Discovery Assistance?
  Yes
  No
  Abstain

## Slide 15: References
[1] IEEE 802.11-18/486r0, “Multi-band Discovery Assistance”, Mohamed Abouelseoud, et.al.
[2] IEEE 802.11-18703r2, “Discussion the Multi-band Discovery Assistance Proposal”, Mohamed Abouelseoud, et.al.

## Slide 16: Expected Latency Due to BHI (1)
TXTIME(µs) = TL-STF+ TL-CE+ ((Length +LL-Header)x 8 + NCW x 168) x 32/1.76e3 + TTRN
LL-Header=5 Octets
BHI
Frame Spacing | Time (µs)
MBIFS ( between BTI and ABFT) | 9
LBIF ( when switching DMG antennas) | 2
SBIF ( between sweeping frames) | 1
 | Length (octets) | TX Time (µs)
SSW Frame | 26 | 14.91
SSW FB Frame | 28 | 18.25
Beacon Frame no TRN | 72 | 30.76
Beacon Frame with 31 TRN | 72 | 118.69

## Slide 17: Expected Latency Due to BHI (2)
 | Beacons/BI | No of SSW slots | SSW frames/ slot | No of DMG Antennas | No of beacon TRNs
Option 1 | 1 | 2 | 8 | 1 | 0
Option 2 | 8 | 4 | 16 | 1 | 0
Option 3 | Full beacon sweep | 9 | 16 | 1 | 0
Option 4 | Full beacon sweep | 9 | 16 | 2 | 0
Option 5 | Full beacon sweep | 9 | 16 | 2 | 16
Option 6 | Full beacon sweep | 9 | 16 | 2 | 31
Option 7 | Full beacon sweep | 36 | 16 | 2 | 31

## Slide 18: Discovery for TDD mode
On demand sweeping is a built-in feature in TDD mode
However, TDD mode as presented in [3] assumes manual triggering of the unicast beamforming frames.
A proper discovery trigger signaling is needed to enable the use of TDD mode for consumer devices

## Slide 19: Discovery for non-TDD mode
Latency reduction can also be achieved through non-TDD mode
Tools already provided in the standard to reduce beacon transmission periodicity(partial sweeping), ABFT period optional, ATI optional
Reducing BHI to minimal affects discoverability
A discovery trigger signal is needed to enable the full beacon sweep only whenever it is needed and keep it minimum otherwise

## Slide 20: Wi-Fi Agile Multi-band
Facilitates better management of Wi-Fi networks changing conditions and improved resource utilization
Uses several mechanisms
  Dynamic network monitoring: APs and client devices continually exchange information about the current Wi-Fi network environment
  Intelligent steering: APs suggest another AP, frequency band, or channel to client devices when the Wi-Fi environment becomes congested
  Fast network transitions: Once a client device decides to roam to a different AP, band, or channel, the association and connection happen quickly and seamlessly
WiFi Agile Multi-band does not consider network discovery and beacon/BF sweeping issues, it only exchanges information of prioritized available networks