## Slide 1: WUR FDMA Channel Access
Date: 2018-05-08
Authors:

## Slide 2: Introduction
The concept of WUR FDMA transmission has been accepted [1]
Each 20MHz only contain one 4MHz sub-channel for wake-up signal transmission.
Similar to 11ax’s 20MHz only operation, one wake-up receiver can stay in one of the sub-channel in wide bandwidth.
In this contribution we discuss some Channel Access issues related to WUR FDMA transmission.

## Slide 3: WUR FDMA Channel Access (1/3)
WUR FDMA transmission is possible only when multiple WUR operating channels are defined in a BSS and WUR STAs are assigned to different WUR operating channels.
Example: 4 WUR channels are assigned within the PCR bandwidth in a 80 MHz BSS.
A related topic of WUR Beacon transmission on multiple WUR channels is discussed in [2]. We only focus on FDMA channel access issues in this contribution.
Primary 20
WUR Signal for STA1
L-Preamble + BPSK Mark
WUR Signal for STA2
L-Preamble + BPSK Mark
WUR Signal for STA3
L-Preamble + BPSK Mark
WUR Signal for STA4
L-Preamble + BPSK Mark
Secondary 20
Secondary 40-L
Secondary 40-H
WUR CH-1
WUR CH-2
WUR CH-3
WUR CH-4
WUR channels
PCR channels
STA1
STA2
STA3
STA4
Assigned
WUR STAs

## Slide 4: WUR FDMA Channel Access (2/3)
WUR FDMA transmission enhances the efficiency of multi-user wake-up operations. However, very often AP may only need to wake a subset of WUR STAs due to different traffic needs, different duty cycle periodicity and so on.
Example: AP only needs to wake STA3 and STA4 assigned on the secondary 40 MHz channel.
802.11 channel access rules does not allow the above WUR FDMA transmission. WUR transmissions to STA3 or STA4 is not possible when P20 or S20 is empty.
Issue-1: How to enable WUR FDMA transmission in the presence of empty WUR channels?
Primary 20
WUR Signal for STA3
L-Preamble + BPSK Mark
WUR Signal for STA4
L-Preamble + BPSK Mark
Secondary 20
Secondary 40-L
Secondary 40-H
WUR CH-1
WUR CH-2
WUR CH-3
WUR CH-4
WUR channels
PCR channels
Empty WUR Channels
STA1
STA2
STA3
STA4
Assigned
WUR STAs

## Slide 5: WUR FDMA Channel Access (3/3)
In the presence of activities on non-primary channels, only the following 3 WUR FDMA transmission scenarios are possible for the above example when the IEEE 802.11 wide-band channel access rule is followed:
WUR transmissions to STA3 or STA4 is only possible when the entire 80 MHz is idle.
Issue-2: Lower WUR transmission opportunities for STAs assigned to non-primary channels.
Primary 20
WUR Signal for STA1
L-Preamble + BPSK Mark
WUR Signal for STA1
L-Preamble + BPSK Mark
WUR Signal for STA2
L-Preamble + BPSK Mark
WUR Signal for STA1
L-Preamble + BPSK Mark
WUR Signal for STA2
L-Preamble + BPSK Mark
WUR Signal for STA3
L-Preamble + BPSK Mark
WUR Signal for STA4
L-Preamble + BPSK Mark
Secondary 20
Secondary 40-L
Secondary 40-H
If S20 is Busy
If either S40-L or S40-H is Busy
Whole 80 MHz is idle
1) WUR TX on Primary 20 only
2) WUR TX on Primary 40 only
3) WUR TX on Full 80 MHz
WUR transmission not allowed
WUR transmission not allowed

## Slide 6: Proposal (1/2) - Addresses Issue-1
The risk of another 802.11 STA starting transmission is high if the Primary 20 MHz is idle.
Proposal: AP may transmit the Legacy Preamble and BPSK-Mark followed by a “NULL Signal” on the empty WUR channel in the Primary 20 MHz.
Primary 20
NULL Signal
L-Preamble + BPSK Mark
L-Preamble + BPSK Mark
WUR Signal for STA3
L-Preamble + BPSK Mark
WUR Signal for STA4
L-Preamble + BPSK Mark
Secondary 20
Secondary 40-L
Secondary 40-H
WUR CH-1
WUR CH-2
WUR CH-3
WUR CH-4
WUR channels
PCR channels
STA1
STA2
STA3
STA4
Assigned
WUR STAs
WUR Signal for STA2

## Slide 7: Proposal (1/2) - Addresses Issue-1 (cont.)
Discussion on the content of the “NULL Signal”:
The “NULL Signal” may be any signal in WUR waveform that fulfills the following conditions:
  Same length as the longest WUR Signal within the WUR PPDU
  May be disregarded by WUR STAs
As an example, the longest WUR Signal within the WUR PPDU may be used as the “NULL Signal”. Alternatively, AP may also choose:
  WUR Wake-up frame having an unused Wake Up ID
  WUR Discovery frame
  WUR vendor specific frame

## Slide 8: Proposal (2/2) - Addresses Issue-2
A WUR AP may “puncture” WUR channels during WUR FDMA transmission, similar to 11ax preamble puncture mode.
Since the receiver side operation at WUR STAs is the same whether or not WUR channels are punctured, puncturing can be more flexible compared to 11ax. Punctured WUR FDMA transmission may be allowed as long as following conditions are fulfilled:
  Primary 20 MHz channel cannot be punctured.
  A valid WUR signal must be transmitted on at least one 20 MHz channel within the secondary 40 MHz.
Primary 20
Secondary 20
Secondary 40-L
Secondary 40-H
NULL Signal
L-Preamble + BPSK Mark
WUR Signal for STA3
L-Preamble + BPSK Mark
WUR Signal for STA4
L-Preamble + BPSK Mark
WUR Signal may still be transmitted on Secondary 40 channels even when Secondary 20 is busy.
The sub-carriers in the busy channels are Nulled.

## Slide 9: Summary
In this presentation we discussed some channel access issues related to WUR FDMA transmission and proposed:
A WUR AP may transmit the Legacy Preamble and BPSK-Mark followed by a “NULL Signal” on empty WUR channels during WUR FDMA transmission.
A WUR AP may “puncture” WUR channels during WUR FDMA transmission.

## Slide 10: Straw Poll 1
Do you agree that a WUR AP may transmit the Legacy Preamble and BPSK-Mark followed by a “NULL Signal” on the empty WUR channel in the Primary 20 MHz during WUR FDMA transmission?
  The “NULL Signal” may be any signal in WUR waveform that fulfills the following conditions:
    Same length as the longest WUR Signal within the WUR PPDUs
    May be disregarded by WUR STAs
Y/N/A

## Slide 11: Straw Poll 2
Do you agree that a WUR AP may “puncture” WUR channels during WUR FDMA transmission?
Y/N/A

## Slide 12: References
[1] IEEE 802.11-17/1625r6 - Efficient FDMA MU Transmission Schemes for WUR WLAN
[2] IEEE 802.11-18/0113r0 - WUR Beacon transmission