## Slide 1: Clarifications on WUR/PCR interactions
Authors:
Alfred Asterjadhi,
George Cherian

## Slide 2: Introduction
Several rules for WUR/PCR interactions are included in SFD[1] & draft[2]
  Switching between WUR mode to PCR modes
  Suspension of WUR modes
  Additional components for the PCR frame delivery, etc.
In this slide deck we discuss the following:
  Existing definition of WUR mode as per SFD and D0.3
  Interactions between the WUR and the PCR of a STA with examples for:
    Individual addressed delivery (with baseline PS modes)
    Group addressed delivery (with baseline DTIM mode)
    TWT-based delivery (with existing TWT modes)
We highlight missing rules (if any) for these operations
  And propose clarifications needed to ensure consistency and finalize behavior

## Slide 3: WUR Mode
The WURx of a WUR non-AP STA can be in one of the two states [2]:
  WURx Awake: the WURx of the WUR non-AP STA is fully powered to receive WUR frame
  WURx Doze: the WURx of the WUR non-AP STA is not able to receive WUR frame
NOTE 1—The PCR component of a WUR non-AP STA can be in awake or doze state as defined in 11.2.1
NOTE 2—The PCR component of a WUR non-AP STA can be in active mode or power save (PS) mode as defined in 11.2.3.2
If a non-AP STA is in WUR mode, then [2]:
  The non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the doze state.
  The existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (e.g. TWT, schedule for WNM Sleep Mode) is suspended:
    STA is not required to wake up during the service period if the service period is suspended.
    The parameters of the negotiated service period for the non-AP STA’s PCR schedule is still saved by the AP and non-AP STA when the negotiated service period is suspended.
  The non-AP STA may not listen for Beacon frames if the non-AP STA is in PS mode.

## Slide 4: AP behavior [1]
An AP that transmits a wake-up frame addressed to a non-AP STA that satisfies condition 1 shall follow existing PCR operation to deliver individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
The AP that intends to schedule a transmission through the PCR for a WUR STA shall schedule it if any of the following conditions is met:
  The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted wake-up frame intended to the non-AP STA has expired
  The non-AP STA has indicated it is in awake state after transmitting a frame through the PCR to the AP
  Note that the transmission is not limited to the individually addressed buffered BU(s)
An AP that transmits a wake-up frame indicating group addressed buffered BU(s) shall follow existing PCR operation to deliver group addressed buffered BU(s)
The AP shall schedule for transmission of group addressed buffered BU(s) through PCR if the following condition is met:
  The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted wake-up frame indicating buffered group addressed BU(s) of PCR has expired

## Slide 5: STA behavior [1]
A non-AP STA that receives a wake-up frame that satisfies condition 1 shall follow existing PCR operation to retrieve individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
A non-AP STA that receives a wake-up frame with an indication of buffered group addressed BU(s) shall follow existing PCR operation to receive group addressed BU(s).
A non-AP STA that receives a wake-up frame with an indication to check PCR beacon shall follow existing PCR operation to attempt to receive the PCR Beacon information.

## Slide 6: Individual addressed delivery
WUR exchanges
  STA is in WUR mode (WUR doze outside of ON duration, and WUR awake during ON duration)
  AP only sends WUR Wake Up frame addressed to STA if it has DL BUs for the STA
    The Address field of the frame has WID of STA, GID assigned to STA, or WID that is present in Frame Body
PCR exchanges
  STA wakes up its PCR after receiving a Wake Up frame addressed to it (no need to read any Beacon)
  STA contends for the WM using EDCA to send a poll (see (11.2.3)) that is
    A PS Poll frame for baseline PS mode (PM bit of PS-Poll is ignored),
    An APSD trigger frame for baseline APSD mechanism (PM bit of frame is 1),
    A frame soliciting immediate response with PM bit of 0 for Active mode
  AP may help the STA to transmit the poll by sending a Trigger frame, after PCR transition delay has expired
  AP shall transmit buffered BUs addressed to the STA at designated times and that comply to restrictions valid for PCR mode of operation (number of BUs, service periods, etc.)
  STA goes to doze state according to its PCR instructions (PM bit set to 1 or after receiving an EOSP bit of 1)
    Note: The WUR operation is enabled when the STA is in doze state by default
Poll
Ack
AP
STA
WUR
frame
AP
STA
Duty Cycle Period
ON Duration
PCR delay
Trigger
individually addressed frame exchanges
DL BU
Ack
…
PCR awake state
WUR awake state
WUR doze state
PCR doze state

## Slide 7: Group addressed delivery
WUR exchanges
  STA is in WUR mode (WUR doze outside of ON duration, and WUR awake during ON duration)
  AP sends Wake Up frame that indicates group addressed delivery in PCR if it has group addressed DL BUs
    Currently the setting of the Address field of the frame for this mode is TBD
    We propose to use Transmit ID since it is addressed to all WUR STAs
PCR exchanges
  STA wakes up its PCR after receiving the Wake Up frame
  STA reads the DTIM Beacon and the following group addressed DL BUs
  AP shall transmit group addressed BUs after DTIM Beacon and prior to sending individual DL BUs
    But not before PCR transition delay has expired for all WUR STAs expected to receive the BUs
  STA goes to doze state according to its PCR instructions (MD is 0 in group addressed DL BUs frames, etc.)
    After which the STA goes to WUR mode by default (and PCR mode is suspended since the STA is in doze state)
  NOTE: When Counter field increases STA obtains beacon information according to baseline PCR procedure
AP
STA
WUR
frame
AP
STA
Duty Cycle Period
ON Duration
PCR delay
DTIM
Beacon
group addressed frame exchanges
DL BU
…
PCR awake state
WUR awake state
WUR doze state
PCR doze state
DL BU

## Slide 8: TWT-based delivery
WUR exchanges
  STA is in WUR mode (WUR doze outside of ON duration, and WUR awake during ON duration)
  AP only sends Wake Up frame addressed to STA if it intends to wake the PCR of the STA
    The Address field of the frame has WID of STA, GID assigned to STA, or WID that is present in Frame Body
PCR exchanges
  After receiving Wake Up frame, the STA wakes its PCR at the nearest TWT SP
  AP and STA exchange frames via the PCR following the rules in 10.43(TWT), and 27.7 (TWT operation)
    AP sends Trigger frame addressed to the STA if the TWT is a trigger-enabled TWT
    STA sends PS Poll/APSD trigger frame (possibly as a response to the Trigger frame) to indicate that it is in awake state if the TWT is an announced TWT
  AP ensures that STA’s PCR delay has expired prior to sending any frames via the PCR to the STA
  STA goes to doze state according to its PCR instructions (EOSP set to 1, TWT SP ended, etc.)
    Note: The WUR operation is enabled when the STA is in doze state by default
UL
AP
STA
WUR
frame
AP
STA
Duty Cycle Period
ON Duration
PCR delay
Trigger
TWT SP
DL
Ack
PCR awake state
WUR awake state
WUR doze state
PCR doze state

## Slide 9: Proposed clarification for AP behavior
An AP that transmits a wake-up frame addressed to a non-AP STA that satisfies condition 1 shall follow existing PCR operation to deliver individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
  Existing PCR operation is whichever PS operation the STA and AP had agreed to use (e.g., baseline PS, APSD, TWT, etc.)
The AP that intends to schedule a transmission through the PCR for a WUR STA shall schedule it if any of the following conditions is met:
  The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted wake-up frame intended to the non-AP STA has expired
  The non-AP STA has indicated it is in awake state after transmitting a frame through the PCR to the AP
  Note that the transmission is not limited to the individually addressed buffered BU(s)
  Individually addressed buffered BU(s) are delivered at specific times, which are already defined and follow existing PCR rules
An AP that transmits a wake-up frame indicating group addressed buffered BU(s) shall follow existing PCR operation to deliver group addressed buffered BU(s)
  Existing PCR operation is whichever PS operation the STA and AP had agreed to use (e.g., DTIM, FMS, etc.)
The AP shall schedule for transmission of group addressed buffered BU(s) through PCR if the following condition is met:
  The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted wake-up frame indicating buffered group addressed BU(s) of PCR has expired
  Group addressed buffered BU(s) are delivered at specific times, which are already defined and follow existing PCR rules

## Slide 10: Proposed clarification for STA behavior
A non-AP STA that receives a wake-up frame that satisfies condition 1 shall follow existing PCR operation to retrieve individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
  Existing PCR operation is whichever PS operation the STA and AP had agreed to use (e.g., baseline PS, APSD, TWT, etc.) and also follows the wake up timing information that was provided along with the agreed PS operation for the next service period
A non-AP STA that receives a wake-up frame with an indication of buffered group addressed BU(s) shall follow existing PCR operation to receive group addressed BU(s).
  Existing PCR operation is whichever PS operation the STA and AP had agreed to use (e.g., DTIM, FMS, etc.) and also follows the wake up timing information (i.e., the next DTIM TBTT) that was provided along with the agreed PS operation
A non-AP STA that receives a wake-up frame with an indication to check PCR beacon shall follow existing PCR operation to attempt to receive the PCR Beacon information.
  The existing PCR operation is whichever PS operation the STA and AP had agreed to use and also follows the wake up timing information (i.e., the next TBTT) that was provided along with the agreed PS operation

## Slide 11: Proposed clarification for WUR mode
If a non-AP STA is in WUR mode, then [2]:
  The non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the doze state.
  The existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (e.g. TWT, schedule for WNM Sleep Mode) is suspended:
    STA is not required to wake up during the service period if the service period is suspended, except that the STA is expected to wake at the next service period following the existing baseline PCR operation (Note: The STA has indicated its intention to wake at the next service period by simply negotiating the PCR schedule).
    The parameters of the negotiated service period for the non-AP STA’s PCR schedule is still saved by the AP and non-AP STA when the negotiated service period is suspended.
  The non-AP STA may not listen for Beacon frames if the non-AP STA is in PS mode.

## Slide 12: Straw Poll 1
Do you agree to use Transmit ID in WUR Wake-up frames to indicate group addressed delivery in the PCR?

## Slide 13: Straw Poll 2
Do you agree with the amended text in slides 9, 10, and 11?

## Slide 14: Motion 1
Move to use the Transmit ID in WUR Wake-up frames to indicate group addressed delivery in the PCR?

## Slide 15: Motion 2
Move to amend the draft D0.3 with spec text that is inline with the concepts outlined in slides 9, 10, and 11?

## Slide 16: References
[1] 11-17-0575-10-00ba-spec-framework
[2] IEEE802.11ba D0.3