## Slide 1: Procedure for Slot Structure Start Time
Date: 2018-05-08
Authors:
Name | Company | Address | Phone | Email
Saehee Bang | LG Electronics |  |  | saehee.bang@lge.com
JinMin Kim |  |  |  | jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
JinSoo Choi |  |  |  | js.choi@lge.com
SungJin Park |  |  |  | allean.park@lge.com
SunWoong Yun |  |  |  | Sunwoong.yun@lge.com
Sang G. Kim |  |  |  | sanggook.kim@lge.com

## Slide 2: Introduction
In 11ay D1.0, the following texts are described regarding TDD slot structure update.
10.36.6.2.2 SP with TDD channel access
Upon reception of a TDD Slot Structure element corresponding to allocations identified by the Allocation ID subfield value within the element, a DMG STA shall adopt the TDD structure within the element for all the TDD SPs identified by the same Allocation ID subfield value until the time it receives an updated TDD Slot Structure element from the DMG AP or DMG PCP for the allocation. The TDD structure shall be adopted at the time indicated by the value of the Slot Structure Start Time subfield within the element.
9.4.2.267 TDD Slot Structure element
The Slot Structure Start Time subfield indicates the lower 4 octets of the TSF timer at the start of the first TDD SP in which the slot structure takes effect.

## Slide 3: Issues
Currently, it is recommended that DNs (distribution networks) use the same TDD slot structure and update it at the same time if possible since the TDD slot structure are shared among associated CNs and DNs.
For multiple DNs to share the same TDD slot structure and update it at the same time, an updated TDD Slot Structure element should be exchanged among DNs early enough before its update takes effect.
For this, the Slot Structure Start Time subfield should be able to indicate the time of several BIs later.
However, it’s not clear which TDD slot structure is applied during the time
  right after a DMG STA received an updated TDD Slot Structure element till the time indicated by the Slot Structure Start Time in the updated TDD Slot Structure element.

## Slide 4: Proposed method
If the newly updated slot structure element is applied after several BIs rather than the current BI, then the current slot structure must be maintained until “Slot Structure Start time”
  Examples of current assumptions
    According to the current spec , when a slot structure element is received, it is updated.
  Examples of proposed assumptions
    The Slot Structure Time indicates the time rather than the current BI, then the current slot structure must be maintained.
Old slot structure applied
Old slot structure applied
Old slot structure applied
Old slot structure applied
new slot structure applied
BI with TDD slot structure changed
Slot Structure Start Time
( Slot structure change time)
Maintained the current slot structure until Slot Structure Start Time
Received New Slot structure element
Indicates non-current BI time
No slot structure applied
No slot structure applied
No slot structure applied
No slot structure applied
new slot structure applied
Slot Structure Start Time
( Slot structure change time)
Received New Slot structure element
Indicates non-current BI time
Slot structure updated, but not applied. And no slot structure applied
A
B

## Slide 5: Proposed method
TDD Slot Structure elements can be sent over several BIs to ensure that DNs update the TDD slot structure simultaneously.
Followings are proposed text:
  Upon reception of a TDD Slot Structure element corresponding to allocations identified by the Allocation ID subfield value within the element, a DMG STA shall adopt the TDD structure within the element for all the TDD SPs identified by the same Allocation ID subfield value until the time indicated in the Slot Structure Start Time subfield in an updated TDD Slot Structure element it receives an updated TDD Slot Structure element from the DMG AP or DMG PCP for the allocation. When a TDD slot structure is updated, the TDD Slot Structure element can be sent over several BIs. The TDD structure shall be adopted at the time indicated by the value of the Slot Structure Start Time subfield within the element.

## Slide 6: Straw poll
Do you agree to include the text for Slot Structure Start Time proposed in (11-18-0844-00-00ay-Procedure for Slot structure Start Time) to the spec draft?
  Followings are proposed text:
  10.37.6.2.2 SP with TDD channel access
  Upon reception of a TDD Slot Structure element corresponding to allocations identified by the Allocation ID subfield value within the element, a DMG STA shall adopt the TDD structure within the element for all the TDD SPs identified by the same Allocation ID subfield value until the time indicated in the Slot Structure Start Time subfield in an updated TDD Slot Structure element it receives an updated TDD Slot Structure element from the DMG AP or DMG PCP for the allocation. When a TDD slot structure is updated, the TDD Slot Structure element can be sent over several BIs. The TDD structure shall be adopted at the time indicated by the value of the Slot Structure Start Time subfield within the element.

## Slide 7: Reference
[1] Draft P802.11ay_D1.0