## Slide 1: ACK operation in TDD SP
Date: 2018-05-08
Authors:
Name | Company | Address | Phone | Email
Saehee Bang | LG Electronics |  |  | saehee.bang@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
JinMin Kim |  |  |  | jinmin1230.kim@lge.com
JinSoo Choi |  |  |  | js.choi@lge.com
SungJin Park |  |  |  | allean.park@lge.com
SunWoong Yun |  |  |  | Sunwoong.yun@lge.com
Sang G. Kim |  |  |  | sanggook.kim@lge.com

## Slide 2: Introduction
Scheduling for mmWave Distribution Networks was proposed. [1]
We propose an efficient method to transmit the ACK frame

## Slide 3: Recap [1]
According to [1] , a Acknowledgement procedure for the TDD channel access is defined.
10.3.2.10 Acknowledgement procedure
A non-AP and non-PCP STA operating in an SP with TDD channel access (see 10.37.6.2.2) has AckTimeout interval value equal to the duration from the PHY-TXEND.confirm primitive of the current frame to the end of the earliest occurring TDD slot the addressed recipient of the MPDU is assigned to, with access permission of the TDD slot set to simplex TX TDD slot, and with slot category of the TDD slot set to Basic TDD slot, as indicated in the TDD Slot Schedule element (see 9.4.2.268).
A DMG AP or DMG PCP operating in an SP with TDD channel access (see 10.37.6.2.2) has AckTimeout interval value equal to the duration from the PHY-TXEND.confirm primitive of the current frame to the end of the earliest occurring TDD slot the addressed recipient of the MPDU is assigned to, with access permission of the TDD slot set to simplex RX TDD slot, and with slot category of the TDD slot set to Basic TDD slot, as indicated in the TDD Slot Schedule element (see 9.4.2.268).

## Slide 4: Issue
According to the definition in the current draft text, the ACK for the TX TDD slot is transmitted in the earliest simplex RX TDD slot. However, in this case, ACK or Block ACK may not be covered.
  Multiple Single MPDUs are transmitted.
  Multiple management frames requiring ACK are transmitted.
In such a case, a block ACK can not be transmitted, and the ACK frame for multiple TX TDD slot is also not defined.
We propose the efficient ACK procedure to TDD slot assignment

## Slide 5: Proposal : option 1
Option1 is proposed to be able to transmit in the existing ACK frame format. Transmit a single MPDU in the TX TDD slot.
  In all TX TDD slots before simplex RX TDD slot, a single MPDU transmits only once.
    In the earliest RX TDD slot, transmit an ACK frame for this single MPDU.
  There is no change in the data frame transmitted in the TDD RX slot. However, there are restrictions on the TDD slot schedule for ACK transmission,

## Slide 6: Proposal : option 2
Before the RX TDD slot in which the ACK frame can be transmitted, only the following TX TDD slot is performed.
  In all TX TDD slots before simplex RX TDD slot, only segmented MSDUs are transmitted.
    The ACK procedure follows the currently defined segmented MSDU ACK procedure.
  In all TX TDD slots before simplex RX TDD slot, transmit only to control PHY.
    The ACK frame can be transmitted using the control trailer.
  There is a restriction that the data frame transmitted in TDD RX slot must be segmented MSDU. However, the flexibility of the TDD slot schedule is maintained.

## Slide 7: Conclusion
We propose the method to ACK for TDD slots with two option.
  option1 is applicable to all STAs.
  option2 is a method applicable to the EDMG STA.
Since option1 has a limitation on TDD slot scheduling, we prefer to apply option 1 to all STAs, and apply option2 to EDMG STA.

## Slide 8: Straw poll
Which option do you prefer to transmit ACK for the TX TDD slot ?
  Option1 :
    In all TX TDD slots before simplex RX TDD slot, a single MPDU transmits only once.
  Option 2 :
    In all TX TDD slots before simplex RX TDD slot, control PHY or segmented MSDUs are transmitted.

## Slide 9: Reference
[1] Draft P802.11ay_D1.1