## Slide 1: Negotiation for HEz Ranging for Passive Location Support
Date: 2018-05-08
Authors:

## Slide 2: Capability and Negotiation
HEz ranging for passive location shares capability announcement and negotiation procedure with regular HEz ranging.
Need bit for a responder to indicate capability to do HEz ranging for passive location support.
Need bit for initiator/responder to request/grant participation in HEz ranging opportunity for passive location.

## Slide 3: Extended Capabilities Element
Add bit for a STA to indicate capability to do HEz ranging for passive location support in the responder role.

## Slide 4: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | NDP Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | <tbd>
Add bit for requesting/granting to be part of HEz ranging opportunity for passive location support
 | Element ID (255) | Length | Element ID Extension | NGP Parameters | VHTz specific subelement (optional) | HEz specific subelement (optional) | EDMGz Specific subelement (optional)
Octets | 1 | 1 | 1 | 2 | <tbd> | <tbd> | <tbd>

## Slide 5
Straw Poll and Motion

## Slide 6: Straw Poll
We support the following:
Add a bit to HEz ranging negotiation parameters in IFTM/FTMR, to indicate request/grant to participate in an HEz ranging opportunity for passive location support.
The bit would be present in the request from an ASTA taking a role of ISTA and as well the RSTA response.
A request for passive HEz Ranging can be made if the RSTA indicated its support for passive ranging.
The capability shall be indicated in the Extended Capabilities element.
Y: N: A:

## Slide 7: Motion
Move to adopt the following requirements for Passive Location operation, instruct the SFD editor to incorporate it in the SFD and empower the editor to perform editorial changes:
Add a bit to HEz ranging negotiation parameters in IFTM/FTMR, to indicate request/grant to participate in an HEz ranging opportunity for passive location support.
The bit would be present in the request from an ASTA taking a role of ISTA and as well the RSTA response.
A request for passive HEz Ranging can be made if the RSTA indicated its support for passive ranging.
The capability shall be indicated in the Extended Capabilities element.
Y: N: A:

## Slide 8
Thank You!