## Slide 1: Negotiation for HEz Ranging for Passive Location Support
Date: 2018-05-08
Authors:

## Slide 2: Capability and Negotiation
HEz ranging for passive location shares capability announcement and negotiation procedure with regular HEz ranging.
Need bit for a responder to indicate capability to do HEz ranging for passive location support.
Need bit for initiator/responder to request/grant participation in HEz ranging opportunity for passive location.

## Slide 3: Extended Capabilities Element
Add bit for a STA to indicate capability to do HEz ranging for passive location support in the responder role.

## Slide 4: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | NDP Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | <tbd>
Add bit for requesting/granting to be part of HEz ranging opportunity for passive location support
 | Element ID (255) | Length | Element ID Extension | NGP Parameters | VHTz specific subelement (optional) | HEz specific subelement (optional) | EDMGz Specific subelement (optional)
Octets | 1 | 1 | 1 | 2 | <tbd> | <tbd> | <tbd>

## Slide 5
Straw Poll and Motion

## Slide 6: Straw Poll
We support the following:
Add a bit to HEz ranging negotiation parameters in the in IFTM/IFTMR, to indicate request/grant to participate in an HEz ranging opportunity for passive location support.
The bit shall be present in the request from an ASTA, taking on the role of ISTA, as well as in the RSTA response.
A request for HEz Ranging for passive location support can be made by the ASTA/ISTA if the RSTA has indicated capability its support for passive ranging.
The capability shall be indicated in the Extended Capabilities element of the RSTA.
Y: N: A:

## Slide 7: Motion
Move to adopt the following requirements for Passive Location operation, instruct the SFD editor to incorporate it in the SFD under Section 3.2.1 (Protocol Negotiation) and empower the editor to perform editorial changes:
Add a bit to HEz ranging negotiation parameters in IFTM/IFTMR, to indicate request/grant to participate in an HEz ranging opportunity for passive location support.
The bit shall be present in the request from an ASTA, taking on the role of an ISTA, as well as in the RSTA response.
A request for HEz Ranging for passive location support can be made by the ASTA/ISTA if the RSTA has indicated capability its support for passive ranging.
The capability shall be indicated in the Extended Capabilities element of the RSTA.
Y: N: A:

## Slide 8
Thank You!