## Slide 1
Subcarrier Structure for WUR Frames
Date: 2018-05-09
Authors:

## Slide 2: Introduction
TGba has defined and is considering multiple types of WUR frame
  Wake-up frame[1]
    Unicast Wake-up frame which requires a response frame from target STA using its primary connectivity radio
    Multicast Wake-up which does not require a response frame from target STAs and the AP can transmit broad cast/multicast frame after the preparation period
  WUR Beacon[1]
    May include WUR and PCR configuration parameters
  WUR discovery frame[2]
    May advertise BSS information without primary connectivity radio
  Vendor specific WUR frame[3]
    Variable length frame structure was considered
    Based on its purpose, it may require primary connectivity radio to wake-up or not

## Slide 3: 11ba PPDU structure
11ba is considering narrower bandwidth structure for WUR specific PPDU part
  Non-HT preamble with 20MHz is reused before WUR specific PPDU part
  WUR specific PPDU part utilizes 13 subcarriers with subcarrier spacing of 312.5kHz for narrow bandwidth WUR PPDU structure[1]
Narrow bandwidth WUR PPDU may cause mid packet CCA problem because of difference of 7dB power caused by -7dB of bandwidth[4]
  WUR PPDU with 20MHz bandwidth could solve this problem
  Specific subcarrier structure has bees discussed but more is needed (e.g., FDM structure, extended tone structure, dummy tone structure, etc.,)
However, still 7dB power spectral density margin is attractive for transmission range if there are no power spectral density restriction
In this presentation we want to examine this trade-off based on types of WUR frames

## Slide 4: Extended WUR PPDU structure
OFF
ON
ON
ON
OFF
OFF
Full-band WUR PPDU may not cause the CCA problem and WURx could receive the signal with narrow bandwidth because the WUR PPDU is OOK modulated (WUR demodulator is an energy detector not an IFFT demodulator)
Extended tone is also “ON” if the narrow band signal is “ON”, otherwise, extended tone is “OFF”, too
Specific extended tone sequence or WUR Rx bandwidth could be either standard issue or implementation issue
L-preamble
Extended band signal
4MHz WUR signal
Extended band signal
WUR Tx Bandwidth
WUR Rx Bandwidth

## Slide 5: WUR frame requiring PCR operation
Basic wake-up frame – Case I (PCR range ≈ WUR range)
  If the distance between an AP and a STA is shorter than PCR range or WUR range, STA and AP can communicate with no problem. If the distance is larger than the range, the STA cannot be waken up by the wake-up frame
Wakeup Frame
ACK
ACK
PCR Unicast Frame
PCR Response Frame
AP
STA

## Slide 6: WUR frame requiring PCR operation
Basic wake-up frame – Case II (PCR range << WUR range)
  If the distance between an AP and a STA is larger than PCR range but smaller than WUR range, meaningless wake up and transmission occurs
  It causes power inefficiency on WUR STAs
Wakeup Frame
Cannot receive PCR response frame
PCR Response Frame
AP
STA

## Slide 7: PCR procedure after receiving WUR Frame
Basically wake-up packet is considered to ‘wake’ STAs up.
Because of this property, we have agreed with the following statement in the PAR document
  The WUR is a companion radio to the primary connectivity radio and meets the same range requirement as the primary connectivity radio[5]
    In order to avoid cases that STAs wake up but cannot communicate with its PCR
There are 2 other solutions to meet the same range requirement between PCR and WUR
  Use TPC for WUR specific signal part
    Allocate lower transmit power for WUR specific 13 carriers
    Range could be adjusted but CCA problem with legacy STAs cannot solved yet
  Adjust Rx sensitivity of WURx
    No transmit power control for WUR specific 13 carriers but WURx STAs reject the WUR frame if the measured energy of received WUR frame does not exceed a certain higher threshold
    Range could be adjusted but CCA problem with legacy STAs cannot solved yet

## Slide 8: Extended WUR PPDU vs Rx sensitivity control

## Slide 9: Extended WUR PPDU vs TPC

## Slide 10: WUR frame not requiring PCR operation
In addition to basic ‘Wake-up Frame’, 11ba has been developing some WUR procedures using a WUR frame which does not wake up PCR
  Some WUR Frames may not require any PCR procedures of target STAs after the WUR frame transmission
  In this cases, not only transmission range requirement between WUR and PCR is not a priority we should consider but also longer range is meaningful
  The WUR frames may not be transmitted frequently so that the CCA problem situation may hardly occur
    WUR Beacon
    WUR Discovery
    Etc.
Additional indication and complexity are not required on receiver side
  WUR STAs don’t need to know whether the receiving frame is Full-band WUR PPDU or not
  Decoding capability on narrow band signal (4MHz) is mandatory, receiving extended tone is optional
  Specific sequence for extended tones could be either a spec issue or not

## Slide 11: WUR frame not requiring PCR operation
WUR Frame for special purpose
  WUR beacon, WUR discovery and some vendor-specific WUR frames may not require PCR operation after WUR Tx&Rx
  These WUR frames are considered as information carriers or a parameter update indicator frames.
  In many cases, these frames are not transmitted frequently
  Therefore, in order to maximize information delivery rate of these frames, using long range WUR PPDU format is more beneficial even though the long range PPDU format may cause CCA problem
WUR Frame for special purpose
No response and no wake-up
AP
STA

## Slide 12: 2 types of WUR PPDU tones for different usage

## Slide 13: Conclusions
Narrow band signal part of WUR PPDU can cause CCA problem on legacy STAs
However, narrow band WUR PPDU has the advantage of long range information delivery
Long range delivery is suitable for some types of WUR frame that does not require PCR operation
Using full-band WUR PPDU format for normal Wake-up packet and narrow-band(long range) WUR PPDU format for others could be a good solution
Specific wave form generation method is TBD (e.g., Full-band 64FFT + time masking, 32 FFT, etc.)

## Slide 14: References
[1] 11-17-0575-11 “Specification Framework for TGba”
[2] 11-17-1608-00 “WUR Discovery Frame for Smart Scanning”
[3] 11-17-1334-00 “Vendor Specific WUR Frame Follow Up”
[4] 11-17-1426-00 “WUP CCA Problem”
[5] 11-16-1045-09 “A PAR Proposal for Wake-up Radio”

## Slide 15: Straw poll
Which option do you prefer for WUR PPDU tone structure?
  Option 1 : Allow Full-band WUR PPDU structure and leave the specific sequence as an implementation issue
  Option 2 : Allow Full-band WUR PPDU structure and specify the specific sequence
  Option 3 : Do not allow using out-band tones (sub-carriers out of 4MHz)
  Option 4 : None of above
  Abstain