## Slide 1: 802.11ba Architecture Discussion
Date: 2017-02-06
Authors:

## Slide 2: Abstract
This presentation addresses some of the issues that were listed as questions to TGba in a prior ARC session
The intent of this presentation is to provide an overview of 802.11ba
  Based on the overview address some issues that were raised in ARC discussions
  Determine if there are architectural issues, if any that needs to be resolved jointly with TGba
The intent in this presentation is not to propose new features to TGba.
  New ideas/proposals to ba is best addressed when proposed and discussed directly in a TGba session

## Slide 3: Definition(s)
Legacy Power Save Mode(s) as defined in IEEE802.11-2016 function as specified
In addition, when the the AP and the non-AP STA are both WUR-capable,
  The AP and non-AP STA agree on a set of parameters required for WUR operation
    By explicitly exchanging WUR-mode setup frame(s)
  When the non-AP STA transitions to the doze state using mechanism(s) defined in IEEE802.11-2016, enables the non-AP STA wake-up receiver (WURx) capability

## Slide 4: Power Save at non-AP STA (AP is WUR-capable)
Legacy PS Mode (no WUR)` | Legacy PS Mode (WUR-capable) | Notes
Unassociated | Unassociated | 
Associated with an AP | Associated with an AP WUR-mode operation parameters may be determined by exchanging WUR-mode Setup frame(s) | Non-AP STA associates with the AP

## Slide 5: Power Save at non-AP STA (AP is WUR-capable)
Legacy PS Mode (no WUR) | Legacy PS Mode (WUR-capable) | Notes
Non-AP STA in PS mode Non-AP STA Primary Communication Radio (PCR) transitions to doze state and operates as defined in IEEE802.11-2016. | Non-AP STA in PS mode Non-AP STA PCR transitions to doze state and operates as defined in IEEE802.11-2016. Non-AP STA WURx Enabled (WURx ON/OFF defined by WUR duty-cycle (part of WUR-mode* operation parameters) | Non-AP STA enter PS mode using mechanisms defined in IEEE802.11 REVmd D1.0
* WUR Mode does not mean WURx is turned on (WURx ON/OFF is determined by WUR duty cycle parameters).

## Slide 6: Power Save at non-AP STA (AP is WUR-capable)
Legacy PS Mode (no WUR)` | Legacy PS Mode (WUR-capable) | Notes
Non-AP STA in PS mode | Non-AP STA in PS mode | 
 | WURx can wake up PCR when it receives wake-up frame WURx status is implementation specific when non-AP STA goes to active state | AP sends WUR-wake up message to the WURx in the non-AP STA
Non-AP STA in active mode | Non-AP STA in active mode | Non-AP may leave PS mode using mechanisms defined in IEEE802.11-2016

## Slide 7: Related Issues/Questions
Does WUR require the STA to be in PS mode?
  See Slide #5
The STA with a WUR is simply in a different power save mode, ….
  No. It is power save mode as defined in IEEE802.11-2016 with some extensions to leverage the WUR-capability
Hence on wakeup does a STA need to send a PS Poll?
  No. Non-AP STA can use any existing sequence to retrieve data from AP when woken up by the wake-up frame. For example, the sequence of U-APSD, which does not require to send a PS Poll.

## Slide 8: Related Issues/Questions
What is the wake up sequence?
  Non-AP STA can use any existing sequence like PS-Poll sequence or U-APSD sequence, to retrieve data from AP when main radio (PCR) is turned on by the wake-up frame.
Is WUR mode a PS mode?
  No. It is an extension to the PS modes defined in IEEE802.11-2016. Look at slides #4, #5 and #6.
Can you move between different PS modes, including WUR mode?
  WUR mode is not a new PS mode. See slides #4, #5 and #6. Transiting between different PS modes if defined in IEEE802.11-2016 still applies.

## Slide 9: Related Issues/Questions
There is a duty cycle mode for the WUR which can be set for a few ms to several seconds (tbd).
  At the AP the WUR transmission can be looked at as “MCS -1”.
  Duty cycle just means that WURx can be on or off based on a specific pattern.
  WUR uses different modulation scheme from main radio.
  WUR Mode configuration is negotiated through 802.11 management frame (WUR Setup) exchanges.

## Slide 10: Related Issues/Questions
Discovery WUR transmissions and related security concerns
  WUR discovery frame is defined and can be used to discover neighboring APs, when the STA is not associated.
  Security is under development and is not in the current draft.
For the non-AP STA: there are two PHYs but it does not operate like how 802.11ad operates –
  WUR has nothing to do with multiband operation.
  PCR may operate in 5GHz while WUR may be setup in 2.4GHz (or vice versa)
  WUR is in 2.4 and 5 GHz with a different mode of modulation (like how 11ax and 11ac introduce different mode of modulation to 11n).

## Slide 11: Related Issues/Questions
Can the WUR receiver receive a wake up frame on a channel or band other than the one the primary connectivity radio (PCR) is associated on?
  Yes. The band/channel for WUR is determined during the WUR-mode setup.
Is there one MAC for the WUR (non-AP STA receiver) and the PCR?
  WUR STA has only one MAC address. The WURx is capable of receiving frames transmitted using a different modulation scheme. This is exactly like how a legacy STA with one MAC operates in HT, VHT and HE modes

## Slide 12: Related Issues/Questions
Does the WUR have its own MAC?
  WUR STA has only one MAC address. The WURx is capable of receiving frames transmitted using a different modulation scheme. This is exactly like how a legacy STA with one MAC operates in HT, VHT and HE modes

## Slide 13: Open Issue(s)
In the March 2018 meeting there was an issue raised related to the protection (setting NAV correctly) for WUR-frames transmitted by the AP to the non-AP STA (in WUR-mode)
  The legacy preamble is part of the Wake Up frame transmitted by the AP to the non-AP STA (in WUR-mode). Hence all the other receivers should be able to set their NAVs correctly
  Not sure what the concern was
  Need more discussion to understand the issue and determine if there is a ARC dependency