## Slide 1: 802.11ba Architecture Discussion
Date: 2017-02-06
Authors:

## Slide 2: Abstract
This presentation addresses some of the issues that were listed as questions to TGba in a prior ARC session
The intent of this presentation is to provide an overview of 802.11ba
  Based on the overview address some issues that were raised in ARC discussions
  Determine if there are architectural issues, if any that needs to be resolved jointly with TGba
The intent in this presentation is not to propose new features to TGba.
  New ideas/proposals to ba is best addressed when proposed and discussed directly in a TGba session

## Slide 3: Definition(s)
All Power Save Mode(s) as defined in IEEE802.11-2016 function as specified
In addition, when the the AP and the non-AP STA are both WUR-capable,
  The AP and non-AP STA agree on a set of parameters required for WUR operation
    By explicitly exchanging WUR-mode setup frame(s)
  When the non-AP STA transitions to the doze state using mechanism(s) defined in IEEE802.11-2016, enables the non-AP STA wake-up receiver (WURx) capability

## Slide 4: State Diagram
WUR Setup is accomplished by exchanging WUR setup frames between the AP and the non-AP STA
Transition between WUR mode and WUR mode suspend is done using WUR setup frame exchange with action type field set to Enter WUR Mode and Enter WUR Mode Suspend respectively

## Slide 5: Power Save at non-AP STA (AP is WUR-capable)
802.11-2016 defined PS Mode (no WUR)` | 802.11-2016 defined PS Mode (WUR-capable) | Notes
Unassociated | Unassociated | 
Associated with an AP | Associated with an AP | Non-AP STA associates with the AP
 | WUR-Mode Configured | AP and non-AP STA exchange WUR-mode Setup frame. The response status field in the WUR Setup response from the AP is set to Accept
Note: frame exchanges defined in 802.11-2016 are not shown. Only frames exchanges enabling 802.11ba are shown

## Slide 6: Power Save at non-AP STA (AP is WUR-capable)
802.11-2016 defined PS Mode (no WUR) | 802.11-2016 defined Mode (WUR-capable) | Notes
Non-AP STA in PS mode Non-AP STA Primary Communication Radio (PCR) transitions to doze state and operates as defined in IEEE802.11-2016. | Non-AP STA in PS mode Non-AP STA PCR transitions between PS Awake/PS doze sub-states and operates as defined in IEEE802.11-2016. | Non-AP STA enter PS mode using mechanisms defined in IEEE802.11-2016
 | Non-AP STA WURx Enabled (WURx ON/OFF defined by WUR duty-cycle (part of WUR-mode* operation parameters) | Non-AP enters WUR Mode by sending a WUR Setup frame with Action Type field set to WUR Mode
WUR Mode does not mean WURx is turned on (WURx ON/OFF is determined by WUR duty cycle parameters).
.
Note: frame exchanges defined in 802.11-2016 are not shown. Only frames exchanges enabling 802.11ba are shown

## Slide 7: Power Save at non-AP STA (AP is WUR-capable)
802.11-2016 defined PS Mode (no WUR)` | 802.11-2016 defined PS Mode (WUR-capable) | Notes
Non-AP STA in PS mode | Non-AP STA in PS mode | 
 | WURx can wake up PCR when it receives wake-up frame WURx status is implementation specific when non-AP STA goes to active state | AP sends WUR-wake up message to the WURx in the non-AP STA
 |  | Non-AP STA sends a WUR Setup frame with Action Type field set to Enter WUR Mode Suspend
Note: frame exchanges defined in 802.11-2016 are not shown. Only frames exchanges enabling 802.11ba are shown

## Slide 8: Power Save at non-AP STA (AP is WUR-capable)
802.11-2016 defined PS Mode (no WUR)` | 802.11-2016 defined PS Mode (WUR-capable) | Notes
Non-AP STA in active mode | Non-AP STA in active mode | Non-AP may leave PS mode using mechanisms defined in IEEE802.11-2016
Note: frame exchanges defined in 802.11-2016 are not shown. Only frames exchanges enabling 802.11ba are shown

## Slide 9: Related Issues/Questions
Does WUR require the STA to be in PS mode?
  See Slide #5
The STA with a WUR is simply in a different power save mode, ….
  No. It is power save mode as defined in IEEE802.11-2016 with some extensions to leverage the WUR-capability
Hence on wakeup does a STA need to send a PS Poll?
  No. Non-AP STA can use any existing sequence to retrieve data from AP when woken up by the wake-up frame. For example, the sequence of U-APSD, which does not require to send a PS Poll.

## Slide 10: Related Issues/Questions
What is the wake up sequence?
  Non-AP STA can use any existing sequence like PS-Poll sequence or U-APSD sequence, to retrieve data from AP when main radio (PCR) is turned on by the wake-up frame.
Is WUR mode a PS mode?
  No. It is an extension to the PS modes defined in IEEE802.11-2016. Look at slides #4, #5 and #6.
Can you move between different PS modes, including WUR mode?
  WUR mode is not a new PS mode. See slides #4, #5 and #6. Transiting between different PS modes if defined in IEEE802.11-2016 still applies.

## Slide 11: Related Issues/Questions
There is a duty cycle mode for the WUR which can be set for a few ms to several seconds (tbd).
  At the AP the WUR transmission can be looked at as “MCS -1”.
  Duty cycle just means that WURx can be on or off based on a specific pattern.
  WUR uses different modulation scheme from main radio.
  WUR Mode configuration is negotiated through 802.11 management frame (WUR Setup) exchanges.

## Slide 12: Related Issues/Questions
Discovery WUR transmissions and related security concerns
  WUR discovery frame is defined and can be used to discover neighboring APs, when the STA is not associated.
  Security is under development and is not in the current draft.
For the non-AP STA: there are two PHYs but it does not operate like how 802.11ad operates –
  WUR has nothing to do with multiband operation.
  PCR may operate in 5GHz while WUR may be setup in 2.4GHz (or vice versa)
  WUR is in 2.4 and 5 GHz with a different mode of modulation (like how 11ax and 11ac introduce different mode of modulation to 11n).

## Slide 13: Related Issues/Questions
Can the WUR receiver receive a wake up frame on a channel or band other than the one the primary connectivity radio (PCR) is associated on?
  Yes. The band/channel for WUR is determined during the WUR-mode setup.
Is there one MAC for the WUR (non-AP STA receiver) and the PCR?
  WUR STA has only one MAC address. The WURx is capable of receiving frames transmitted using a different modulation scheme. This is exactly like how a legacy STA with one MAC operates in HT, VHT and HE modes

## Slide 14: Related Issues/Questions
Does the WUR have its own MAC?
  WUR STA has only one MAC address. The WURx is capable of receiving frames transmitted using a different modulation scheme. This is exactly like how a legacy STA with one MAC operates in HT, VHT and HE modes

## Slide 15: Open Issue(s)
In the March 2018 meeting there was an issue raised related to the protection (setting NAV correctly) for WUR-frames transmitted by the AP to the non-AP STA (in WUR-mode)
  The legacy preamble is part of the Wake Up frame transmitted by the AP to the non-AP STA (in WUR-mode). Hence all the other receivers should be able to set their NAVs correctly
  Not sure what the concern was
  Need more discussion to understand the issue and determine if there is a ARC dependency

## Slide 16: Open Issues (from ARC review Wed AM1)
Does the non-AP STA when it wakes up via WUR and is in PCR state – what is the PCR timing on wake – how is this maintained?
  WUR Beacons provide enough information for keeping the non-AP STA synchronized with the AP.
  How PCR synchronizes itself using the synchronized state of the WUR is an implementation matter

## Slide 17: WUR Discovery Operation
The WUR discovery frame provides a low power means of discovering APs
  WUR Discovery is a ‘mini-Beacon” containing SSID, BSSID and operating band/channel
Potential for using this mechanism to render ‘background scanning’ more efficient?
  PCR stays associated with the current AP and operates as specified
  WUR listens to WUR discovery frames and compiles a list of APs
Is there a need to define a new 802.11 role
  the device transmitting the WUR frame – is this an AP or a yet to be defined 802.11 entity?

## Slide 18: PCR-State after wake up from WUR mode
Is the non-AP STA after WUR wake, fully awake and immediately asking for its data frames?
Or
Is the non-AP STA after WUR wake, wakes in legacy PS mode?
  Use the state diagram to discuss this

## Slide 19: WUR and PCR association
Are the AP sending WU frames and the associated AP required to be collocated and in communication?
  This is a concern only when the PCR and WUR are operating on different band/channel. In this configuration the non-AP STA’s PCR is associated with a BSS while the WUR is operating outside the BSS (to which the non-AP STA’s PCR is associated). Hence the co-location question.
  Should the mechanism describing how the WUR and the PCR communicate be specified or left as an implementation detail.
If no what information needs to be shared between the APs?

## Slide 20: Security
Are WU frames protected frames? If so, how are security parameters shared between the AP sending WU frames and the associated AP?
  No entry in the SFD for security
  Security aspects of WUR wake up frame are being discussed in TGba currently
  Overview of the Security Strategy
    Use of MIC as a mechanism to determine if the source of the WUR wake up frame is the correct one
How is the security context at the PCR maintained?
  AP refreshed security keys while the non-AP STA was in WUR mode.

## Slide 21: Others Issues
Is WUR supported only for infra-structure topology
  Only BSS?
Mobility
  When the WURx at the non-AP STA (while in WUR mode) does not hear WUR Beacons from the AP, WUR wakes up the PCR
  No roaming support needed since the roaming non-AP STA is no longer in WUR mode once it leaves the range of the AP with which it has setup WUR
Is WUR band agnostic?
  WUR operation only in 2.4/5 GHz bands
  Current Tgba draft only addresses PCR operating in 2.4/5 GHz modes (in HT, VHT or HE modes)