## Slide 1
Discussion on the response of a multicast wake-up frame
Date: 2018-05-07
Authors:

## Slide 2: Introduction
In unicast wake-up radio procedure, the retransmission procedure is based on the response frame as in [1]
  In unicast WUR operation, a STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up frame.
  AP may retransmit the WUR packet when it does not receive the response frame of wake-up packet from STA.
However, for multicast wake-up frame or wake-up frame containing multiple WUR ID, the response procedure is not defined
  When the rule is not defined, STAs may transmit the response frame or data frame, then AP does not know the behavior of the STA
In this contribution, the discussion on several methods for response transmission is proceeded

## Slide 3: WUR operation for multicast wake-up frame
In current SFD, AP may schedule the downlink frame after transmitting the multicast Wake-up frame
  R.4.7.G: If a STA receives a non-individually addressed wake-up frame indicating a group addressed frame through the PCR, the STA may attempt to receive a group addressed frame through PCR
To check the STAs’ state, AP may transmit the short 802.11 frame (e.g. the trigger frame, null frame, BAR etc.)

## Slide 4: The ambiguity of the response frame for wake-up frame
There is no rule for multicast wake-up frame if they transmit the response frame
The ambiguity of response for multicast Wake-up frame may cause confusion in STA
  The rule for response frame is needed
To resolve the ambiguity, two options are possible:
  Use the indication in wake-up frame(GID type, indicator)
  Define the rule not to transmit the response frame

## Slide 5: Option 1: Use the indication in wake-up frame
As in [2], AP may require the response frame in multicast Wake-up case
The STAs receiving the indicator may transmit the response frame of the wake-up frame
  If the response frame is not received, AP may retransmit the wake-up frame

## Slide 6: Option 2: Define the rule not to transmit the response frame
The response frames for multicast Wake-up frame may cause collision
To avoid collision, the STA should not send the uplink frame after the wake-up frame.

## Slide 7: Conclusion
In this presentation, we discussed the ambiguity of response procedure of the wake-up frame in case of the multicast wake-up frame
The rule for response frame for the multicast wake-up frame is needed, to avoid the confusion
Two way for response frame is possible:
  Use the indicator in Wake-up frame
  Set the rule for multicast wake-up frame: The STA should not transmit the uplink frame in case of the multicast wake-up

## Slide 8: Straw poll
Do you agree with the following?
  In group-addressed WUR operation, a STA shall not send a response frame for the WUR wake-up frame, unless it is solicited by AP

## Slide 9: Reference
[1] IEEE 802.11-17/0575r11 “Spec framework”
[2] IEEE 802.11-18/103r3 “Further considerations on WUR frame format”