## Slide 1: BSS Color in NDP Ranging
Date: 2018-05-06
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell |  |  | 
Christian Berger | Marvell |  |  | 
Niranjan Grandhe | Marvell |  |  | 
Yongho Seok | MediaTek |  |  | 

## Slide 2: Recap: BSS Color in 11ax
BSS color in 11ax is used for
  Tow NAV setting,
  Power save,
  Spatial reuse.
The valid BSS Color values are 0 to 63
  BSS color 1 to 63 are used for the transmission (HE PPDU) in the BSS
  BSS color 0 is used for the transmission (HE PPDU) outside of BSS
    The PPDU transmitted between two HE devices that are not in the same BSS

## Slide 3: Issues with 11ax Color Rules in NDP Ranging
The legacy PHY header, HE SIG-A of HE MU PPDU, HE TB PPDU are transmitted in unit of 20MHz channels.
  If a 20MHz channel are shared by both associated and unassociated STAs in HE TB/MU PPDU, the receiver may not be able to decode the PPDU correctly because of the different BSS color values in HE SIG-A from different STAs.
Trigger
Transmitted by STA 2 and STA 3
Transmitted by STA 0 and STA 1

## Slide 4: MU Ranging Solution: Same BSS Color of MU NDP Ranging among Associated STAs and Unassociated STAs
AP sends its BSS color through EFTM Response frame.
Within MU NDP ranging, the unassociated STAs use the BSS Color of the AP which is used by associated STAs.
Trigger
UL NDPs
Trigger
FTM frame
PHY header per BSS color
PHY header per BSS color

## Slide 5: MU Ranging Solution 1.1: Same BSS Color of MU NDP Ranging among Associated STAs and Unassociated STAs (Cont’d)
If an AP changes its BSS color, one of the following methods can be done:
  the AP terminates the MU NDP ranging agreement with the unassociated STAs in the negotiated ranging service period.
  The AP transmits HE BSS Color Change Announcement frame with the updated BSS color in the negotiated ranging service period.
  The AP transmits the EFTM Response with the updated BSS color in the negotiated ranging service period.

## Slide 6: Straw Poll 1
Do you support that in HEz ranging associated and/or unassociated STAs should only use BSS Color announced by AP for HEz transmissions and receptions?