## Slide 1: HEz RTT Location Using Anchor Stations and Client Cooperation
Date: 2018-05-08
Authors:

## Slide 2: Introduction
The purpose of this presentation is to make the case for adding reporting of ‘cross’ RTT measurements in the regular HEz ranging protocol, just as we have for passive location.
The main reason for this is that such cross RTT measurements are useful for enabling anchor client STAs to facilitate (active) locationing.
In addition this enables cooperative client location which can be useful is some cases.

## Slide 3
Generalized HEz Ranging Location Signaling Topology
AP
AP
AP
AS
AS
AS
Types of ranging exchanges:
Between AP and Client to be located.
Between AS and Client to be located.
Between Clients to be located.
Access Point
Clients to be located - Red, gold, and yellow stars
AS - Client Anchor Station

## Slide 4
Example of HEz Ranging Locationing Using Client Anchor Stations

## Slide 5
HEz Ranging Location Using Anchor Client STAs
AP
AP
AP
AS
AS
AS
Access Point
Clients to be located - Red star
AS - Client Anchor Station

## Slide 6: HEz-Ranging Using Anchor Station
DL
NDP
UL
NDP
TF
Responder
AP
Initiator AS
Initiator
Client STA
UL
NDP
UL
NDP
DL
NDPA
Green arrows – Exchanges in HEz ranging protocol today.
Exchanges not in HEz ranging protocol today, except when for support for passive location.
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
iSTA to rSTA
LMR
In this case, because of utilization and time-stamping of the ‘blue’ ranging exchanges, the client STA ranges to both the AP and the AS (a client Anchor station), both with known and shared locations.

## Slide 7: Summary for HEz Ranging Location Using Anchor Client STAs
By enabling measuring and reporting of TOAs of NDPs between client (anchor) STAs in the general HEz ranging protocol, we enable the use client anchor STAs in HEz locationing.
For example, this enables locationing in scenarios with single AP and two anchor client STAs.

## Slide 8
Example of HEz Ranging with Client Cooperative Locationing

## Slide 9
HEz Ranging Signaling Topology with Client Cooperative Locationing
AP
AP
AP
AS
Access Point
Clients to be located - Red, gold, and yellow stars

## Slide 10: HEz-Ranging Using Client Cooperation
DL
NDP
UL
NDP
TF
Responder
AP
Initiator Client STA 1
Initiator
Client STA 2
UL
NDP
UL
NDP
DL
NDPA
Green arrows – Exchanges in HEz ranging protocol today.
Exchanges not in HEz ranging protocol today, except when for support of passive location.
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
iSTA to rSTA
LMR
In this case, because of utilization and time-stamping of the ‘blue’ ranging exchanges, the client STA ranges to AP as well as to each other. With the broadcasting of the time-stamps at the end of the HEz ranging opportunity, all stations, the AP as well as the client STAs all end up with the same time-stamp information. These time stamps enables location based on the ranging to the AP (or APs assuming the above measurement is repeated to multiple APs), and ranging between the clients. This can give increased accuracy, especially in scenarios with few APs.

## Slide 11: General Simulation Procedure
AP1
AP2
Clients
Modeling of imperfections:
0.25 ns stdev Gaussian clock gitter
1 m stdev Gaussian multipath error
All errors independent
AP3
Setup:
3 APs in circle with 15 m radius
8 clients

## Slide 12: Location of 8 Clients Using 3 APs

## Slide 13: Cooperative Location Among 8 Clients Using 3 APs

## Slide 14: Relative Performance with Cooperative Location

## Slide 15: Summary for HEz Ranging with Client Cooperative Locationing
By enabling measuring and reporting of TOAs of NDPs between client STAs in the general HEz ranging protocol, we enable client cooperative locationing.
In scenarios with a small number of APs this can give a performance improvement.
Also, not shown here, but it can enable locationing in scenarios with only two APs.

## Slide 16: Time-Stamp Reporting and Security
Looks not possible to combine RTT cross reporting with PHY security.
However, time-stamps can be reported under MAC security.
Client ISTAs or Client ASTAs time stamps can be securely relayed to the client STAs via the ‘UL LMR’ and ‘DL LMR’ reporting frames.
As we have the ‘DL LMR’ reporting frame prior to the ‘ ‘UL LMR’ reporting frame, a delay would be introduced in the reporting.

## Slide 17
Appendix:
Example Regular RTT and Cooperative RTT Localization Estimation Calculations

## Slide 18: Example RTT Location Estimation Calculations
AP1
AP2
AP3
Client
(x0,y0)
Unknowns:
Client coordinates x0,y0
2 unknowns
Equations:
ToF equations
  ToF1 = R1/c
  ToF2 = R2/c
  ToF3 = R3/c
3 equations
t1
t2
Rij
R1(x0,y0)
In two dimensions with 3 APs:
(x3,y3)
Solve for location, e.g. with Newton iterations – described in following slides.
t4
t3
ToF1=(t2-t1+t4-t3)/2

## Slide 19: Newton’s method for solving non-linear equation
x
x1
x3
x2
etc.
Solve equation:

## Slide 20: Solving of non-linear system of equations
Use Newton’s method for multiple variables:
Iterate according to:
Non linear system of equations:
Linearization:
where
Over-determined non-linear system of equation to solve for Dx:
Least squares solution for iterative step:
- solve for x*

## Slide 21: RTT Location Derivatives
To simplify the equations, measure time in light seconds - the distance light travels in one second.

## Slide 22: Iterative solution for client position (x0,y0) for RTTL
Iterations:
Step calculation. LS solution to:
Note: Time in units of light seconds

## Slide 23: Additional Equations and Derivatives for Cooperative RTT Location Derivatives
To simplify the equations, measure time in light seconds - the distance light travels in one second.
For each pair, (i,j) of clients add equation:
where
The derivatives in the Newton iterations become:

## Slide 24: Iterative solution for client position (x0,y0) for CRTTL
Iterations:
Iterate with Newtons method to find LS solution to set of equations for all users jointly with one RTT ranging equation per client and AP and one per each pair of clients. The equation for a pair of clients is:
Note: Time in units of light seconds

## Slide 25
Thank You!