## Slide 1: BCS Problem Statement
Date: 2018-05-10
Authors:

## Slide 2: Abstract
Requirements and problem statements from the BCS Study Group use case presentations

## Slide 3: Use Cases
Simultaneous transmission of the (same / similar) information from one STA to several STAs
Use Cases
  Downstream Broadcasting (11-17/0999r2)
    Live Streaming
    Advertisements / Billboards (Less Frequently Changed Information)
    Emergency Information
  ARC-IT Broadcast (Cooperative and Intelligent Transportation) (11-18/0711r0)
    Advanced Railroad Grade Crossing
    Broadcast Traveler Information
  Uplink Broadcast (11-18/0875r0)
  Sensor Data Collection (11-17/0999r2)

## Slide 4: Downstream Broadcast
Security:
  Requirements:
    Prevent “fake APs”
    Encrypt downlink broadcast
  Problem:
    With existing schemes: a malicious user can produce fake broadcast frames [11-17/0999r2, slide 9]
  Solution:
    Enhances security [11-17/0999r2, slide 10]
    No constrains if the STA has to be associated or not
Notes: - Add BCS subclause to "General description" clause
Add BCS primitive to "MAC data service" clause
- Modify Association in "MLME SAP interface" in "Layer Management" clause if the key is distributed by Association frame
- Add some IEs in "Information elements" in "Frame formats" clause
- Add some capability bits to somewhere
- Add security description to "Security" clause

## Slide 5: Downstream Broadcast (cont.)
Privacy:
  Requirement:
    Maintain privacy of receivers
  Problem
    Is it one?
  Solution:
    Open authentication & randomized MAC addresses could solve this?
    Not requiring assoc / auth is another solution

## Slide 6: Downstream Broadcast (cont.)
QoS:
  Requirement
    Reduced “loss rate”
  Problem:
    802.11aa GCR (group cast with retries: Unsolicited retries & Block Acks / poll every STA):
      Inefficient channel usage
      Adds delay
      Does not scale with a large number of devices
      Requirement towards large buffers, not only at the AP but also at the receiver (that should be simple / low cost)
    Requires association between STAs and AP (at least for Block ACK part)
      Is this fact itself a (performance / scalability) problem?
  Solution:
    FEC
      This would require changes in silicon
      Silicon changes out of scope per BCS discussion?  discuss if BCS should allow for this very specific enhancement (i.e. _no_ new PHY but FEC hardware enhancements)
      FEC enhancements might be relevant for a lot of other use cases as well; not only broadcasting
    Other ?

## Slide 7: Downstream Broadcast (cont.)
Support for a large number of STAs:
  Requirement
    Support _large_ number of STAs covered by a single AP
  Problem
    Assoc. / Auth put the STA in a state that enables the STA to conduct bidirectional message exchange, though this is not needed for broadcasting
      waste of channel time
      Is this a real problem? Any simulation data for a large number of STAs per use cases?
    Is the 4-way hand-shake power consumption
      Really a problem?
    AP has to maintain state for a large number of STAs
      Limits by TIM (max. 2008 STAs in power safe mode)  check 11ah if this is changed and for “all of .11”
      AP does not know that STAs are broadcast receivers (only)  has to reserve resources such as buffer space etc.
  Solutions:
    Do not require association / authentication for broadcast STAs
    Increase TIM field
    Provide means that a STA could tell the AP (after or during Assoc. & Auth) it is a broadcast / receiver only STA (thus not requiring buffers)

## Slide 8: Downstream Broadcast (cont.)
Downstream reception of broadcast data in an unassociated state
  Requirement:
    Receive (emergency) broadcast information from APs (though the AP normally requires a STA to be associated in order to exchange information)  Reception of data in an “unassociated state”
    Sender of MAC frame should be identifiable (i.e.: “receiver trust sender” should be verifiable)
    Sender does not need to trust receiver, anyone who overhears transmission can receive it
  Problem:
    STA will not have permission to connect to the AP – but should receive broadcast frames
      in case of emergencies
      Containing detailed configuration information to integrate the receiving device in a home / office network
  Solution:
    Allow reception of broadcast frames even without having an association with the AP
    Authentication & encryption of broadcasted data
      Out of scope if at application level
      May be solved between STA and AP (MAC level) by intelligently using private/public keys
    This is provided in general by 802.11 OCB MAC mechanisms (requires small extensions)
      Could be extended to use for non-life-critical data exchange in non-DSRC bands
        At least so far, communication is only allowed if the ToDs/FromDS bits are both zero
        Likely to add some security features to
    Could 11aq / GAS be used / amended as an alternative solution?
    Could EAS be reused / extended?

## Slide 9: ARC-IT Broadcast
Security:
  Requirements:
    Prevent “fake APs”
    Encrypt downlink broadcast not mandatory BUT: authenticity / detection of message corruption needed
    Note: all use cases are NOT life critical
  Problem:
    With existing schemes: a malicious user can produce fake broadcast frames [11-17/0999r2, slide 9 applies as well]
  Solution:
    Enhances security [11-17/0999r2, slide 10]
    No constrains if the STA has to be associated or not
      FILS will help in providing a fast link set-up but
        Then the STA (car) has to know that relevant information is broadcasted  11aq extensions possible
      Allowing 802.11 OCB-based message exchange lots of advantages
        11aq not required
        Even faster as FILS

## Slide 10: ARC-IT Broadcast (cont.)
QoS:
  Requirement
    Reduced “loss rate”
  Problem:
    802.11aa GCR (group cast with retries: Unsolicited retries &Block Acks / poll every STA):
      Inefficient channel usage
      Adds delay
      Does not scale with very large number of devices
      Requirement towards large buffers, not only at the AP but also at the receiver (that should be simple / low cost)
      STAs might stay long enough in coverage of AP to allow use of GCR Block ACK / polling scheme
    Requires association between STAs and AP (at least for Block ACK part)
      STAs (cars) are unlikely to disassociate but are simply leaving the coverage of an AP  timeout of association before buffer can be reallocated  waste of memory at AP
  Solution:
    FEC
      This would require changes in silicon
      Silicon changes out of scope per BCS discussion?  discuss if BCS should allow for this very specific enhancement (i.e. _no_ new PHY but FEC hardware enhancements)
      FEC enhancements might be relevant for a lot of other use cases as well; not only broadcasting
    Other ?

## Slide 11: ARC-IT Broadcast (cont.)
Fast Service Discovery:
  Requirements
    STA has to quickly discover and receive, which service / information is distributed via an AP and to which location this relates
  Problem:
    11aq provides information on service in general (e.g. ITS information available) but not to which location those information relate to or which precise information is provided
    STA is forced to associate (maybe consecutively to several APs to receive actual information in order to decide if it is relevant)
      Too much time due to amount of APs to connect to
      FILS only solves problem for one AP
    Relevant information is distributed via different APs
      STA has to associate / dissociate (in a round robin manner) to receive them all
      Cannot associate to several APs simultaneously
  Solution:
    Enhance / reuse 11aq to provide information that the right AP is immediately selected
      Use 11aq to distribute actual data / information before STA associates
    Employ 802.11 OCB to distribute information in a BSS from the AP to the STA

## Slide 12: Uplink Broadcast
Energy efficient (upstream) delivery of data:
  Requirements
    Reduce energy consumption at STA as much as possible to increase lifetime
    Mainly unreliable transmission of packets (no ACKs) but ACK at MAC level useful for some scenarios
    STA may not stay in coverage of AP while in sleep mode
  Problem
    Packet exchange for association / authentication too demanding in terms of energy consumption
      Why not do it only once and then go into power save?
      Really an issue if Assoc/Auth done for every data packet exchange?
    Suitable power saving features are NOT widely deployed
      Cannot find certified products in the market (to provide BSS Max Idle/Proxy ARP/DMS, STA maintains association and wakes up to transmit data when available) -- why?
      STA required to wake up every DTIM
      STA has to associate every time (as it sleeps and association times out)
      What about 11ah power saving enhancements?
    All existing power saving solutions assume that the STA resides with a single AP; if the STA is moving (and hence frequently leaving an APs coverage – relation between sleep time and time within AP coverage), all existing schemes do not work as the build upon having an established association between AP and STA
  Solution
    Single, self-contained data frame sent before association, but proving similar trust / security according to the requirements
    Extending 802.11 OCB could be one approach

## Slide 13: References
11-17/0999r2
11-18/0711r0
11-18/0875r0