## Slide 1: Baseband feedback for hybrid MU MIMO beamforming
Date: 2018-05-16
Author:

## Slide 2: Introduction
11ay supports hybrid MU MIMO beamforming
11ay defines a 2-stage training (in Section 10.38.9.2.4 Hybrid beamforming for SU-MIMO and MU-MIMO)
  Applying Digital beamforming sounding to enable further separating STAs in spatial domain after applying analog beamforming training.
This presentation considers the digital beamforming matrix feedback with impact of analog beamforming.
STA can reduce digital beamforming matrix feedback overhead by reporting CSI involving partial of AP’s TX antennas.

## Slide 3: Recap: Hybrid beamforming for MU-MIMO defined in 11ay*
The hybrid beamforming protocol enables the determination of the baseband beamformer based on the DMG antenna configuration selected as a result of the MU-MIMO beamforming protocol.
Apply one of MU-MIMO transmission configurations for MIMO sounding
*in 11ay Section 10.38.9.2.4 Hybrid beamforming for SU-MIMO and MU-MIMO

## Slide 4: Impacts of analog beamforming
After analog training, AP can get a group of STAs with the a set of sectors/AWVs （analog beams） which can enhance signal and suppress interference.
  For some co-located STAs (e.g. STA3 and STA4 in figure), AP can not differentiate them via analog beamforming. AP can mitigate inter-STA interference by further using digital beamforming.
  For some separated STAs(e.g. STA3 and STA1 in figure), they will not be interfered by each other’s sector/antennas (e.g. sector 3 from antenna 3, sector 1 from antenna 1).

## Slide 5: Issue in digital beamforming feedback for MU MIMO
For AP with Nt Tx antennas and STA with Nr Rx antennas, full dimension channel state information is as a matrix of size Nrx x Ntx.
  E.g. 1x4 if STA3 has 1 Rx antenna or 2x4 if STA3 has 2 Rx Antennas and supports 2 streams in Fig.5
However, when a STA is not covered by some Tx antennas, the CSI feedback can be compressed.
  Only the partial dimension CSI (between STA’s rx antenna and AP’s tx antennas, using sectors in current MU-MIMO transmission configuration) is needed.
  E.g. matrix size reduced to 1x2 (Nrx x Ntx) or 2x2 for STA3, by reporting channel coefficients from AP’s Tx Ant3 and Tx Ant4 to STA3.
Fig.5 MIMO CSI
AP has 4 RF chains and 4 antennas

## Slide 6: Feedback overhead (Givens method as an example)
11ay MIMO BF feedback contains lots of angles generated by Givens method.[1]
  Feedback overhead increases dramatically with matrix size.
Consider the example in last page
  STA3 which supports 1 spatial stream originally needs to feedback V of size 4x1 (Nr x Nc) with 6 angles, when AP has 4 antennas. With proposed method, since antenna 1 and 2 are not pointing at STA3, STA3 can feedback V of size 2x1 (Nr x Nc) with 2 angles. 67% saving!
  STA3 which supports 2 spatial streams originally needs to feedback V of size 4x2 (Nr x Nc) with 10 angles, when AP has 4 antennas. With proposed method, since antenna 1 and 2 are not pointing at STA3, STA3 can feedback V of size 2x2 (Nr x Nc) with 2 angles. 80% saving!
80% saving if STA3 supports 2 streams
67% saving if STA3 supports 1 stream

## Slide 7: Digital beamforming matrix feedbacks
Opt.1 STA selects the Tx Antennas to be included in MIMO BF Feedback
  Step 1) STA measures MIMO channel.
  Step 2) STA selects the Tx antennas to be included in MIMO BF Feedback. STA uses TX Antenna Mask field (a 8-bit bitmap) to indicate which Tx antennas are selected.
    CSI from Tx antenna with trivial impact can be not included. Specific algorithm for antenna selection is implementation depended, e.g. based on SNR or based on SINR.
  Step 3) Digital beamforming matrix feedback size is reduced. The weights in beamforming matrix is for the tx antennas selected in the TX Antenna Mask.

## Slide 8: Digital beamforming matrix feedbacks
Add Tx Antenna Mask subfield to MIMO Feedback Control element proposed in [1]
Illustration, e.g. reduce 4x1 (Nr x Nc) to 2x1
Add Tx Antenna Mask subfield:
8-bit with each bit to indicate whether a corresponding Tx antenna’s beamforming matrix element has been included in Digital Beamforming Feedback information field of Digital BF feedback elements

## Slide 9: Digital beamforming matrix feedbacks
Opt.2
  Step 1) AP selects STAs for each of its Tx antennas. User Mask field in MIMO Selection Control frame indicates if STA is selected by a Tx antenna or not. Thus, a STA will involve with a subset of TX Antennas.
  Step 2) STA measures MIMO channel.
  Step 3) The STA includes CSI from this subset of in digital beamforming matrix feedback. Thus, no explicit Tx Antenna Mask field is needed.

## Slide 10: Comparison of digital beamforming matrix feedbacks
Opt.1 STA uses TX Antenna Mask field in digital beamforming matrix feedback. Thus, the weights in beamforming matrix is for the tx antennas selected by the TX Antenna Mask.
  Low feedback overhead
  STA can include the tx antenna which does not have this STA in its User Mask. It provides flexibility for STA. When any tx antenna which does not have this STA in its User Mask cause interference to the STA, the STA can report its CSI and enable AP to use digital beamforming to cancel interference.
Opt.2 STA uses TX Antenna Mask field in digital beamforming matrix feedback. Thus, the weights in beamforming matrix is for DMG AP’s tx antennas which have this STA in their User Mask.
  Low feedback overhead
  Not as flexible as opt.1.
Opt.3 STA provides digital beamforming matrix feedback for all Tx Antennas.
  High feedback overhead
  Always provide full dimension channel info

## Slide 11: Performance Evaluations
DL MU MIMO with 1 AP and 3 STAs
  Each STA has one omni antenna with H and V polarizations
  AP has 3 PAA (8x16=128 elements per array) antennas with H and V polarizations
  3 STAs. Each STA has 2 streams. 6 Spatial Streams in total
11ay QD Hotel Lobby LoS channel
In opt.2, STA can’t report CSI for some Tx antennas which cause significant interference but do not have this STA in their User Masks
Opt.1 has significant feedback saving while keep almost the same rate performance as full feedback (Opt.3).
Chart: Mean Number of Angles in Feedback
| N_tx_ant =6 | N_tx_ant =8
Opt.1 | 8.9773 | 12.773
Opt.2 | 2 | 2
Opt.3 | 18 | 26
Fig.1 N_tx_ant=6 (3 PAA with H+V)
Fig.2 N_tx_ant=6 and 8 (3 and 4 PAAs with H+V)
50% saving
52% saving

## Slide 12: Summary
This presentation considers the digital beamforming matrix feedback with impact of analog beamforming.
STA can reduce digital beamforming matrix feedback overhead by reporting CSI involving partial of AP’s TX antennas:
  By adding Tx Antenna Mask field in Digital BF Feedback Control field of MIMO feedback control element in MIMO BF feedback frame

## Slide 13: Straw Poll
Do you agree to accept the text modifications proposed in 11-18/1035r1 into the next version of 11ay draft standard?
Y/N/A

## Slide 14: Reference
[1] 11-18-0441-02-00ay-cr-on-hybrid-beamforming-feedback
[2] 11-18-0503-00-00ay-digital-bf-feedback-format.pptx
[3] 11-18-0442-00-00ay-differential-feedback-for-compressed-beamforming.pptx
[4] 11-18-0192-01-00ay-hybrid-beamforming-feedback-in-802-11ay.pptx

## Slide 15: Appendix: Calculation of PPDU Duration Overhead
We assume two MCS level: Control-PHY and SC- MCS2
  The calculation of feedback PPDU Transmission Duration considers size of PHY preamble, MAC Header, BRP Action frame elements, MIMO control field (assume VHT-like) and compressed beamforming feedback subfield (assume VHT-like)
SC-MCS2: LDPC-1/2, pi/2-BPSK | Number of Selected Tx Antennas | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | Feedback PPDU Duration(ns) | 3564 | 5309 | 7055 | 8800 | 10545 | 12291 | 14036
 | Time Ratio | 100% | 149% | 198% | 247% | 296% | 345% | 394%
Control PHY | Number of Selected Tx Antennas | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | Feedback PPDU Duration(ns) | 44218.18 | 93090.91 | 141963.6 | 190836.4 | 239709.1 | 288581.8 | 337454.5
 | Time Ratio | 100% | 211% | 321% | 432% | 542% | 653% | 763%
If 2 out of 8 Tx Antennas involving this STAs, there is 4x saving (significant).

## Slide 16: Appendix: MIMO BF Selection in analog beam training
AP announces MU grouping results via MIMO BF Selection frame(s)
  A Group User Mask is provided for each Tx Antenna
  Some STAs (e.g. STA1 and STA2 in Fig.3) can be well separated via analog Tx beams while other STAs (e.g. STA3 and STA4 in Fig.3) needs both analog and digital beamforming to reduce inter-STA interference.
    User Mask for Antenna 2 in MIMO Selection Control frame does not include STA3
    User Mask for Antenna 3 and 4 in MIMO Selection Control frame includes STA3
AP’s analog beam from antenna 2 (sector 2) has trivial impact on STA3
Fig.3 MU group
Fig.4 MIMO Selection frame in 11ay D1.0