## Slide 1: Discussion on WUR (802.11ba) States
Date: 2018-07-06
Authors:

## Slide 2: Abstract
This contribution provide a first draft state diagram for the 802.11ba non-AP STA and some supporting discussion.
r1: provides alterative drafts of the state diagram and supporting discussion based on discussion and listed references.

## Slide 3: Assumptions (1/2)
The PS mode (this includes both legacy PS mode configuration and WUR mode configuration) is established during association or with a frame exchange between the non-AP STA and its associated AP when the STA is in the active state or Awake state.
After PS mode parameters are agreed the non-AP STA may move into a PS mode by sending a frame to the AP with the Power Management subfield of the Frame Control field set to 1 and then receiving an ACK of the frame from the AP.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the non-AP STA: e.g. the AP will buffer frames and notify the non-AP STA as specified for the configured PS mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the non-AP STA’s “ability” to move into a low power state of: Doze, WUR Awake or WUR Doze.
The non-AP STA may change its state to Active at any time by sending a frame to the AP with the Power Management subfield is set to 0.

## Slide 4: Assumptions (2/2)
The non-AP STA in WUR PS mode may change its PS mode to the pre-configured “legacy” PS mode by sending a suspend WUR mode frame to the AP with the Power Management subfield set to 1, which is ACKed.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the non-AP STA: e.g. the AP will buffer frames and notify the non-AP STA as specified for the configured “legacy” PS mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the non-AP STA’s “ability” to move into a low power state of Doze.
The non-AP STA with a negotiated WUR PS mode which has suspended the WUR mode may return to the negotiated WUR mode by sending a resume WUR mode frame to the AP with the Power Management subfield set to 1, which is ACKed.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the non-AP STA: e.g. the AP will buffer frames and notify the non-AP STA as specified for the WUR PS mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the non-AP STA’s “ability” to move into a low power states of WUR Awake and WUR Doze.

## Slide 5: Therefore there are Six Allowed Non-AP STA States:
UnAssociated
  STA is active – PPDUs can be received and transmitted – infrastructure BSS services are not available.
Associated
  STA is active – PPDUs can be received and transmitted – infrastructure BSS services are available.
“legacy PS Mode”
  Awake
    STA PRC is active and associated – PPDUs can be received and transmitted.
  Dose
    STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
“WUR Mode”
  WURx Awake
    STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
    WUR is active, WUR PPDUs can be received
  WURx Dose
    STA PRC is not active, but is still associated – PPDUs can not be received or transmitted.
    WUR is not active, WUR PPDUs can not be received

## Slide 6: Changing State of A Non-AP STA
Unassociated can go to: Associated via association.
Associated can go to: Unassociated via disassociation, a different Associated State via reassociation. If configured an associated STA can also go to Power Save Mode or WUR mode and move to Awake State, Doze State, WURx Awake State, or WURx Doze State.
Awake can go to: Dose as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
Dose can go to: Awake as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
WURx Awake can go to: WURx Doze via the configured WUR mode. If a WUR wakeup frame is received move to Associated, and an WUR STA can suspend WUR mode and move to Awake, or Doze.
WURx Doze can go to: WUR Awake as allowed by the configured WUR mode
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 7: AP Expected Behavior for each non-AP STA State
Unassociated: An AP can receive frames from any non-AP STA.
Associated: An AP can receive and send frames from/to the non-AP STA and provides infrastructure services.
Awake: An AP assumes the STA can receive and send frames with the AP.
Dose: An AP assumes the STA cannot receive frames from the AP, and the AP buffers the traffic to the STA.
WURx Awake: An AP assumes the STA WURx can receive a WUR wake up frame and that the STA will signal the AP once it is in associated or awake state. The AP also assume the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
WURx Doze: An AP assumes the STA WURx can not receive a WUR wake up frame. The AP also assume the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 8: WUR State Diagram Proposal-Hamilton
from: [1]

## Slide 9: WUR State Diagram Proposal-Alternate based on [1],[2],[3]

## Slide 10: References
IEEE 802.11-18/1016r2: “WUR State Diagram Proposal – Hamilton”
E-mail from the reflector from Mika Kasslin “Re: [STDS-802-11-TGBA] Updated WUR architecture and state machines uploaded” 2018-07-05
IEEE 802. 11-18/1098r0: “ARC SC Teleconference Minutes June 21 2018”