## Slide 1: Agenda for IEEE 802.11 Coexistence SC meeting in San Diego in July 2018
11 July 2018
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Welcome to the 7th F2F meeting of the Coexistence Standing Committee in San Diego in July 2018
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
    To discuss issues related to the 3GPP RAN1 request to IEEE 802.11 WG to adopt an ED of -72dBm
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018), Warsaw (May 2018) and will meet twice this week
    Wed PM1
    Thu PM1

## Slide 3: The first task for the Coexistence SC today is not to appoint a secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …

## Slide 4: The Coexistence SC will review the official IEEE-SA patent material for pre-PAR groups

## Slide 5: The Coexistence SC hoc will operate using accepted principles of meeting etiquette
  IEEE 802 is a world-wide professional technical organization
  Meetings shall be conducted in an orderly and professional manner in accordance with the policies and procedures governed by the organization
  Individuals shall address the “technical” content of the subject under consideration and refrain from making “personal” comments to or about others

## Slide 6: The Coexistence SC will review the modified “Participation in IEEE 802 Meetings” slide
Participation in any IEEE 802 meeting (Sponsor, Sponsor subgroup, Working Group, Working Group subgroup, etc.) is on an individual basis
  Participants in the IEEE standards development individual process shall act based on their qualifications and experience (IEEE-SA By-Laws section 5.2.1)
  IEEE 802 Working Group membership is by individual; “Working Group members shall participate in the consensus process in a manner consistent with their professional expert opinion as individuals, and not as organizational representatives”. (sub-clause 4.2.1 “Establishment”, of the IEEE 802 LMSC Working Group Policies and Procedures)
  Participants have an obligation to act and vote as an individual and not under the direction of any other individual or group. A Participant’s obligation to act and vote as an individual applies in all cases, regardless of any external commitments, agreements, contracts, or orders
  Participants shall not direct the actions or votes of any other member of an IEEE 802 Working Group or retaliate against any other member for their actions or votes within IEEE 802 Working Group meetings, (IEEE-SA By-Laws section 5.2.1.3 and the IEEE 802 LMSC Working Group Policies and Procedures, subclause 3.4.1 “Chair”, list item x)
By participating in IEEE 802 meetings, you accept these requirements. If you do not agree to these policies then you shall not participate

## Slide 7: The Coexistence SC will consider a proposed agenda for San Diego
Proposed Agenda
  Bureaucratic stuff, including approving minutes
  What is happening this week? (in no particular order)
    Scope of IEEE 802.11 Coexistence SC (a reminder)
    Relationships
      Review recent ETSI BRAN meeting results
      Review recent 3GPP RAN1 activities
      Discuss possibility of a coexistence workshop (and/or LS) with 3GPP
      Follow up on WFA’s recent LS to 3GPP RAN4
      …
    Technical issues
      Adaptivity in EN 301 893
      Blocking energy in ETSI BRAN
      “Paused COT” interpretation in EN 301 893
      Greenfield coexistence
      …
Additional agenda items are requested from all interested stakeholders

## Slide 8: The Coexistence SC will consider a proposed agenda for San Diego
Proposed Agenda
    …
    Other issues
      Next ETSI BRAN meeting
      …
  Other business
Additional agenda items are requested from all interested stakeholders

## Slide 9
  Scope of IEEE 802.11 Coexistence SC

## Slide 10: The agreed Coexistence SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 11: Coexistence SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 12
  Agenda items
  Review of recent ETSI BRAN meeting

## Slide 13: The Coex SC will hear reports of the ETSI BRAN meeting held in June 2018
  The last meeting of ETSI BRAN was held in June 2018
    Dates: 18-21 June 2018
    Location: Sophia Antipolis
  The Coex SC will hear a full report of the meeting particularly on issues related to:
    Timeline
    Adaptivity
    Paused “COT” feature
    Blocking energy

## Slide 14
  Agenda items
  Review of recent ETSI BRAN meeting
  Timeline

## Slide 15: A revision of EN 301 893 is probably needed by about mid 2019, or Notified Bodies will need to be used
  A primary driver of the Coex SC’s interest in revising EN 301 893 is to ensure that 802.11ax based equipment:
    Can be sold in Europe at the earliest possibility
    Using traditional Wi-Fi PD/ED mechanisms and thresholds
    To ensure fairness with W-Fi and other technologies
  It is believed that early draft 802.11ax equipment will start hitting the market in mid 2019
  This suggests the new revision of EN 301 893 is needed at about that time to ensure an unimpeded market
    “Plan B” is for vendors to go to a Notified Body (at a cost), probably using stable drafts of the proposed revision of EN 301 893

## Slide 16: There is quite a lot of work to be completed before EN 301 893 is done!
  Adaptivity is not the only topic that needs to be addressed in the revision of EN 301 893
  The ETSI BRAN Chair has noted that the EC will probably not approve & publish any revision of EN 301 893 unless it includes:
    Receiver Sensitivity requirements
    Maybe Adjacent Channel Selectivity requirements
    Tests for new/revised requirements
  At this time, there have not been any serious discussions in ETSI BRAN yet on the additional rx requirements

## Slide 17: It appears the earliest EN 301 893 can be published is Sept 2019 if the content finished in Dec 2018
  Assume EN 301 893 content finished in December 2018
    Probably an enthusiastic assumption!
  Best case schedule is Sept 2019 (based on ETSI BRAN Chair’s estimate)
    15 Dec 2018: BRAN approves for ENAP
    15 Jan 2018 – 15 April 2019: ENAP (90 days)
    16 May 2019: BRAN resolution meeting
    15 Jun 2019 – 15 Aug 2019: National vote (60 days)
    15 Sep 2019: Publication by ETSI
    ???: Publication by the EC
  Therefore, it is likely that early products will be using the Notified Body route

## Slide 18
  Agenda items
  Review of recent ETSI BRAN meeting
  Adaptivity

## Slide 19: IEEE 802.11 WG sent a LS to ETSI BRAN in May 2018 in relation to the adaptivity clauses in EN 301 893
  At the meeting in Warsaw in May 2018, IEEE 802.11 WG approved a LS to ESTI BRAN supporting a compromise for the adaptivity clause
    The LS is in 11-18-0708-04 (uploaded as BRAN(18)098003)
  The LS supported the adaptivity mechanism previously proposed in a LS in 11-18-0586-01 (uploaded as BRAN(18)097012), but with two documented motivations
    The motivation being documented as “market reality”
    An agreement that there should be future science based investigation of coexistence that may lead to future changes to EN 301 893

## Slide 20: ETSI BRAN considered an 802.11 WG aligned adaptivity proposal for in EN 301 893 from four Wi-Fi companies
  Broadcom, Intel, Cisco & HPE submitted a revised proposal for refining the adaptivity clause in EN 301 893 in June 2018
    See BRAN(18)098005 (embedded with permission)
    Previous version was BRAN(18)097004/5
  The revised proposal from Broadcom, Intel, Cisco & HPE was aligned with the IEEE 802.11 WG LS from May 2018, quoting it extensively
    Any technology can use the traditional Wi-Fi ED/PD mechanisms & thresholds
    Any technology can use ED-only mechanism with threshold of -72 dBm (varies up to -62dBm as lower tx powers used)
  The proposal allows 802.11ax (& EHT, etc) to continue use the traditional PD/ED approach in many cases, but also allows the use of ED-only for:
    Specialist scenarios, eg stadiums
    802.11ax style spatial reuse, albeit with a lower ED threshold
    The situation if evidence shows everyone is better off using the ED-only mechanism & threshold (Ericsson’s simulation conclusions)

## Slide 21: ETSI BRAN considered an alternative compromise adaptivity proposal from Ericsson in June 2018
  Ericsson presented an alternative adaptivity proposal in June 2018 based on an assertion that it was previously agreed in ETSI BRAN that 802.11ax would use ED-only mechanism/thresholds
    See BRAN(18)098009
  Ericsson’s compromise adaptivity proposal:
    Defined an “exception” for 802.11a/n/ac/ax to allowed them to use traditional ED/PD mechanism/thresholds
    Was unclear if 802.11a/n/ac/ax were able to use ED-only mechanism/threshold
    Forced 802.11 beyond 11ax and non-802.11 devices to use ED-only mechanism/threshold
  It was proposed that the compromise only be adopted if stakeholders agreed that 802.11ax would be the last exception
    The impact if this condition was not accepted was that all new 802.11a/n/ac/ax equipment in Europe would be forced to use the ED-only mechanism/threshold

## Slide 22: ETSI BRAN discussed the adaptivity issue at length in June 2018 before coming to consensus
  It was agreed by all after extensive discussion that 802.11ax should be able to use the traditional PD/ED mechanisms
  It was also generally agreed that 802.11 should be able to use the ED-only mechanism (at -72dBm) if desired
  The main open issue was whether 802.11ax would be the last “exception” allowed to use the PD/ED mechanism/threshold
    Some argued that it was agreed 802.11ac was the last “exception” when developing the current version of EN 301 893, and allowing 802.11ax is a compromise
    Others argued that a restriction on the use of the PD/ED mechanism/threshold needs to be justified by ED-only deployment experience, which does yet exist
    It was also noted that the proposed reference to 802.11ax D3.0 in EN 301 893 was not allowed under ETSI rules; the reference to a draft and the fact that D3.0 draft would not available after D4.0 was approved are the problems

## Slide 23: ETSI BRAN discussed the adaptivity issue at length in June 2018 before coming to consensus
  The inability for the group to come up with an acceptable way to specify 802.11ax in EN 301 893 before it was ratified meant the IEEE 802.11 WG aligned adaptivity proposal was the only viable alternative
    The ETSI BRAN Chair also noted that it was inappropriate for ETSI BRAN today to be constrained by an alleged ETSI BRAN agreement two years ago
  It was also generally agreed that it would be very useful for industry to gather deployment based evidence to allow a future ETSI BRAN to refine the adaptivity rules in the future
    ED-only
    ED/PD
    Mixed ED-only & PD/ED
  While the IEEE 802.11 WG aligned adaptivity proposal was accepted by consensus because of objections by Ericsson L.M. to include the text at this time in the draft, the text will be included with square brackets

## Slide 24: Some draft adaptivity text was agreed by ETSI BRAN
Clause 4.2.7.3.2.5 in revised EN 301 893
Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment. Equipment shall not change the ED Threshold Level (TL) for a contiguous period of at least 60 s. The ED Threshold Level (TL) is expressed assuming a 0 dBi receive antenna.
The ED Threshold Level (TL) shall either be proportional to the equipment's maximum transmit power (PH):
For PH ≤ 13 dBm: TL = -75 dBm/MHz
For 13 dBm < PH < 23 dBm: TL = -85 dBm/MHz + (23 dBm - PH)
For PH ≥ 23 dBm: TL = -85 dBm/MHz
Or, if the equipment determines per IEEE 802.11-2016 [9], clause 17.3 that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
Introductory text cleaned up

## Slide 25: Some draft adaptivity text was agreed by ETSI BRAN
Clause 4.2.7.3.2.5 in revised EN 301 893
Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment. Equipment shall not change the ED Threshold Level (TL) for a contiguous period of at least 60 s. The ED Threshold Level (TL) is expressed assuming a 0 dBi receive antenna.
The ED Threshold Level (TL) shall either be proportional to the equipment's maximum transmit power (PH):
For PH ≤ 13 dBm: TL = -75 dBm/MHz
For 13 dBm < PH < 23 dBm: TL = -85 dBm/MHz + (23 dBm - PH)
For PH ≥ 23 dBm: TL = -85 dBm/MHz
Or, if the equipment determines per IEEE 802.11-2016 [9], clause 17.3 that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
Old option 2: ED-only

## Slide 26: Some draft adaptivity text was agreed by ETSI BRAN
Clause 4.2.7.3.2.5 in revised EN 301 893
Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment. Equipment shall not change the ED Threshold Level (TL) for a contiguous period of at least 60 s. The ED Threshold Level (TL) is expressed assuming a 0 dBi receive antenna.
The ED Threshold Level (TL) shall either be proportional to the equipment's maximum transmit power (PH):
For PH ≤ 13 dBm: TL = -75 dBm/MHz
For 13 dBm < PH < 23 dBm: TL = -85 dBm/MHz + (23 dBm - PH)
For PH ≥ 23 dBm: TL = -85 dBm/MHz
Or, if the equipment determines per IEEE 802.11-2016 [9], clause 17.3 that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
Old option 1: PD/ED

## Slide 27: Some draft adaptivity text was agreed by ETSI BRAN
Clause 4.2.7.3.2.5 in revised EN 301 893
Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment. Equipment shall not change the ED Threshold Level (TL) for a contiguous period of at least 60 s. The ED Threshold Level (TL) is expressed assuming a 0 dBi receive antenna.
The ED Threshold Level (TL) shall either be proportional to the equipment's maximum transmit power (PH):
For PH ≤ 13 dBm: TL = -75 dBm/MHz
For 13 dBm < PH < 23 dBm: TL = -85 dBm/MHz + (23 dBm - PH)
For PH ≥ 23 dBm: TL = -85 dBm/MHz
Or, if the equipment determines per IEEE 802.11-2016 [9], clause 17.3 that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
Ref to 802.11a preamble

## Slide 28: Some draft adaptivity text was agreed by ETSI BRAN
Clause 4.2.7.3.2.5 in revised EN 301 893
Equipment shall consider a channel to be occupied as long as other RLAN transmissions are detected at a level greater than the ED Threshold Level (TL). The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of all Operating Channels used by the equipment. Equipment shall not change the ED Threshold Level (TL) for a contiguous period of at least 60 s. The ED Threshold Level (TL) is expressed assuming a 0 dBi receive antenna.
The ED Threshold Level (TL) shall either be proportional to the equipment's maximum transmit power (PH):
For PH ≤ 13 dBm: TL = -75 dBm/MHz
For 13 dBm < PH < 23 dBm: TL = -85 dBm/MHz + (23 dBm - PH)
For PH ≥ 23 dBm: TL = -85 dBm/MHz
Or, if the equipment determines per IEEE 802.11-2016 [9], clause 17.3 that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
Open for discussion

## Slide 29
  Agenda items
  Review of recent ETSI BRAN meeting
  Adaptivity text final tweaks?

## Slide 30: The Coex SC has a short time to suggest any final tweaks to the adaptivity text in EN 301 893
  Since the ETSI BRAN meeting in June 2018, many stakeholders have had a chance to reflect on the outcome
  The new adaptivity text for EN 301 893 was put together by an ad hoc in real time and most people seem to be happy with it
    There have been no complaints so far on the ETSI BRAN e-mail reflector
  Given the difficulty of getting to this point of (almost) consensus and the importance of finishing soon, any final tweaks need to be minor and agreed soon

## Slide 31: A suggestion has been made to clarify an ambiguity in the revised adaptivity clause
  A stakeholder (not the Chair) has commented that the language is ambiguous:
    The current text appears to suggest that the referenced ED threshold is used only when a preamble is actually determined, …
    …while the intent is that it can be used when a process is active to determine preambles.
  The stakeholder suggested a minor tweak that clarifies the assumed intent
    The changes attempt to reflect that, but let me know what you think.
  Are there any comments or objections?
Clause 4.2.7.3.2.5 in revised EN 301 893
…
Or, if the equipment uses determines per IEEE 802.11-2016 [9], clause 17.3 to determine that the channel is occupied, the ED Threshold Level (TL) shall be independent of the equipment's maximum transmit power (PH):
TL = -75 dBm/MHz
…

## Slide 32: A suggestion has been made to clarify an ambiguity in the multi-channel part of the revised adaptivity clause
  A stakeholder (not the Chair) has commented that the language is ambiguous:
    Wi-Fi multi-channel operation has multiple operating channels, but I think the intent is that the ED threshold applies to each operating channel individually
  The stakeholder suggested a minor tweak that clarifies the assumed intent
    Should it perhaps read as follows: (see panel)
  Are there any comments or objections?
Clause 4.2.7.3.2.5 in revised EN 301 893
…
The ED Threshold Level (TL) is integrated over the total Nominal Channel Bandwidth of each all Operating Channels used by the equipment
…

## Slide 33: A suggestion has been made to make it clear operation is on a per channel basis
  An extension of the previous comment is that the limit on swapping between the two modes of operation should apply on a channel by channel basis
  This means that a particular device could use different modes for radios on different channels
    eg PD/ED access on the primary channel and ED-only access on the secondary channels
Clause 4.2.7.3.2.5 in revised EN 301 893
…
Equipment shall not change the ED Threshold Level (TL) for a particular channel for a contiguous period of at least 60 s…

## Slide 34: Does the Coex SC have a view on the 60 second parameter in the adaptivity clause?
  The purpose of having a limit on how often a device can change modes was to avoid “game playing”
    eg an device switching into ED = -62 dBm for short enough periods that PD is not effective
  It is currently proposed that the limit is implemented a time limit, with the 60 sec chosen somewhat arbitrarily
  Is the 60 second limit reasonable?
    Should it be longer?
    Should it be shorter?

## Slide 35: Does anyone else have proposed tweaks to the adaptivity clause?
  It is important to get the adaptivity clause right … and unambiguous!
  It is also important to get the adaptivity clause finished soon!
  Does anyone else have proposed tweaks to the adaptivity clause?

## Slide 36: How should the proposed tweaks be communicated to ETSI BRAN?
  Previously, the IEEE 802.11 WG has sent formal LS’s to ETSI BRAN in relation the adaptivity clause
  Do we need to take such a formal approach this time, or should be just rely on ETSI BRAN participants to communicate the discussions?
    Note: they could not represent the material as a formal IEEE 802.11 WG position
  If there is a desire to send a formal LS, could we please have a volunteer to draft some text for consideration on Thursday?

## Slide 37
  Agenda items
  Review of recent ETSI BRAN meeting
  Paused COT issue & adaptivity

## Slide 38: The submission refining adaptivity related to “paused COT” was not discussed by ETSI BRAN in March 2018
  BRAN(18)097006/7 were submissions from Cisco, Intel, Broadcom & HPE that were discussed at the Coex SC meeting in Chicago in March 2018
  BRAN(18)097006/7 documented a proposed minor change to the adaptivity clause related to “paused COT”
    The proposal only allows the use of the ED-only option of -72 dBm with the “paused COT” feature to maintain the status quo
  A Coex SC motion for the 802.11 WG to support these submissions failed 15/10/7 in Chicago, and it was not considered by the WG
  The submissions were not discussed in ETSI BRAN in March, beyond noting them, because they were dependent on a consensus on the adaptivity proposal in BRAN(18)097004r1/5

## Slide 39: The SC will again discuss the issues related to adaptivity combined with the “paused COT” feature
  The submissions were not discussed in ETSI BRAN in June 2018 because of the focus on obtaining consensus on the adaptivity proposal
  Now that there is a consensus, it is likely its use with the “paused CoT” feature will need to be clarified at the next ETSI BRAN meeting in Sept 2018
  Currently, the Coex SC has no position on restricting responding devices using the “paused COT” feature to use ED-only but now is an opportunity to discuss the issue

## Slide 40: The problem is the revised adaptivity clause effectively allows UE to use ED of -62 dBm with “paused COT”
Reminder of the fundamental issue
  In EN 301 893 v2.1.1, ED-only of -72dBm is always used by LAA UE’s with the “paused COT” feature because LAA device can only use this mode
  In the currently proposed revised EN 301 893, an LAA UE using the “paused COT” feature will effectively be able use ED-only of -62 dBm because it is very unlikely it will detect an 802.11a preamble in 25us
    Preamble length is 20us (including Service Field)
    Very unlikely a 20us preamble will fit into a random 25us window
  Therefore, the currently proposed revised EN 301 893 changes the status quo for no good reason, introducing a potential for misuse beyond the intended use

## Slide 41: The solution is to specify a responding device using “paused COT” must use ED-only at -72 dBm
Potential solution
  The potential solution is to specify the use of ED-only at -72 dBm (actually a function of tx power) with the “paused COT” feature
  This was a very simple solution previously (as described in BRAN(18)097006) because ED-only was labelled “Option 2”
  The option nomenclature has now disappeared from the proposed evisio of EN 301 893, making the drafting a little more difficult … but not impossible!

## Slide 42: Does the SC want to take a position on requiring the use of ED-only with “paused COT” feature?
  If the Coex SC wants to take a position on this issue, now is the time?
  If it decides not to take a position, it is likely the topic will be discussed by ETSI BRAN without IEEE 802.11 WG input
  If it decides to take a position, a volunteer is required to put together a draft LS for Thursday …

## Slide 43
  Agenda items
  Review of recent ETSI BRAN meeting
  Paused COT

## Slide 44: There was a disagreement within ETSI BRAN on an interpretation of the “paused COT” feature
  EN 301 893 contains a feature called “paused COT” that was inserted to allow:
    An LAA eNB to send a grant to an EU
    The LAA UE to access the medium after a “pause” and 25µs of energy detection
  When it was included in EN 301 893, it was understood by many that:
    Only a single grant per UE per COT was allowed
    If energy was detected in the 25 µs period then the UE would have to wait for another grant
  3GPP took a different view of what was agreed, asserting that the LAA UE can have multiple grants
  The extrapolation of this view is a device could be issued with an infinite number of grants, which would effectively give the device access whenever there was any 25 µs period with energy less than -72 dBm

## Slide 45: The interpretation of the “paused COT” feature has been discussed previously in Coex SC & ETSI BRAN
  The pause COT interpretation issue was discussed by the Coex SC in Nov 2017
    See 11-17-1577-00
  It was subsequently discussed by ETSI BRAN in Dec 2017 without consensus
    There was no agreement
    However, it was requested that explicit text be proposed for discussion

## Slide 46: The interpretation of the “paused COT” feature has was discussed by ETSI BRAN in March 2018
  At the March 2018 meeting of ETSI BRAN, Broadcom proposed explicit text in BRAN(18)097031 as follows:
    The Channel Access Engine may grant a maximum of one authorization to transmit for each Responding Device within a single COT
  There was limited discussion on the issue and no consensus
    Ericsson volunteered to work with Broadcom on an appropriate number of grants (per Responding Device?) between 1 and 10
    Broadcom suggested a rate limit of a maximum of one grant per ms per Responding Device
    Qualcomm asked to be kept in the loop
  It was decided to address the issue again at BRAN in June 2018, but there seemed to be some agreement at the time that there should be some sort of finite limit to the number of attempts

## Slide 47: Recent 3GPP RAN discussion of the use of the “paused COT” feature makes interpretation important
  The issue of the interpretation of the paused COT feature may be important because 3GPP RAN1 is reported to be relying on the features as part of NR-U
  In particular, it has been reported that they are considering access schemes for NR-U that allow multiple DL-UL switching points (grants) within a TXOP along with gaps > 25 us

## Slide 48: It appears ETSI BRAN is converging on a compromise interpretation of “paused COT”
  There were two main contributions on the interpretation of “paused COT” at ETSI BRAN in June 2018
    BRAN(18)098013r1 from Broadcom
    BRAN(18)098011 from Ericsson
  Both contributions gave each responding UE up to ten attempts (roughly) to find a 25us window where the medium was free and thus where the UE could continue the “paused COT”
  There was general agreement that this was a reasonable compromise interpretation
  Both proposals were included in the draft revision of EN 301 893 in square brackets
  Ericsson and Broadcom have an implicit action to develop final text

## Slide 49
  3GPP NR-U
  Status report on the most recent 3GPP RAN1 meeting

## Slide 50: The Coex SC will hear an update on coexistence relevant activities at the recent 3GPP RAN1 meeting
  The Coex SC may hear a status update … focused on coexistence issues of course!
    See 11-18-1295r0

## Slide 51
  3GPP NR-U
  Minutes

## Slide 52: The Coexistence SC will consider approval of the meeting minutes from Warsaw
  The minutes for the Coexistence SC at the Warsaw meeting in May 2018 are available on Mentor:
    11-18-1061-01
  Note that r1 has more summaries than r0 of the “he sad, she said” aspects (albeit without names)
    These modifications to better align r1 with the IEEE 802 EC requirements for minutes
    There is also an r2, which is just a diff of r0 and r1
  Motion:
    The IEEE 802 Coex SC approves 11-18-1061-01 as minutes of its meeting in Warsaw in May 2018
    Moved:
    Seconded:

## Slide 53
  3GPP NR-U
  Actions out of most recent 3GPP RAN1 meeting

## Slide 54: The SC may consider a LS to 3GPP RAN4 out of yesterday’s discussion
  During Wednesday’s session, an apparent contradiction between RAN1/2 and RAN4 specs was highlighted, with a potential adverse affect on 802.11 operation
  There is now a proposal to send RAN4 a LS on this topic
    See 18-11-1305

## Slide 55
  3GPP NR-U
  6GHz greenfield

## Slide 56: The Coex SC previously noted another perspective on sharing new spectrum from LTE community
  In previous meetings, the Coex SC has discussed the possibility of new coexistence mechanisms in new spectrum
    eg a new preamble at 6Ghz
  There was not much interest at the time, mainly because most in the 802.11 community want to think of 6GHz as an extension of 5GHz
    The simplest approach, aligned with status quo
  However, it appears the LTE community has different ideas
    See embedded document from Qualcomm, Nokia & Ericsson to CEPT ECC FM57
  This material was discussed by the Coex SC in Warsaw in May 2018

## Slide 57: A submission to FM57 proposes non LBT style access in the 6GHz band

## Slide 58: The Coex SC Chair sent a call to action in May 2018
Call to action sent by Coex SC Chair to reflector
  … discussions are beginning to transition from coexistence in the legacy 5GHz band (legacy in the sense they contain a large number of existing Wi-Fi deployments) to coexistence in the greenfield 6GHz band (greenfield in the sense it currently contains few/no Wi-Fi or unlicensed LTE deployments). The greenfield nature of 6GHz means that we can more easily consider different coexistence mechanisms and thresholds.
  Indeed, a variety of suggestions have been made for mechanisms that are claimed to support fair and efficient coexistence between 802.11 and other technologies in the 6Ghz band, including:
    Status quo: use the 5GHz rules (from refined EN 301 893) in 6Ghz band
    ED-only: all technologies use ED-only (ie no use of PD)
      Thresholds suggested include -72dBm, -62dB or even -52dBm
    …

## Slide 59: The Coex SC Chair sent a call to action in May 2018
Call to action sent by Coex SC Chair to reflector
    …
    Common preamble: all technologies use the traditional 802.11 mechanism and thresholds using a common preamble
      Could be either 802.11a preamble or a new preamble
      Note: the use of the 802.11a preamble is likely to unpopular in 3GPP, and previously 802.11 chip vendors indicated it was too late for them to consider a new preamble in 6GHz
    Alt 4: any technology that detects its own preamble at -82 dBm can use an ED of -62 dBm, otherwise a an ED of -72 dBm
      Note: this means that LAA would only defer to 802.11 at ED of -62dBm
      Note: IEEE 802.11 WG’s LS to ETSI BRAN noted that 3GPP simulations have already demonstrated this approach is unfair to 802.11 systems using the traditional mechanism and thresholds

## Slide 60: The Coex SC Chair sent a call to action in May 2018
Call to action sent by Coex SC Chair to reflector
  Call for action: I would ask that anyone who has studies that support any of these options, or that show any of these options are unacceptable, to make them available for consideration by the IEEE 802.11 Coexistence SC in July or Sept or at the proposed 802.11/3GPP Coexistence Workshop.
  Studies could be based on analysis, old or new simulations or actual deployment measurements.
  If you think you might be able to contribute such a study, please ping me as soon as possible so I can plan upcoming agendas.

## Slide 61: The Coex SC will discuss next steps for discussion about 6GHz coexistence
  At this time there is no forum discussing coexistence issues with other similar systems (eg NR-U) in the 6Ghz band
    ETSI BRAN discussions have explicitly excluded 6GHz
  Some questions:
    Does anyone believe it is important that the industry consider 6GHz coexistence issues now?
      Why or why not?
    In what forum should these issues be discussed?
      Coex SC, 3GPP RAN, ETSI BRAN?
      A joint workshop? (proposal in next section)
    Is anyone willing to respond to the call for action, and actually provide some material to this SC?
      Anyone?

## Slide 62
  Agenda items
  A workshop?

## Slide 63: 802.11 WG will probably need to work with 3GPP RAN1 on “fair” access in 6GHz
  It was noted in Chicago that 3GPP is treating 802.11 as an incumbent in the 5GHz band, which they have agreed to protect with a “one way definition”
    ie, the addition of an LAA systems will not cause any more loss of performance on a Wi-Fi system that the addition of a Wi-Fi system will cause
    ie, there is no expectation that Wi-Fi (with possible exception of 802.11ax) will do the same to LAA
  It was also noted that 3GPP consider 6 GHz to be greenfield spectrum and so Wi-Fi should expect no “incumbency” based protection
  This highlights the need for 3GPP RAN1 and IEEE 802.11 to engage with the goal of agreeing on how fair access between all technologies can be maintained in the 6GHz band

## Slide 64: The SC will discuss the possibility of a workshop to engage with 3GPP RAN1 on sharing of 5/6GHz
  In Chicago, it was suggested that IEEE 802.11 WG be proactive about engaging with 3GPP on “fair” sharing mechanisms for 6GHz
  It was further suggested that IEEE 802 could invite 3GPP RAN1 to participate in a workshop on this topic (as well as 5GHz)
    Possibly at the IEEE 802.11 interim in Sept 2018 or the plenary in Nov 2018 (with invitation in July 2018)
  There has been some positive feedback to the suggestion for a workshop but no one has really stepped up … until now!
  Lili Hervieu (Cablelabs) will propose a Workshop with 3GPP RAN
    See 11-18-1139-01

## Slide 65: The Coex SC will discuss the next steps for a workshop
  Do we have a LS related to the proposed Workshop?

## Slide 66
  Agenda items
  Status of WFA LS to 3GPP RAN

## Slide 67: In Irvine, the SC discussed a LS from WFA to 3GPP RAN in relation to coexistence testing
  In Irvine, the IEEE 802.11 Coex SC discussed LS from WFA to 3GPP RAN that was copied to IEEE 802.11 WG
    See 11-17-1853-00
  It appeared the WFA was concerned that 3GPP RAN4 developed coexistence tests:
    Do not test all the LAA Release 14 features
    Are not being used to validate coexistence claims, as previously committed to IEEE 802 in Nov 2016 (in 3GPP R1‐1613770)
  Ultimately, the SC decide to not participate in the LS ping pong but did formally recommended to the WG that it pass a motion express support for the content of the LS
    Just in case it was useful in discussions at 3GPP RAN
  The IEEE 802.11 WG approved the recommendation

## Slide 68: The reply to the WFA confirmed 3GPP is reneging on previous validation commitments
  The IEEE 802.11 WG was not copied on the response from 3GPP RAN
  However, the response is available as 3GPP R1-1801314
  In the reply, 3GPP RAN:
    Confirmed that they do not plan to use the RAN4 tests to validate LAA coexistence
    Informed WFA there is no Study Item to extend the tests for Rel-14 updates to LAA
    Informed WFA there is no current Work Item to define pass/fail criteria for the RAN4 tests
  The reply is as one might expect and essentially confirms that 3GPP RAN is reneging on previous commitments to IEEE 802 in relation to coexistence testing
  One possible reasonable conclusion is that future commitments from 3GPP RAN should be taken with a “grain of salt”

## Slide 69: The Coex SC will review the most recent LS from WFA to 3GPP
  The WFA has sent a LS response to 3GPP RAN/RAN1/RAN4, copied to IEEE 802.11 WG
    See 11-18-1087-00
  The response acknowledges RAN statement that it has no current work item for pass/fail multi-node coexistence testing
    Wi-Fi Alliance thanks 3GPP TSG RAN for their reply [3] to the Wi-Fi Alliance requests for clarification and comment on the status of multi-node Wi-Fi LAA-LTE coexistence testing [1] and [2]
    Wi-Fi Alliance acknowledges 3GPP’s response that it has no current work item for the development of pass/fail criteria for multi-node coexistence testing, no approved study item to extend 3GPP TR 36.789 to cover LAA Rel-14, and has stated that it is beyond the scope of 3GPP to either mandate co-existence tests or develop pass/fail criteria for coexistence tests with technologies developed outside 3GPP
  …

## Slide 70: The Coex SC will review the most recent LS from WFA to 3GPP
  The LS also notes that WFA has expanded its LTE-U test plan to cover LAA
    In light of this clarification, Wi-Fi Alliance respectfully informs 3GPP that is has revised its Coexistence Test Plan to include coverage of coexistence between Wi-Fi and LTE-LAA
    The revised test plan has been published at https://www.wi-fi.org/file/coexistence-test-plan
  There does not appear to be anything for IEEE 802.11 Coex SC to do beyond noting that the test plan may represent a resource for the future

## Slide 71
  Agenda items
  Review of recent ETSI BRAN meeting
  Blocking energy

## Slide 72: IEEE 802 has a long standing position about the use of blocking energy
  IEEE 802 has expressed concern to 3GPP RAN/RAN1 about the use of blocking energy by some implementations of LAA for a number of years
  Blocking energy is the energy transmitted in the time between when the LBT mechanism gives it access and the time it is ready to use the medium
    Also known as reservation signals
  The primary purpose of blocking energy is to stop other system gaining access to the medium in the meantime
  The concern expressed by IEEE 802 in various Liaison Statements regarding blocking energy was that it was unnecessary use of the medium and, as such, it represented inappropriate interference to other devices

## Slide 73: IEEE 802’s discussion with 3GPP related to blocking energy ultimately went nowhere
  The position expressed by IEEE 802 to 3GPP RAN/RAN1 was that blocking energy should be limited to a level less than currently used by some LAA implementations
    Current blocking energy is used up to 0.5ms or 1ms per COT (up to ~8ms)
  3GPP RAN/RAN1 agreed that the use of blocking energy is undesirable
    They noted it is unnecessary for good performance
    They noted it is so unnecessary that the LAA spec did even not define it
  3GPP RAN/RAN1 agreed at one point to limit the need for blocking energy by defining additional starting positions to the LAA spec
    This would reduce the length of any blocking energy
  IEEE 802 agreed that this approach might be a reasonable compromise, subject to testing with real systems
  Unfortunately, 3GPP RAN1 later reneged on their commitment to define additional starting positions in LAA

## Slide 74: There was not consensus in ETSI BRAN on restricting the use of blocking energy
  There has been a series of discussions about blocking energy in ETSI BRAN over a number of years, without consensus
  In Dec 2017, Cisco made a compromise proposal that any use of blocking energy be limited to 100µs
    This would have the effect of limiting the use of blocking energy by LAA implementations to no longer than the time before the next symbol
    It recognised that some use of blocking energy is reasonable/acceptable
  There were many objections to this proposal from both Wi-Fi & LTE communities
    Some objections were self interested because of a desire not to change LAA implementations in the pipeline
      Note: it believed this is why 3GPP couldn’t agree on adding new starting positions
    Some objected on the basis it was not fair to pick on blocking energy when there were many other examples of inefficient use of the medium
      eg padding, use of low data rate, etc
      Some in Wi-Fi community were concerned some 802.11ax features might be impacted

## Slide 75: There is not consensus in ETSI BRAN on a new methodology being applied to blocking energy in LAA
  Before the March 2018 BRAN meeting, Cisco (Andrew Myles) facilitated an e-mail discussion on a new approach to dealing with blocking energy
  The discussion and conclusions are summarised in BRAN(18)097010, which was presented to ETSI BRAN in March 2018
    BRAN(18)097010 documented a methodology for dealing with “blindingly obvious” cases
    The BRAN(18)097010 methodology applied to blocking energy means it should be disallowed for LAA
    BRAN(18)097010 did not propose a mechanism for disallowing blocking energy for LAA
  Despite this work, there is still not consensus in ETSI BRAN on the question of blocking energy

## Slide 76: The new methodology applied to blocking energy means it should be disallowed for LAA
Summary of BRAN(18)097010 methodology applied to LAA
  3GPP RAN1 is an authoritative source on LAA matters
    Particularly on the use of blocking energy (also known as reservation signals)
  3GPP RAN1 has explicitly stated in LS’s to IEEE 802.11 WG that reservation signals are unnecessary for good performance
  3GPP RAN1 has also stated blocking energy is not defined in the LAA specification
    Suggesting blocking energy is so unnecessary that it is not even defined
  There is thus a “blindingly obvious” case that blocking energy should not be allowed in the very specific case of LAA
    Note: this conclusion creates no precedent for any other situation because it depends on the existence of an authoritative source (3GPP RAN1 in this case) to judge the particular facts

## Slide 77: Ericsson used an access method taxonomy to justify the use of blocking energy
  There was a presentation from Ericsson in March 2018 that was related to blocking energy
  It provided a taxonomy of access methods in BRAN(18)0000001
    The main purpose was not to make a proposal for a change in the standard, but to bring discussion on mechanism to a technical matter (the purpose these mechanism serve)
  BRAN(18)0000001 listed various mechanisms for devices to share the medium with other devices using the same & different technologies
    At both PHY and MAC levels
  It highlighted that many PHY based synchronisation methods need to use padding of various types, ie padding can be necessary
    Pre-pending, appending or inserted into a transmission
  The implication of the presentation was that blocking energy (as a PHY synchronisation mechanism) is also justified
File link

## Slide 78: There was not consensus on the conclusions that can be drawn from the access method taxonomy
  There was limited discussion of in BRAN(18)0000001 at the time of presentation; it was discussed in more detail as part of the blocking energy discussion
  Andrew Myles asserted BRAN(18)0000001 cannot be used to justify the use of blocking energy by some implementations of LAA; he noted that:
    BRAN(18)0000001 highlighted the inclusion of a mechanism in the taxonomy does not mean it is appropriate for use
      eg PCF is in the taxonomy and yet its use is not allowed under EN 301 893 rules because it does not enable sharing
    There is agreement that many PHY sync methods are indeed necessary, whereas even 3GPP RAN1 agrees the use of blocking energy with LAA is unnecessary

## Slide 79: The Coex SC will hear an update on discussions about blocking energy at ESTI BRAN in June 2018
  There was further discussion of the blocking energy issue at the ETSI BRAN meeting in June 2018
  BRAN(18)098008 asked for agreement on the principle that:
    Transmissions that are agreed to be unnecessary or transmissions whose sole purpose is preventing other devices using the spectrum are not allowed
  While there was not consensus on the question of blocking energy, the representative from the German regulator suggested that blocking energy is already not allowed by regulation in Germany
    He later provided a translation of rules for 2.4GHz and 5GHz
    The rules state “Emissions that intentionally disturb or prevent the intended use of WLANs, such as emissions of radio signals and/or data packets that have the intention to log off or influence the WLAN connections of other users against their will, are prohibited”

## Slide 80: The WG may consider a LS to ESTI BRAN asking they consider discouraging or limiting blocking energy
  It is proposed that IEEE 802.11 WG consider a LS to ESTI BRAN asking they consider discouraging or limiting blocking energy
    The complete proposed LS is in 11-18-0706r1
  This would be consistent with IEEE 802’s previous LS’s to 3GPP RAN/RAN1 related to blocking energy
  A possible motion (for Thu PM1) is:
    The IEEE 802.11 Coex SC recommends that the material in 11-18-0706r1 be sent to ETSI BRAN, expressing support for discouraging or limiting the use of blocking energy

## Slide 81
  Agenda items
  Plans for next ETSI BRAN meeting

## Slide 82: The SC may discuss the next ETSI BRAN meeting in September 2018
  The SC may also discuss the next ETSI BRAN meeting in September 2018 (week after IEEE 802.11 WG meeting in Hawaii)
    Topics
    Participation by Wi-Fi stakeholders
    Potential LS’s
    …

## Slide 83
  Agenda items
  Plans for next meeting

## Slide 84: The Coex SC will discuss plans for the next session in Hawaii
  Possible items include
    Preparation for next ETSI BRAN meeting
      The following week, and so more likely to be reviews of submitted documents
    Review of 3GPP RAN1 activities
      Focus on NR-U
    … <other suggestions?>
Bottom line: do not rely on a few people/companies to drive good coexistence between 802.11 and other technologies – they can’t do it by themselves

## Slide 85: The IEEE 802.11 Coexistence SC meeting in San Diego in July 2018 is adjourned!