## Slide 1: Flexible Group ID Allocation
Date: 2018-06-12
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Sun Bo |  |  | sun.bo1@zte.com.cn
Wei Ning |  |  | wei.ning@zte.com.cn

## Slide 2: Abstract
A STA supporting WUR Group ID operation could be waken up by multicast wake-up frame. The group ID(GID) is carried in the address field of a wake-up frame to identify one or more WUR STAs belonging to the same group.
In the current draft text, the frame body of a multicast wake-up frame can carry a bitmap to further indicate the specific WUR STAs of the group to be waken up by this frame.
A method about STA grouping and Group ID allocation for WUR operation is proposed in this proposal.

## Slide 3: Motivation
The length of the frame body field is in units of octets and is equal to 2x(L+1), where L is the value of the Length subfield in the Frame Control field. The minimum length and the maximum length of the frame body are 2 octets and 16 octets, respectively.
A WUR STA can belong to multiple groups based on the granularity of grouping, so that AP can flexibly wake up multiple WUR STAs by using variable bitmap size in the frame body of a multicast WUR frame.
  grouping granularity parameter means how many WUR STAs with contiguous WIDs are contained in one group.

## Slide 4: Proposal
AP uses grouping granularity parameters to group WUR STAs.
  Once the size of WID is settled, the identifier’s space is fixed. A subset of consecutive values of the identifier's space are reserved for Group ID[1].Other identifiers are allocated or to be allocated to a WUR STA.
  Besides notifying the Group ID range values, the AP also notifies grouping granularity parameter to the WUR STAs.
The WUR STAs are grouped based on the grouping granularity parameters, and each group is assigned a Group ID in sequence within the Group ID range.
  Eg. grouping granularity parameter may be set to 2 octets, 4 octets, 8 octets and 16 octets, respectively.
  A specific WUR STA can be grouped into multiple groups with different grouping granularity.

## Slide 5: Proposed Group ID Allocation Scheme
ID for AP
Group IDs
IDs for WUR STA(WID)
IDs for WUR STA(WID)
IDs for WUR STA(WID)
grouping granularity x
grouping granularity 2x
#1
Group ID numbering
#2
…
…
#3
#4
# m
# m+1
# n
AP may use multiple grouping granularities to group WIDs, in which case a WUR STA with a specific WID will belong to multiple groups at the same time.
ID Space
number of Group IDs ≥n

## Slide 6: Proposed Group ID Allocation Scheme
As an example shown above, one WUR STA can belong to multiple groups based on the grouping granularity.
  WUR STA a & b belong to group ID #1 and STA c belongs to group ID #2 respectively when grouping granularity is x
  WUR STA a &b & c belong to group ID #m+1 when grouping granularity is 2x
When ONLY STA a & b are to be waken up, the AP can send a multicast WUR frame with group ID #1 with bitmap size of 2 octets for example.
When STA a & b & c are to be waken up, the AP can send a multicast WUR frame with group ID #m+1 with bitmap size of 4 octets for example.
IDs for WUR STA(WID)
grouping granularity x
grouping granularity 2x
#1
Group ID numbering
#2
…
…
#3
#4
# m
# m+1
# n
STA a & b
STA c
STA a & b & c

## Slide 7: Conclusion
We discussed Group ID allocation scheme in this proposal.
  AP notifies Group ID range values and grouping granularity parameter to a WUR STA.
  By knowing grouping granularity, a WUR STA could determine which group(s) it belongs, and its position in the group(s).
  AP does not need to explicitly signal the specific Groups IDs which the WUR STA belongs to.
  A WUR STA can belong to multiple WUR groups so that AP can flexibly wake up multiple WUR STAs by using variable bitmap size in the frame body of a multicast WUR frame.

## Slide 8: Straw Poll
Do you agree the Group ID Allocation Scheme in slide 5?

## Slide 9: References
[1]11-17-0575-11-00ba-spec-framework