## Slide 1: Wake Up Procedure After Receiving Broadcast/Group Addressed Wake Up Frames
Date: 2018-07-09
Authors:

## Slide 2
Abstract
In this contribution, we discuss different options for wake up behaviors after a STA receives a broadcast/group addressed wake up frame.

## Slide 3: Introduction (1/2)
TGba agreed to use broadcast wake up frames to wake up all STAs
  A non-AP STA that receives the Counter subfield of the TD Control field in a WUR Wake-up frame that contains a value that is different from the previously received Counter field shall follow the procedure defined in 11.2.3.17 (TIM Broadcast) to attempt to receive the PCR Beacon information subject to its PCR delay constraints. [1]
    The wake up procedure after receiving individually addressed wake up frame is clear
  A non-AP STA should send a response frame to the associated AP using its PCR component after receiving a WUR Wake-up frame with Address field set to the WID that identifies the non-AP STA.[1]
  A non-AP STA enters WUR mode after successful frame exchange using PCR: WUR Mode Setup frame and WUR Mode Response frame [1]

## Slide 4: Introduction (2/2)
The procedure after receiving a broadcast wake up frame may need some discussion or clarification:
  Q1: Do STAs need to let the AP know that its PCR is in the awake state?
  Q2: Do STAs need to conduct frame exchanges using its PCR before they go back to WUR mode?
  These related behaviors are not clearly defined in the draft and should be clarified to avoid confusion
Similar questions may be relevant when a STA receives a group-addressed wake up frame indicating that there are PCR group addressed frames available for the STA
In this contribution, we discuss a few options regarding the procedure after receiving a broadcast/group addressed wake up frame

## Slide 5: Options After Receiving A Broadcast Wake Up frame (1/3)
STAs will turn on its PCR and receive a beacon [1]
Q1: Do STAs need to let the AP know that it is awake?
  Choice 1: STAs send a frame to the AP/receive the PCR beacon
  Choice 2: STAs will receive the PCR beacon without sending any frames to the AP
Choice 1:
  May be beneficial if the STA happens to have UL packets or if the AP happens to have a DL packet for the STA; could achieve some power saving; seems to be a rare event.
  May lead to extra energy consumption if no UL/DL packets are available
  Use more energy to conduct frame exchange with the AP before entering WUR Mode again
Choice 2:
  Achieve the purpose of BSS parameters update
  Will not miss wake up frames since the STA’s WURx is still on
  Do not waste energy by transmitting frames to the AP

## Slide 6: Options After Receiving A Broadcast Wake Up frame (2/3)
Q2: Do STAs need to conduct frame exchanges with the AP before entering WUR mode?
  Choice 1: STAs conducts frame exchanges with the AP before entering WUR mode again
  Choice 2: STAs will receive the PCR beacon and enter the WUR mode directly
Choice 1:
  Necessary if Option 1 is chosen for Q1, i.e., if the STA has sent a frame to the AP
  May be necessary if the AP considers STAs’ PCRs to be awake after a broadcast wake up frame with increased Counter value
  Consumes extra energy
Choice 2:
  Can achieve significant power saving if Option 2 is chosen for Q1, i.e., if the STA just turns on its PCR and receives the beacon without sending the AP any frames
  Will not miss wake up frames since the STA’s WUR is still on; with the assumption that the AP considers the STAs to still be in WUR mode

## Slide 7: Options After Receiving A Broadcast Wake Up frame (3/3)
To summarize, the options after a STA receives a broadcast wake up frame with increased Counter value include the following:
  Option 1: A STA wakes up, receives a beacon and return to WUR mode immediately
    Most energy efficient approach; achieving the goal of receiving updated beacon
    Don’t miss any wake up frame since the STA’s WURx is still on
  Option 2: A STA wakes up, sends a frame to AP/receives updated beacon, and conducts frame exchange with its AP before entering WUR mode
    Consumes energy to send frame as well as conduct WUR mode frame exchanges
    No obvious gain compared to Option 1 except in the rare event that there happen to be UL/DL packets at the STA/AP
  Option 3: A STA wakes up, receives updated beacon, and conducts frame exchange with its AP before entering WUR mode if the AP considers all STAs’ PCRs to be in awake state after sending a broadcast wake up frame with increased Counter value
    Consumes energy to conduct WUR mode frame exchanges before entering WUR mode
    No obvious gain compared to Option 1

## Slide 8: Options After Receiving A Group Addressed Wake Up frame (1/2)
Similarly, the options after a STA receives a group addressed wake up frame indicating a PCR group addressed packet include the following:
  Option 1: A STA wakes up, receives the group addressed PCR frame and returns to WUR mode immediately
    Most energy efficient approach; achieve the goal of retrieving group addressed PCR frames
    Group addressed PCR frames do not require acknowledgement
    Don’t miss any wake up frame since the STA’s WURx is still on
  Option 2: A STA wakes up, sends a frame to AP/receives the group addressed PCR frame, and conducts frame exchange with its AP before entering WUR mode
    Consumes energy to send frame as well as to conduct WUR mode frame exchanges
    No obvious gain compared to Option 1 except in the rare event that there happen to be UL/DL unicast packets at the STA/AP

## Slide 9: Options After Receiving A Group Addressed Wake Up frame (2/2)
Similarly, the options after a STA receives a group addressed wake up frame indicating PCR group addressed packet include the following:
  Option 3: A STA wakes up, receives the group addressed PCR frame, and conducts frame exchange with its AP before entering WUR mode if the AP considers the STAs’ PCR to be in the awake state after sending group addressed wake up indicating group addressed PCR frames
    Consumes energy to conduct WUR mode frame exchanges with the AP before entering WUR mode
    No obvious gain compared to Option 1

## Slide 10: Conclusion
We discussed three options of STA behaviors after a STA receives a broadcast wake up frame including a increased Counter or a group addressed wake up frame indicating group addressed PCR frame
  Option 1: A STA wakes up, receives the PCR frame and returns to WUR mode immediately
  Option 2: A STA wakes up, sends a frame to AP/receives the PCR frames, and conducts WUR mode frame exchange with its AP before entering the WUR mode
  Option 3: A STA wakes up, receives the PCR frames, and conducts WUR mode frame exchange with its AP before entering the WUR mode if the AP considers all STAs’ PCR to be in awake state after sending the broadcast/group addressed wake up frame
Option 1 seems to be the most power efficient approach while achieving the desired behavior

## Slide 11
References
[1] IEEE P802.11ba Draft 0.3, May 2018
[2] IEEE P802.11RevMD Draft 1.0, Feb. 2018

## Slide 12: SP 1
Which option of STAs’ behaviors do you prefer after a STA receives a broadcast wake up frame including a increased Counter or a group addressed wake up frame indicating group addressed PCR frame
  Option 1: A STA wakes up, receives the PCR frame and returns to WUR mode immediately
  Option 2: A STA wakes up, sends a frame to AP/receives the PCR frames, and conducts WUR mode frame exchange with its AP before entering WUR mode
  Option 3: A STA wakes up, receives the PCR frames, and conducts WUR mode frame exchange with its AP before entering WUR mode
  Option 4: abstain
  Option 1/2/3/4: