## Slide 1: Recommendations on OOK waveform and CSD setting
Date: 2018-07-09
Authors:

## Slide 2: Introduction
It has been agreed by the TGba group not to mandate any OOK waveform, but specify few examples that does into the spec draft
  In [1,2], we studied the WUR performance for different pulse shapes and CSD values
  In this presentation, we compare the WUR performance with different OOK pulse designs [1-6] and CSD values and investigate the reasons for differences between reported PER vs. SNR results
We provide recommendations on OOK waveform and the CSD settings for multi-antenna transmission

## Slide 3: OOK pulse designs
For the low data rate, the 4 us OOK pulse was generated by populating the center 13 subcarriers with subcarrier spacing of 312.5 KHz. Center sub-carrier is nulled.
For the high data rate, the 2 us OOK pulse was generated by populating every other subcarrier out of these 13 subcarriers.
  We have 6 non-zero subcarriers
  In [1], we studied the PER and PAPR performance for 64 different pulse shapes
    Identified a pulse shape that provides good tradeoff between PER and PAPR
      The proposed design provides best performance in Channel D
      The PAPR of proposed design is significantly smaller than legacy preamble (STF, LTF, and SIG)

## Slide 4: Why do we see different PER results?
Pulse design proposals
  Our proposed design (Proposal 1)
    High data rate: [1 0 1 0 -1 0 0 0 -1 0 -1 0 1]
    Low data rate: [1 -1 1 -1 -1 1 0 -1 -1 1 1 1 1]
  The proposed design [3] (Proposal 2)
    High data rate: [1 0 1 0 1 0 0 0 -1 0 1 0 -1]
    Low data rate: [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1]
Differences:
  Receiver architectures for performance evaluation
    WUR decoding based on Energy detection (Example: [3])
      Metric used: Sum(abs(.)^2)
    WUR decoding based on Envelope detection (Example: [5])
      Metric used: Sum(abs(.))
  SNR Calculation: before or after 4 MHz filter

## Slide 5: Energy detection vs. Envelope detection
Very similar performance for both receivers: energy detection and envelope detection
Comparison between different pulse designs
  Our proposed design performs better in Channel D
    In [5], it was confirmed that equal allocation of power in frequency domain provides best performance in fading channel (due to gains from frequency diversity), while low PAPR pulse provides best performance in AWGN

## Slide 6: PER Performance SNR @20 MHz BW vs. SNR @ 4MHz
Performance gap between two designs is different for different SNR measurements (SNR @ 20 MHz bandwidth or SNR @ 4 MHz bandwidth)
  Partly due to the different frequency domain pulse shapes
  Filter itself further changes the shape of the OOK pulse
  For a practical receiver, SNR in the 4 MHz, post filter is more relevant

## Slide 7: Difference in spectrum of the pulses
The pulse in proposal 2 [3] has significantly higher side lobes
  Relatively smaller energy in the 4 MHz WUR signal bandwidth
  Requires a sharper filter at the receiver to mitigate the ACI, which increases receiver complexity and power consumption

## Slide 8: OOK waveform comparison
Proposal 1
  Low Data Rate: reuses the L-STF coefficients, which are already implemented in PCR, and we have shown that they have good performance and low PAPR
    S = [1 -1 1 -1 -1 1 0 -1 -1 1 1 1 1] (PAPR = 2.28 dB)
  High Data Rate
    S = [1 0 1 0 -1 0 0 0 -1 0 -1 0 1] (PAPR = 3.4 dB)
We compare the performance of the above proposed sequences to [3-6]
  Proposal 2 [3]
    Low Data Rate: [1 1 1 -1 -1 -1 0 -1 1 -1 -1 1 -1] (PAPR = 2.09 dB)
    High Data Rate: [1 0 1 0 1 0 0 0 -1 0 1 0 -1] (PAPR = 2.6 dB)
  Proposal 3 [5]
    Low Data Rate: [-9-5j -7+9j -1+1j 9+15j 15-9j -9+1j 0 1-9j 9-15j 15+9j -1+1j 9-7j 5+9j] (PAPR = 1.23 dB)
    High Data Rate: [3+7j 0 1+15j 0 -5+13j 0 0 0 13-5j 0 -15-1j 0 7+3j] (PAPR = 0.8 dB)

## Slide 9: CSD recommendations
Based on the studies in [2] and further, we recommend the following CSD settings:
Number of antennas | CSD setting (ns)
2 | [0 3000]
3 | [0 1500 3000]
4 | [0 1000 2000 3000]
5 | [0 750 1500 2250 3000]
6 | [0 600 1200 1800 2400 3000]
7 | [0 500 1000 1500 2000 2500 3000]
8 | [0 450 850 1300 1700 2150 2550 3000]
Number of antennas | CSD setting (ns)
2 | [0 1500]
3 | [0 750 1500]
4 | [0 500 1000 1500]
5 | [0 400 750 1150 1500]
6 | [0 300 600 900 1200 1500]
7 | [0 250 500 750 1000 1250 1500]
8 | [0 200 450 650 850 1050 1300 1500]
2 us OOK waveform
4 us OOK waveform

## Slide 10: Multi-antenna performance study with different designs
Considered waveform proposals 1, 2 and 3
Study the performance to these waveforms with our recommended CSD values
Simulation settings
  Low data rate and high data rate
  Considered 1 Tx, 2 Tx, 4 Tx and 8 Tx antennas
  Channel model D
  SNR measured post 4 MHz filter
  Filter: 3 rd order Butterworth filter with 2.5 MHz cutoff frequency

## Slide 11: HDR Performance in Channel D
Observations
Single Tx antenna: Proposal 1 waveform was 1.50 dB better than Proposal 2 waveform
For 2, 4 and 8 Tx antennas, proposed CSD works very well with different pulse shapes

## Slide 12: SNR @ 10% PER (Channel D, HDR)
 | Pulse: Proposal 1 +Proposed CSD | Pulse: Proposal 2 +Proposed CSD | Pulse: Proposal 3 +Proposed CSD
1 TX antenna | 5.54 dB | 7.04 dB | 6.25 dB
2 TX antenna | 4.33 dB | 4.82 dB | 4.85 dB
4 TX antenna | 3.71 dB | 3.46 dB | 3.93 dB
8 TX antenna | 2.65 dB | 2.60 dB | 3.15 dB
Observations
Single Tx antenna: Proposal 1 waveform was 1.50 dB better than Proposal 2 waveform
For 2, 4 and 8 Tx antennas, proposed CSD works very well with different pulse shapes

## Slide 13: LDR Performance in Channel D
Observations
Single Tx antenna: Proposal 1 waveform is marginally better (0.4 dB) than Proposal 2 waveform
For 2, 4 and 8 Tx antennas, proposed CSD works very well with different pulse shapes

## Slide 14: SNR @ 10% PER (Channel D, LDR)
 | Pulse: Proposal 1 +Proposed CSD | Pulse: Proposal 2 +Proposed CSD | Pulse: Proposal 3 +Proposed CSD
1 TX antenna | 3.10 dB | 3.63 dB | 3.59 dB
2 TX antenna | 1.46 dB | 1.38 dB | 1.46 dB
4 TX antenna | -0.12 dB | -0.05 dB | 0.23 dB
8 TX antenna | -0.93 dB | -0.76 dB | -0.38 dB
Observations
Single Tx antenna: Proposal 1 waveform is marginally better (0.4 dB) than Proposal 2 waveform
For 2, 4 and 8 Tx antennas, proposed CSD works very well with different pulse shapes

## Slide 15: Conclusions
The proposed pulse shape has been optimized for good tradeoff between Channel D performance and PAPR
Proposal 2 [3,6] and Proposal 3 [5] pulse shape was optimized for AWGN performance and PAPR
The recommended CSD values work very with different pulse shapes
We recommend to have multiple examples of sequences & CSD values in the Draft 1.0, optimized for performance in different channel conditions

## Slide 16: Straw poll 1
Do you support to have three examples of ON pulse shapes, for 2 us and 4 us?
  Yes/No/Abstain:

## Slide 17: Straw poll 2
Do you support to include the following IFFT coefficients for construction of 2 us OOK pulse, as one of the example in the draft?
    S = [0 0 0… 0 1 0 1 0 -1 0 0 0 -1 0 -1 0 1 0….0 0 0]
    Yes:
    No:
    Abstain:

## Slide 18: Straw poll 3
Do you support the following CSD that goes with 2 us OOK waveform, as one of the examples in the draft?
    Use linear CSD spacing, with max CSD of 1500 ns between first and last antenna
    Yes:10
    No:0
    Abstain:4
Number of antennas | CSD setting (ns)
2 | [0 1500]
3 | [0 750 1500]
4 | [0 500 1000 1500]
5 | [0 400 750 1150 1500]
6 | [0 300 600 900 1200 1500]
7 | [0 250 500 750 1000 1250 1500]
8 | [0 200 450 650 850 1050 1300 1500]

## Slide 19: Straw poll 4
Do you support to include the following IFFT coefficients for construction of 4 us OOK pulse, as one of the example in the draft?
    S = [0 0 0… 0 1 -1 1 -1 -1 1 0 -1 -1 1 1 1 1 0…0 0 0]
    Yes:
    No:
    Abstain:

## Slide 20: Straw poll 5
Do you support the following CSD that goes with 4 us OOK waveform, as one of the examples in the draft?
    Use linear CSD spacing, with max CSD of 3000 ns between first and last antenna
    Yes:
    No:
    Abstain:
Number of antennas | CSD setting (ns)
2 | [0 3000]
3 | [0 1500 3000]
4 | [0 1000 2000 3000]
5 | [0 750 1500 2250 3000]
6 | [0 600 1200 1800 2400 3000]
7 | [0 500 1000 1500 2000 2500 3000]
8 | [0 450 850 1300 1700 2150 2550 3000]

## Slide 21: References
[1] Vinod Kristem, Shahrnaz Azizi, Thomas Kenney, “IEEE 802.11-18/97r0 2 us OOK pulse for high rate,” January 2018
[2] Vinod Kristem, Shahrnaz Azizi, Thomas Kenney, “IEEE 802-11/772r0 Updated results on WUR performance with multiple TX antennas,”, May 2018
[3] Steve Shellhammer, et.al, “IEEE 802.11-18/97r0 Multiantenna TX Diversity,” May 2018
[4] Steve Shellhammer, et.al, “IEEE 802.11-18/1198r0 Simulations with Recommended Symbols and CSD”, July 2018
[5] Miguel Lopez, Dennis Sundman, Leif Wilhelmsson, “MC-OOK Symbol Design,” IEEE 802.11-18/479r2,” March 2018
[6] Eunsung Park , et.al, “11-18-0421-01-00ba-ook-waveform-generation-follow-up,” March 2018

## Slide 22: Channel D performance of different waveforms (SNR in 20 MHz bandwidth)
Performance with different waveforms
  Low rate: Proposal 1 waveform is marginally better (0.2 dB)
  High rate: Proposal 1 waveform is better by 0.6 dB

## Slide 23: AWGN performance of different waveforms (SNR in 4 MHz bandwidth)
Comparable performance with different waveforms
  Low rate: Proposal 1 and proposal 3 are marginally better than proposal 2 (around 0.25 dB)
  High rate: Proposal 3 and proposal 2 are marginally better (around 0.4 dB)

## Slide 24: AWGN performance of different waveforms (SNR in 20 MHz bandwidth)
Performance with different waveforms
  Low rate: Very similar performance with all proposals
  High rate: Proposal 2 and proposal 3 are better than proposal 1 (by 1 dB and 0.8 dB)