## Slide 1: View on EHT Objectives and Technologies
Date: 2018-07-08
Authors:
Name | Affiliations | Address | Email
Jinsoo Choi | LG Electronics | LG Seocho R&D Campus, Korea | js.choi@lge.com
Kiseon Ryu | LG Electronics |  | kiseon.ryu@lge.com
Jeongki Kim | LG Electronics |  | jeongki.kim@lge.com
Jinmin Kim | LG Electronics |  | jinmin1230@lge.com
HanGyu Cho | LG Electronics |  | hg.cho@lge.com

## Slide 2: Abstract
This presentation :
provides our view on EHT objectives and technologies with investigation of current features under the objective in [1] and additional features required from customer perspective

## Slide 3: Background
In previous Warsaw meeting, EHT (Extreme high throughput) TIG was formed with the objective to increase peak throughput
  Candidate features include but are not limited to: 320MHz bandwidth, multiband aggregation and operation, and 16 spatial streams to support high throughput applications such as video-over-WLAN, AR and VR
Those candidate features mainly focus on enhancing BSS/AP peak throughput, not much for improvement from STA because such wide bandwidth and high spatial streams are not easy to support at STA
Considering the Wi-Fi client devices have been significantly extended to many areas for years (smartphone/pad, home appliance, home agent/robot, AR/VR device, etc.), we think the post 11ax (EHT) should also take into account enhancement from STA aspect

## Slide 4: View on EHT current candidate features by Peak Throughput
High level consideration on the current EHT candidate features
  320MHz
    Various band composition is possible to support 320MHz bandwidth, e.g. 320MHz, 160MHz+160MHz, 80MHz+80MHz+80MHz+80MHz, etc.
    We can re-use 11ax OFDM numerology (80MHz/160MHz tone plan) or may define a new one if needed
  16 Spatial Stream (SS)
    Required LTF symbols and feedback overhead for 16 SS may not be trivial amount considering 11ax OFDM numerology, so we may need to consider a compact design
  Multi-band aggregation/operation (MBAO)
    New preamble punctured patterns that improves 11ax may be designed
    Channel access using multiple primary channels may be considered
Our view
  Those features are much focusing on BSS/AP peak increase by straightforward HW extension that may not be easy for STA side, so the gain will be mainly driven by MU features
  MU features like MU-MIMO can be helpful (e.g. less contention) but we can not guarantee to always use those features depending on channel condition and device capability

## Slide 5: Required objectives and candidate features for EHT
AR/VR
Customer
Needs
Required Objectives
Raw rate 20Gbps~,
5~10ms [2]
4K/8K Video
6~23Gbps,
10~20ms [2]
Home Agent/
Robotics
Agg. UL throughput [3]
Wi-Fi Service Quality
Guaranteed performance [4]
320MHz
16-Spatial Stream
Multi-band Aggregation/
Operation
Scheduled Channel Access for 6GHz
Flexible DL and UL
HARQ
Candidate Features
(BSS) Peak &
Average
Throughput
① Peak
Antenna/BW/MCS
extension
Control/Flexibility/
Tx opportunity extension
② Average
4096-QAM1)
1) Adopted in cable network (DOCSIS 3.1)
Spatial Reuse
①
①
②
②
New Services
Pain Point
By practical backhaul limitation, average metric should be considered as well
Discussed in this presentation

## Slide 6: EHT additional candidate features : Flexible DL and UL (1/2)
Motivation:
  Legacy method which consists of different BSSs over multi-bands has a limitation that STA is only scheduled in an associated band
  Multi-band operation [6] can solve the problem but it still has potential issues
Issue 1: Padding is always required
to align PPDU length between multi-bands
Issue 2: When there is ongoing UL in Band1,
DL in Band2 is not possible
DL
DL to STA1
UL
DL
DL to STA 2
UL
ACK
ACK
Padding
Band1
Band2
AP↔STA1
AP↔STA2
UL from STA1
ACK
Cannot be used for DL
DL
UL
DL
UL
Band1
Band2
AP↔STA1
AP↔STA2

## Slide 7: EHT additional candidate features : Flexible DL and UL (2/2)
Candidate approach:
  Flexible DL and UL that enables simultaneous DL/UL Tx over multi-bands can solve issues and increase BSS average throughput
    Unnecessary padding isn’t required
    Additional DL/UL transmission is possible, if any
DL to STA1
DL to STA 2
ACK
ACK
UL from STA1
ACK
DL
UL
DL
UL
Band1
Band2
AP↔STA1
AP↔STA2&3
DL to STA 3
ACK
The usage may be extended to a single STA case (multi-band capable STA)

## Slide 8: EHT additional candidate features : Scheduled Channel Access for 6GHz (1/2)
Motivation:
  In dense environment, EDCA access degrades the Wi-Fi performance by more contention and collision
  11ax developed trigger-based transmission for increasing MU efficiency and controlling DL/UL resources efficiently
    In [5], with large number of STAs UL OFDMA only scenario gains about more than 4 times (depending on scenario) throughput than pure EDCA
  But, in 2.4GHz/5GHz, there exist legacy STAs and 11ax STAs which disable UL MU, which access the channel based on the EDCA
2.4GHz/5GHz
Contention by AP, STAs
UL frame
(STA 1)
BA
TF
UL frame (STA2)
M-
BA
UL frame (STA3)

## Slide 9: EHT additional candidate features : Scheduled Channel Access for 6GHz (2/2)
Candidate approach:
  In 6GHz (or dedicated CH), AP can restrict the EDCA access of the STAs and leverage the controlled access for enhancing BSS average throughput
    E.g. Disallow EDCA access in the band
    E.g. Allow only EHT STA in the band
    E.g. Steer UL MU disabled STAs to other band (e.g., 2.4/5GHz)
6GHz (or dedicated CH)
Contention only by AP
TF
UL frame (STA1)
M-
BA
UL frame (STA2)
UL frame (STA3)
TF
UL frame (STA4)
M-
BA
UL frame (STA5)

## Slide 10: EHT additional candidate features : HARQ [2][7] (1/2)
Motivation
  In a single AP (that usually targets a small/middle home, e.g. ~10 x 10m), STAs in BSS edge or in bad channel condition degrade the BSS average throughput due to using lower data rate
    The service quality of Wi-Fi is not always guaranteed
  In Wi-Fi, there has been insufficiency of good link adaptation tool so that it would be good to have more reliable and beneficial solution for future Wi-Fi
Low MCS
High MCS
Single AP scenario [4]
Kitchen
Children’s Room
Guest Room
UHD Video
VR/AR
Terminal
Agents
Remote Office
VR/AR
UHD
Remote AP
Main AP
Wireless Backhaul
Multi-AP scenario [3]
  Note that multi-APs [3] (that may target a large home, e.g. 16.7 x 16.7m, home network use case) can extend the coverage but it may have high cost and delay issue by multi-hops (degraded rate)

## Slide 11: EHT additional candidate features : HARQ (2/2)
Candidate approach:
  An aggressive MCS & PHY combining by HARQ can reduce the TX airtime, which potentially increases the BSS average throughput
    HARQ ACK (PHY-level) may require shorter Tx time than ARQ ACK
    SIFS based immediate response in Wi-Fi may be suitable for adopting HARQ scheme (e.g. better handling buffer management)
ARQ
A-MPDU
(N MPDUs)
BA
A-MPDU – ReTx
(Nx0.1 MPDUs)
BA
A-MPDU – ReTx
(Nx0.01 MPDUs)
HARQ
HARQ PPDU
(N HARQ bursts)
BAR
Air time
Air time
HARQ PPDU
-ReTx (N x 0.5 HARQ bursts)
HARQ ACK/NACKs
A/N
BA
A/N
A/N
Exemplary HARQ procedure
BA

## Slide 12: Conclusion
We present our view on EHT objectives and candidate features
We think the meaning of the objective with current candidate features is closer to BSS(/AP) peak throughput driven by MU rather than single link STA peak throughput
In addition, considering practical limitation, we provide additional objective/candidate features for improving BSS average throughput (or efficiency)
We suggest clearly defining the goal and objective of EHT based on required features/technologies discussion in the group

## Slide 13: Reference
[1] 11-18-0789-10-0wng-extreme-throughput-802-11
[2] 11-18-0846-01-0wng-next-generation-phy-mac-in-sub-7ghz
[3] 11-18-0903-01-0wng-next-generation-home-use-case
[4] 11-17-0784-00-0wng-wi-fi-enhancement-for-full-coverage-at-smart-home-part-i-coverage-investigation
[5] 11-15-1095-10-00ax-ofdma-performance-in-11ax
[6] 11-18-857-00-Beyond 802.11ax - Throughput Enhancement Utilizing Multi-bands across 2.4 5 6GHz Bands
[7] 11-13-0852-00-0hew-potential-approach-to-improve-wlan-bss-edge-performance