## Slide 1: Clarification of WUR frame related to group addressed frame
Date: 2018-07-04
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Abstract
This contribution is to clarify the operation of receiving a Wake up frame for indicating group addressed frame.

## Slide 3: Introduction (1/2)
In [1], TXID is used to indicate the group addressed frame TX in the Wake up frame. But, TXID is already used in Wake-up frame for indicating the broadcast wake-up for BSS parameter update with Counter field
If TXID is used for both cases, when WUR STA receives a Wake-up frame with increased Counter, the STA cannot know whether or not the group addressed frame is really present in PCR
So, in this case the STA should wake up at DTIM TX time for checking whether or not the group addressed frame is really sent.
It will increase unnecessary power consumption of the STA when DTIM indicates no group addressed BU
AP
STA
Wake-Up
Frame
Counter++
AP
STA
Duty Cycle Period
ON Duration
PCR delay
TIM Beacon
PCR awake state
WUR awake state
WUR doze state
PCR doze state
DTIM Beacon
…
GA BU
Unnecessary wake-up and power consumption
PCR
WUR

## Slide 4: Introduction (2/2)
WUR STA may receive broadcast wake-up frame several times
  AP may send broadcast wake-up frame(B-WUF)s several times for reliable TX
  In duty cycle mode, the location of On-Duration of a STA may be different from those of the other STAs. In this case, always-on mode STAs will unnecessarily wake up several times whenever receiving multiple broadcast wake-up frames as below figure
AP WUR
PCR
B-WUF
Counter=2
WUR
ON Duration
TIM Beacon
PCR awake state
AP PCR
PCR
WUR
ON Duration
Stored Counter=1
Stored Counter=1
…
PCR
WUR
Always-ON
Stored Counter=1
Unnecessary wake-up and power consumption
DTIM Beacon
B-WUF
Counter=2
TIM Beacon
DTIM Beacon
G
G
G
No Group addressed BU
STA1
STA2
STA3

## Slide 5: Proposal
The power consumption for operations in PCR is much larger than that for operations in WUR [2]
Because the WUR is mainly targeted to power sensitive devices such as sensors [3], WUR should carefully be designed with minimizing the unnecessary wake-ups of the devices
Proposal: The information of indicating group addressed frame TX in PCR needs to be distinguished from the information for indicating BSS parameter update
  Option 1: adding a bit in MAC header of Wake-up frame (e.g., TD Control field or Misc. field)
    The bit set to 1 indicates that there is group address frame TX in PCR
  Option 2: using new ID which is different from TXID (e.g., TXID +1)
    E.g.,) while TXID is used for no group addressed frame, TXID + 1 is used for indicating group addressed frame

## Slide 6: Reference
[1] 18/0834r2, Clarifications on WUR-PCR interactions
[2] 15/1307r1, “Low-power wake-up receiver for 802.11”
[3] 17/0029r10, WUR Usage Model Document

## Slide 7: Straw Poll
Which option do you prefer as a method for indicating a group addressed frame TX in PCR?
  Option 1: Adding a bit in MAC header
  Option 2: using new ID which is different from TXID
  Abstains
  Result: Option 1: 13, Option 2: 2

## Slide 8: Spec texts
  TGba Editor: Add the following texts and figure after the second paragraph of subclause 9.10.3.2 (WUR Wake-up frame format) :
  If the Length Present subfield of broadcast WUR Wake-up frame is set to 0, the Misc field contains the Group Addressed BU subfield and Reserved subfield as defined in 9-747x (Misc field of broadcast WUR Wake-up frame).
  The Group Addressed BU subfield is set to 1 when an AP has buffered group addressed BU(s).
 | B0 | B1 B2
 | Group Addressed BU | Reserved
Bits: | 1 | 2
Figure 9-747x- Misc field format of broadcast WUR Wake-up frame

## Slide 9: Spec texts
  TGba Editor: Modify the following texts of 31.7.1 as following:
  31.7.1 General
  (…existing texts…)
  The AP may transmit a broadcast WUR wake-up frame with Group Addressed BU subfield set to 1 to a non-AP STA to indicate that group addressed buffered BU(s) are available for all the STAs via the PCR.
  (…existing texts…)

## Slide 10: Straw Poll 2
Do you agree to add the spec texts (in slide 8 and 9) in doc 18/1172r2 into the next TGba Draft?
Y:, N:, A:

## Slide 11: Motion
Move to adopt the spec texts (in slide 8 and 9) in doc 18/1172r2 into the next TGba Draft